## Slide 1
Chapter 06 – Using Networks
AS Applied ICT – 9626 - Theory
2017-20
Year 12

## Slide 2: 1 – Key Concepts
As a teacher, you will refer to these concepts again and again to help unify the subject and make sense of IT. If mastered, learners can use the concepts to solve problems or to understand unfamiliar subject-related material.
Impact of Information Technology Information Technology (IT) is the application of technology to process information. The impact of IT on all aspects of everyday life is immense. The enormity of the impact can be seen in industry and commerce, transport, leisure, medicine and the home. The impact on the work force is a very important factor to consider and communications using new technologies have made the World seem smaller.
Hardware and software Many hardware components and software applications are used in IT systems. It is important to understand how these work, and how they interact with each other and within our environment.
Network Computer systems can be connected together to form networks allowing them to share resources.

## Slide 3: 1 – Key Concepts
The internet The internet is a global communications network that allows computers worldwide to connect and share information in many different forms. Examples include email, web pages, and audio and video files. The impact of the internet on our lives is profound. While it provides huge benefits to society, security of data is an issue, both in the work place and for personal data.
System life cycle
Information systems are developed within a planned continuous cycle that covers the initial development of the system through to its scheduled updating or redevelopment. Each phase of development is organised into separate stages.
New technologies As the information industry changes so rapidly, it is important to keep track of new and emerging technologies and consider how they might affect everyday life.
Guided learning hours
Guided learning hours give an indication of the amount of contact time teachers need to have with learners to deliver a particular course. Our syllabuses are designed around 180 guided learning hours for Cambridge International AS Level, and around 360 guided learning hours for Cambridge International A Level.
These figures are for guidance only. The number of hours needed to gain the qualification may vary depending on local practice and the learners’ previous experience of the subject.

## Slide 4: 2 – Assessment Structure
For Cambridge International AS and A Level Information Technology, candidates:
take Papers 1 and 2 only (for the Cambridge International AS Level qualification)
or
follow a staged assessment route by taking Papers 1 and 2 (for Cambridge International AS Level qualification) in one series, then Papers 3 and 4 (for Cambridge International A Level qualification) in a later series
or
take Papers 1, 2, 3 and 4 in the same examination series, leading to the full Cambridge International A Level.
All components are externally assessed.

## Slide 5: 2 – Assessment Structure
Component | Weighting | 
 | AS Level | A Level
Paper 1 Theory 1 hour 45 minutes This written paper tests sections 1–10 of the syllabus content. Candidates answer each question in the spaces provided on the question paper. All questions are compulsory. 90 marks | 50% | 25%
Paper 2 Practical 2 hours 30 minutes This paper tests sections 8–10 of the syllabus content. Candidates will also need to use their previous knowledge from sections 1–7. All tasks are compulsory. Candidates must use the most appropriate software and the most appropriate methods. 110 marks | 50% | 25%

## Slide 6: 2 – Assessment Structure
Component | Weighting | 
 | AS Level | A Level
Paper 3 Advanced Theory 1 hour 45 minutes This written paper tests sections 11–19 of the syllabus content. The content of sections 1–10 is assumed knowledge. Candidates answer each question in the spaces provided on the question paper. All questions are compulsory. 90 marks | - | 25%
Paper 4 Advanced Practical 2 hours 30 minutes This paper tests sections 16–19 of the syllabus content, and sections 8–9 of the syllabus content within a problem-solving context. Candidates will also need to use their previous knowledge from all sections of the syllabus. All tasks are compulsory. Candidates must use the most appropriate software and the most appropriate methods. 110 marks | - | 25%

## Slide 7: 2 – Grade Descriptors – Grade A
To achieve a Grade A, a candidate will be able to:
recall and communicate precise knowledge and display comprehensive understanding of scientific phenomena, facts, laws, definitions, concepts and theories
apply scientific concepts and theories to present reasoned explanations of familiar and unfamiliar phenomena, to solve complex problems involving several stages, and to make reasoned predictions and hypotheses
communicate and present complex scientific ideas, observations and data clearly and logically, independently using scientific terminology and conventions consistently and correctly
independently select, process and synthesise information presented in a variety of ways, and use it to draw valid conclusions and discuss the scientific, technological, social, economic and environmental implications
devise strategies to solve problems in complex situations which may involve many variables or complex manipulation of data or ideas through multiple steps
analyse data to identify any patterns or trends, taking account of limitations in the quality of the data and justifying the conclusions reached select, describe, justify and evaluate techniques for a large range of scientific operations and laboratory procedures.

## Slide 8: 3 – Assessment Objectives
Cambridge International AS and A Level Information Technology has three assessment objectives:
AO1 Recall, select and communicate knowledge and understanding of IT
AO2 Apply knowledge, understanding and skills to produce IT-based solutions
AO3 Analyse, evaluate, make reasoned judgements and present conclusions
2.3 Relationship between assessment objectives and components
The approximate weightings allocated to each of the assessment objectives are summarised below.
The table shows the assessment objectives (AO) as a percentage of each component.
Component | AO1 % | AO2 % | AO3 %
Question Paper 1 Theory | 50 | 32 | 18
Question Paper 2 Practical | 5 | 90 | 5
Question Paper 3 Advanced Theory | 32 | 40 | 28
Question Paper 4 Advanced Practical | 10 | 85 | 5

## Slide 9: 06 – Using Networks - Syllabus Content
Candidates should be able to:
6.1 Network types
discuss the advantages and disadvantages of networking computers
compare the characteristics of a local area network (LAN) with a wide area network (WAN)
describe client-server and peer-to-peer networks
describe the characteristics and purpose of virtual private networks (VPN)
discuss the advantages and disadvantages of different network types (including: client-server, peer-to-peer, VPN)
describe the characteristics and purpose of intranets and extranets
describe the characteristics and purposes of the internet
define the term the internet
describe how the internet is used for communication (including: IM, VOIP and news services)
discuss the benefits and drawbacks of using the internet
define the term World Wide Web
discuss the difference between the internet and the World Wide Web
discuss the advantages and disadvantages of mobile networks
6.2 Video and web conferencing
describe how to set up a video conference
describe how to set up a web conference
describe the use of networks in video and web conferencing (including: Integrated Services Digital Network (ISDN), LAN, WAN, VPN, 802.11 a/b/g/n (wireless), Asynchronous Digital Subscriber Lines (ADSL), Synchronous Digital Subscriber Lines (SDSL), 3G/4G mobile networks)
discuss the impact of video conferencing on society (including: the general public, legislation, education, medicine, business, media)
describe how data is transmitted and converted in a video conference (including: use of codecs)
Page 78

## Slide 10: 06 – Using Networks - Syllabus Content
Key Terms
Data: raw numbers, letters, symbols, sounds or images without meaning
Discussion Point
When answering a question
!
Example
A company creates websites using style sheets.
Identify one
Questions
Which of the
Task
K
Remember
The motherboard is a

In a computer,
?
Tip

## Slide 11: 06 – Using Networks - Learning Objectives
By the end of this chapter, you will be able to:
understand the advantages and disadvantages of networking computers
be able to describe the characteristics and purpose of diff erent types of networks, such as LAN, WAN, VPN, client-server, peer-to-peer, intranets, extranets and the internet
be able to define the terms internet and World Wide Web and discuss the diff erence between the two
be able to discuss the benefits and drawbacks of using the internet
understand how the internet is used for communication
be able to discuss the advantages and disadvantages of mobile networks
understand how to set up a video and a web conference and describe how they use networks
be able to describe how data is transmitted in a video conference
understand the impact of video conferencing on our lives
Page 79

## Slide 12: 6.1 – Networking Computers
A single computer is known as a stand-alone computer, up until the 1990s, computers in homes and organisations were largely stand-alone devices. Today, many computers are connected together.
The first instance of computers being linked together was in 1969 with the Advanced Research Projects Agency Network (ARPANET). Universities connected computers together with the intention of being able to communicate and share resources. This network was the predecessor to the internet.
Networking computers has a number of advantages and disadvantages.
The advantages of networking computers will mostly outweigh the disadvantages. This is why we choose to network computers together.
Key Terms
Network: a set of computers and devices connected together so they can communicate and share resources Network architecture: the design of a network
K
When we connect stand-alone computers together we create a network.
?
Tip
Remember
The way a network is designed is called its architecture.
A network’s architecture can be described by its geographical and physical nature, and by how data is stored and accessed on it.

Page 79

## Slide 13: 6.1 – Networking Computers
We can describe a network by its geographical and physical architecture. This creates two categories of network:
local area network (LAN)
wide area network (WAN).
Key Terms
Local area network (LAN): a network that covers a small geographical area
Wide area network (WAN): a network that covers a large geographical area
K
Page 79

## Slide 14: 6.1 – Networking Computers
Page 79
Advantages | Disadvantages
An internet connection can be shared, allowing each user an the network to access the internet. | A high amount of network traffic may cause a network to run slowly and cause frustrating delays.
Users can access their data from different computers on the network. | A whole network could fail if one element of the network fails. This will depend on how the network is structured.
File servers can be used to store data in a central location. This makes it easier to keep the data secure and to create a back-up copy. | Viruses could easily spread from one networked computer to another, if a network is not sufficiently protected.
Application servers can be used to store software in a central location. This can often reduce software costs as a site licence could be purchased, if available. A software site licence is generally cheaper than individual licences. This also means that software updates would only need to be run on the server. | Setting up a larger network can be expensive, especially if the network requires cabling, several servers, switches and wireless access points. The staffing costs to maintain a network can also be expensive.
Printers can be shared. This means that a number of users can share resources in a company or home, rather than requiring their own. | Networks can have security risks. Many users’ data may be accessed if an unauthorised user gains access to a networked file server.
Communications can be sent from one computer to another. | 
Users can share their data with other users on the network. | 
Table 6.01 - Advantages and disadvantages of a network.

## Slide 15: 6.1 – Networking Computers
A LAN is a network that is restricted to a small geographical area. LANs are usually found in homes, schools, universities and small businesses.
A WAN is a network that covers a larger geographical area A WAN may be contained within a country or can spread across several countries. Organisations such as banks, police forces and hospitals use WANs to share data. The internet is a global WAN. Several LANs can be connected together to form a WAN. A business that has several different branches often operate their networks this way.
The use of a LAN and a WAN can be compared using several different factors.
Page 80
Figure 6.01 - A basic structure for a LAN

## Slide 16: 6.1 – Networking Computers
Page 80
Figure 6.02 - A basic structure for a WAN.
The terms LAN and WAN describe the geographical architecture of a network and how it is physically structured. They do not describe how data is stored and accessed. The two architectures for storing and accessing data on a network are:
  Client-server
  Peer-to-peer
Client-Server and Peer-to-Peer
A client-server network uses a dedicated computer to store data, manage resources and control user access. This computer is known as a server.
The server acts as a central point on the network that other computers connect to. A computer that connects to the server to access the data and resources it manages is known as a client.

## Slide 17: 6.1 – Networking Computers – Client and Peer
Page 81
Factors | Local Area Network | Wide Area Network
Data transfer rates | Can have up to 1 Gb per second. | Often restricted to less than 200 Mb per second.
Data transmission errors | Fewer errors as data packets are sent over short distances. | Greater chance of error as packets are sent over longer distances.
Connection method | Restricted to within a small location. Copper wire, fibre optic cable or radio waves are mostly used. | Expanded to a wider location. Copper wire, fibre optic cable or microwaves are mostly used. They can often use public telephone network systems, leased lines, transmission towers and satellite communication.
Security | Comparatively high as security can be easier to implement over a smaller number of devices and connections. | Comparatively low as security is difficult to implement across a higher number of devices and connections.
Ownership | Mostly owned by individuals or individual organisations. | Elements of the network often use communication infrastructures owned by others.
Table 6.02 - Comparison of a LAN and a WAN.

## Slide 18: 6.1 – Networking Computers – Client Server
Page 81
Figure 6.03 - Example of a client-server network.
Network servers handle a variety of functions, including:
storing a database of usernames and passwords to control user access
data storage and data security
assigning levels of access that determine what resources a user may access
monitoring network traffic
hosting of shared applications
managing an internet connection
scheduling and running back-ups services
Email services
Printing jobs on network printers
domain name services.
A client-server network will usually have at least one server and several clients. A network may have more than one server, each one dedicated to handling a specific function. E.g., one server may handle user access, while another may handle data storage. This often occurs in larger networks where a server has to service many clients at the same time. Spreading the load across several servers helps to keep the network running efficiently.

## Slide 19: 6.1 – Networking Computers – Peer-To-Peer
Page 81
A peer-to-peer network has no central server to manage the network. Each computer on the network shares its data and resources with all the others. No computer has control over another. Each computer is known as a peer.
On a peer-to-peer network, users store data on their own computer, but may allow other users access to it. Alternatively, they may choose to keep their data private. Individual peers may provide resources that others do not.
For example, a peer may have a printer attached to it and other peers may print to that printer.
Figure 6.04 - Example of a peer-to-peer network.

## Slide 20: 6.1 – Networking Computers – Peer-To-Peer
Page 82
Table 6.03 shows a comparison of the architecture of a client-server and a peer-to-peer network.
Client-server network | Peer-to-peer network
A dedicated computer controls the network. | No individual computer controls the network.
Centralised database of users, usernames and passwords. | No centralised database.
Centralised data storage. | Data is stored on individual computers.
Suited to large networks with many computers. | Relies on users remembering to back-up individual computers.
Centralised back-ups. | Suited to small networks with few computers.
Each type of architecture has its advantages and disadvantages. Peer-to-peer networks are often cheaper to install and maintain than client-server networks. Client-server networks can be expensive to purchase and often require trained staff to maintain them.

## Slide 21: 6.1 – Networking Computers – Peer-To-Peer
Page 82
Table 6.04 - Advantages and disadvantages of a client- server network.
Advantages of a client- server network | Disadvantages of a client- server network
Centralised database of users, usernames and passwords provides login security. | Expensive to set up and maintain.
Users do not have to make backups as backups are centralised and handled by the network manager. | Failure of a central server may make the whole network fail.
Users do not have to worry about security as a network manager maintains the network. | Requires specialist technical staff to maintain.
User data is kept private. | 
Levels of access can be applied to resources. | 
On larger networks several servers can be used for different functions to maintain network efficiency. | 

## Slide 22: 6.1 – Networking Computers – Peer-To-Peer
Page 82
Each type of network is used in many different ways, for example:
Banks use client-server architecture to provide online banking services. When a device (such as a personal computer (PC), tablet or smartphone) connects to the bank through the internet, the device becomes a client. The bank’s servers handle the client and provide access to online banking facilities.
Companies use servers to host websites. Client computers access the web pages they contain.
On-demand tv and film providers have servers that stream content to client devices.
Many peer-to-peer networks exist over the internet that allow users to share music, images and videos. Each peer has some content, allowing other users access to it.
Advantages of a peer-to- peer network | Disadvantages of a peer-to-peer network
Cheap to set up and maintain. Does not require expensive servers. | Users have to worry about making backups as no centralised backup service exists.
Failure of an individual peer only removes access to the resources and data which that peer handles. The rest the network remains unaffected. | No centralised database of users, usernames and passwords, making it harder to maintain security.
Does not require specialist technical staff to maintain. | The more computers there are on a peer-to- peer network, the slower it will run.
Table 6.05 - Advantages and disadvantages of a peer-to- peer network.

## Slide 23: 6.1 – Networking Computers – Virtual Private Network
Page 83
Virtual Private Network (VPN)
Companies or organisations may want to allow users : access a network, often a LAN, from a remote location. They will need to use external resources to create this connection.
The external resources will -be owned or maintained by the owner of the LAN, which can make access to the LAN network much less secure. This can be of great concern to the owner of the LAN and the users who want to remotely access it.
The issue of security can be overcome by implementing a virtual private network (VPN).
Once connected to the VPN, the remote computer then has secure access to the LAN’s resources, just as if it were directly connected to the LAN.
Key Terms
Tunnelling protocol: a tunnel between two points on a network that is governed by a set of rules
Encryption: scrambling data so it cannot be understood without a decryption key, to make it unreadable if intercepted
K
Remember
A VPN is a method of allowing a remote computer to connect securely to a private network using external resources.


## Slide 24: 6.1 – Networking Computers – Virtual Private Network
Page 83
Virtual Private Network (VPN)
Security is implemented through the use of tunnelling protocols and encryption. For example, the secure shell (SSH) tunnel protocol uses encryption to securely transmit unencrypted data packets across an unsafe network.
To connect to a VPN, a user remotely logs on to the network. Once the user’s identity has been authenticated, the VPN’s tunnelling protocol sets up an encrypted link to the user’s computer. Data can then be transmitted securely.
There are several advantages and disadvantages for an organisation using VPNs as shown in Table 6.06.
Remember
VPNs are often used by organisations to provide LAN access to travelling employees, employees who telework and users that want to access LAN resources at home.
Users who want to securely access data on a home computer when they are away can also use a VPN.

Find out what kind of network you have in your school or home. What is the structure of it and how does it store data? Does your school or home network have any servers? If it does, what are they used for?
Task

## Slide 25: 6.1 – Networking Computers – Intranet and Extranet
Page 83
Intranets and Extranets
An intranet is a privately owned network that uses internet technologies, for example web pages, for internal use within an organisation. Web pages hold organisations’ information such as news, events, historical data and commonly used documents.
Email and instant messaging can also be used for internal communication. Training videos or corporate messages can be streamed and watched by employees.
Table 6.06 - Advantages and disadvantages of a VPN.
Advantages of a VPN | VPN Disadvantages
VPNs maintain a high level of security for data transmission over the internet. | A certain amount of technical expertise is required to set up and maintain VPNs. The cost of this expertise must be factored in when deciding whether to implement a VPN.
VPNs use external resources. Organisations that use VPNs can save money as they do not need to purchase or implement secure, dedicated connections, called leased lines, for users who want to access the network. | 
The cost of maintaining the external resources is covered by someone else. | Performance of the VPN may be outside the control of the organisation. It is dependent on the external resources that are used.
Adding extra clients costs very little as the network is virtual. | 

## Slide 26: 6.1 – Networking Computers – Intranet and Extranet
Page 84
Intranets and Extranets
Intranets usually use client-server architecture. They often use several servers. A web server hosts the intranet's web pages, while an email server handles email communication. Another server will handle user accounts and access.
Many organisations now use an intranet. For example, schools use a virtual learning environment (VLE) to provide teaching and learning resources to students. The VLE is an intranet.
Additionally, unlike when browsing the internet, only information relevant to the organisation is available. An intranet is for internal use only. This increases security and confidentiality as only users within the organisation can access information on the intranet.
Remember
Intranets are used to increase efficiency because all information is stored centrally and can be easily accessed.

Intranet vs. Extranet

## Slide 27: 6.1 – Networking Computers – Intranet and Extranet
Page 84
Intranets and Extranets
There may be times when an organisation will want to allow users that are currently external to the organisation to access information on its intranet. It can do this by using an extranet. An extranet is an intranet that has been opened up to allow external user access. Extranets use VPNs to allow an external user to securely access the information on them.
Extranets usually only allow certain information to be accessed. For example:
A school’s VLE may allow parents to access their child’s marks, attendance data and reports.
A doctor’s surgery may be able to access a local hospital’s extranet to make appointments for patients.
A company may provide tracking information on deliveries it is making to customers.
Access to an extranet is normally available through the organisation’s website. A user logs in using an email address and password that will notify the extranet that the user is an authorised external user.
Remember
Intranets are used to increase efficiency because all information is stored centrally and can be easily accessed.

Intranet vs. Extranet

## Slide 28: 6.2 – The Internet
Page 84
The Internet
The beginnings of the internet were quite different from how it is now. In the 1950s and 1960s, the United States government formed several organisations whose purpose was to develop new technology.
One organisation was the Advanced Research Projects Agency (ARPA). As projects developed, employees at ARPA became frustrated at the lack of computing power available to them. At the time, only a handful of powerful computers were available across the country. These were often at locations far away from the researchers who needed them.
The invention packet switching allowed the creation of computer networks. Taking advantage of this communication breakthrough, ARPA created ARPANET, a network of computers that could share data and computing power.
Remember
The internet is a global network made up of interconnected networks and individual computers.
This global network allows users to access online facilities such as electronic communication, information sharing, data storage, banking, video and music streaming and social networking.

Packet Switching

## Slide 29: 6.2 – The Internet
Page 85
The Internet
The 1970s saw the introduction of the protocol, TCP/IP. This allowed separate networks to connect to each other, forming the basis for the internet. The term ‘internet’ originates from ‘inter-network’, meaning a network that was formed from the joining of networks.
The 1990’s saw a huge increase in the size of the internet and its purpose, as many commercial, educational and home users took advantage of the facilities available online.
Today, the number of users and devices on the internet runs into billions. It has become like a backbone, the purpose of which is to allow communication and shading of data on a global scale.
What is TCP/IP

## Slide 30: 6.2 – The Internet
Page 85
Characteristics of the Internet
Any device connected to the internet forms part of the Internet. To connect to the internet we need to use internet service provider (ISP). ISPs use public phone systems, underwater cables, microwave transmissions via satellites and radio waves to provide connections.
Data and information is held and distributed by content providers. A content provider is an organisation, group or company that offers content on web pages, for example text, images, sound and video, or web-based services, for example streaming media, gaming, shopping and electronic communication.
Although many of the computers connected to the internet can act as a server, most act as clients. The majority of data is held on web servers that are accessed by individual computers.
Internet in Maps

## Slide 31: 6.2 – The Internet
Page 85
Characteristics of the Internet
The widespread nature of the internet means that it has no centralised control. No one company or organisation runs or has authority over the internet, although various independent organisations control aspects of it:
The Internet Corporation for Assigned Names and Numbers (ICANN) regulates domain names and their suffixes, such as .com, .co.uk, .in, .sa, .ae and .cn.
The Internet Engineering Task Force (IEFT) devises and administers internet standards, such as protocols that govern communication.
The World Wide Web Consortium (W3C) attempts to enforce agreement from organisations to adopt new standards.
Telecommunications companies own the infrastructure that the internet uses for communication.
Remember
The lack of authority means that the information the internet carries is of mixed value. Information can be useful and correct, it can also be inaccurate, out of date or completely incorrect.
Some information is deliberately designed to mislead.


## Slide 32: 6.2 – The Internet
Page 85
Characteristics of the Internet
The internet is constantly changing and evolving. E.g.:
Every day, newly bought devices connect to it.
The internet is expanding geographically as remote regions are connected through the installation of cables or through satellite communication.
The data it holds constantly changes as organisations add, edit and delete data from their websites, and social networking users add and remove data.
Newer technologies allow the range of facilities to expand. For example, the introduction of broadband connections has encouraged the growth of internet- based, on-demand television services.
The huge scale and size of the internet means that using it has many benefits and drawbacks for organisations, businesses and individuals.
Discussion Point
What would your life be like if you did not have the internet? What would be different? Would it be better or worse
!

## Slide 33: 6.2 – The Internet
Page 86
Benefits of using the internet | Drawbacks of using the internet
Information. A vast range of information is available on virtually any topic. | Incorrect information. Anyone can publish information on the internet. This means that some of the information available is inaccurate, out of date, incomplete or simply incorrect.
Global audience. The internet is worldwide, therefore contributors have a global audience. | Unsavoury behaviour. One serious problem with the internet is that it allows people to interact anonymously with other people. Users are unsure with whom they are really communicating. This means that people can make up fake identities in order to cyberbully, intimidate, steal and commit abuse.
Immediate transmission of information. Users can send messages immediately across the world. Postings on news sites and social media can be seen immediately by an audience. | Hacking. Some users may use the internet to attempt to gain access to other users’ computers. This is often in an attempt to steal personal data or to crash websites. Protection against hacking can be expensive to an organisation.

## Slide 34: 6.2 – The Internet
Page 86
Benefits of using the internet | Drawbacks of using the internet
Immediate availability of services. Users can quickly access services such as to bank online, book medical appointments, pay bills and book tickets for transport and for leisure. | Viruses. An organisation or individual will need to protect their computer against viruses. A virus is malicious software installed on a computer without consent or knowledge. Removal of a virus can be a difficult job.
International ecommerce. Users have access to online shops 24 hours a day and products from all over the world. Companies can also market products to consumers nationally and internationally. | Identity theft through phishing and pharming. Phishing uses fake emails pretending to be from an organisation. Phishing emails deceive users into giving their personal data by tricking them into following a link to a fake website. The website asks them to enter personal details. Once gathered, this data is used for criminal activities. Pharming works in a similar way. When users attempt to visit a known website, they are instead directed to a fake website that looks just like the real one. The cost of identity theft to individuals and businesses can be enormous.

## Slide 35: 6.2 – The Internet
Page 86
Benefits of using the internet | Drawbacks of using the internet
Entertainment. Products such as software, music, films and books can be purchased and immediately downloaded. Users can play online games, or join in multiplayer games over the internet. | Unsuitable material. The free nature of the internet means that unsuitable content is present, such as pornography, graphic violence, promotion of terrorism, torture and physical and written abuse. Social networking allows anyone to publicly abuse friends, colleagues, celebrity figures and people in the news, often with little consequence to the offender.
Free education. Many free online tutorials and educational resources are available to help people learn new skills or knowledge. | Spamming. The ease of communication means that anyone can generate and transmit unwanted emails to millions of users. It is estimated that 69% of emails sent in 2014 were spam.
Social networking. The internet allows families, friends, organisations and businesses to regularly communicate, share and engage in social activities. | Online addiction. Some people have difficulty separating virtual environments from reality. Others find virtual worlds, such as those in massively multiplayer online role-playing games (MMORPGs) more alluring and comforting than the real world. They feel safer and happier in these environments than they do in real life. This can lead to social isolation and insecurity.

## Slide 36: 6.2 – The Internet
Page 87
Benefits of using the internet
Up-to-date news. News stories on the internet can be read as soon as they are published.
Reduction in costs to businesses and organisations. Marketing over the internet, especially through social media, can be extremely cheap compared with traditional advertising and promotional methods.
Feedback. The internet has allowed companies and organisations to easily gain feedback on products and devices through rating systems, comments, online surveys and ‘likes’ on social media.
Big data. The nature of the internet allows vast : mounts of data to be collected by organisations. User behaviour on websites can be monitored, such as the choice of products a person buys, or what information searches they make. Social networking sites collect : eta on what news items are trending, and what users like and dislike. Apps on smartphones collect data about online habits and behaviour. All of this : collected data can be analysed by researchers or sold to businesses for marketing purposes.
New. communication applications. The internet allows communication applications that previously were not possible. E.g., home security cameras can be monitored while the householder is away from home. Central heating can be remotely switched on or off - using a smartphone app.

## Slide 37: 6.3 – The World Wide Web
Page 87
The World Wide Web
The term ‘internet’ describes the physical, global network of computers. The internet does not actually contain any information. It is a physical infrastructure.
The World Wide Web is an information system comprising of documents, images, videos and sounds. It uses the internet as its base. Users access this information through websites and web pages, which are accessed through the web browser.
The concept of the World Wide Web was developed by Tim Berners-Lee in 1989 when he worked for CERN. Berners-Lee proposed a system for a more efficient communication system for CERN that allowed documents on an information system to be accessed via hyperlinks.

## Slide 38: 6.3 – The World Wide Web
Page 87
The World Wide Web
Berners-Lee proposed a system for a more efficient communication system for CERN that allowed documents on an information system to be accessed via hyperlinks. He realised that any document could be accessed by a hyperlink, whether it is a text document, an image or a sound clip.
In 1990 Berners-Lee and Robert Cailliau published a proposal to build a World Wide Web of hypertext- linked documents that could be viewed by a browser. Documents would be stored on servers, with users’ computers acting as clients. From this proposal the World Wide Web was born and in 1991 it became available to the public.
Today the World Wide Web is the basis for, among other things, national and international information sharing, banking, shopping, on-demand television broadcasting and social networking. It has billions of users, including businesses, organisations, governments, schools, colleges, universities and domestic users.
Key Terms
Hyperlink: a link that can be clicked to locate to another place in a document, or a different document entirely
Web browser: a software application for retrieving and ; resenting information on the World Wide Web
K

## Slide 39: 6.4 – Communicating Using the Internet
Page 87
Communicating Using the Internet
The internet is for communication. It allows users to communicate in several ways, including:
instant messaging (IM)
voice over IP (VOIP)
news services.
Instant messaging (IM) is a form of communication that allows real-time text transmission over a network, often the internet. Depending on the type of IM service, messages are either transmitted once a message is composed and sent by the user, or transmitted character by character as the user types. Some services allow files to be transferred and conversations to be saved.
IM is now a feature of many social networking sites, allowing users to chat online instead of posting messages on their profile page. Many organisations see IM as a valuable tool for customer interaction, for example support helplines. This can be especially useful where a support technician needs to give instructions to a customer. The customer can read (and reread) and follow the instructions in their own time.
Users of IM often see it as an equivalent or alternative to text messaging used on smartphones. They make use of text speak (where common words and expressions are abbreviated), for example LOL (laughing out loud), and emoticons to reduce typing and speed up replies.
An example of an IM service is the private messaging system available on Facebook. Users can send messages to each other privately as well as posting on each other’s profile.
Figure 6.06 - Many social networking services now offer an instant messaging feature

## Slide 40: 6.4 – Communicating Using the Internet
Page 87
Communicating Using the Internet
Voice over IP (VOIP) technologies allow users to have voice communications, just as if they were using a telephone system. Instead of using an analogue telephone transmission, the user’s voice is recorded by the computer and transmitted digitally to the recipient. The VOIP system can work internally across a network, or externally by making use of the internet to carry the data transmission.
VOIP has advantages over traditional analogue telephone systems. When the system is run by using an organisation’s LAN, calls within the organisation will be free. Extra VOIP phones can be added to a network, simply by connecting a new phone to a network point or by adding it to a wireless network. However, if a network is experiencing heavy traffic, voices can become garbled, distorted or missing altogether.
An example of a VOIP service is Skype. Users can make calls using the Skype application on the internet.

## Slide 41: 6.4 – Communicating Using the Internet
Page 87
Communicating Using the Internet
News services are organisations that collect and broadcast news stories for subscribers. Users can sign up for news alerts using a smartphone application. Some services allow news stories to be filtered out so that only news that covers topics a user is interested in is sent to their smartphone. Others broadcast headline news to subscribers.
An example of a news service is Google News. Users can subscribe and receive news stories on a daily basis, often in the categories of their choice.
All of these services are available because of packet switching technology.
Figure 6.07 - Users can subscribe to news services to receive news stories in the category of their choice.

## Slide 42: 6.5 – Mobile Networks
Page 89
Mobile Networks
Mobile networks are broken down into small areas called cells. At the heart of each cell is a radio base station mat transmits and receives messages. The base stations connect to public telecommunications services allowing access to the internet.
Tells vary in size:
picocells cover an area of less than 200 metres
microcells cover an area up to 2 kilometres
macrocells cover larger regions.
There have been several generations of mobile networks, each providing faster access speeds and 'eater reliability:
1G networks. These were the first generation mobile networks that used analogue signals. These networks were largely limited to voice and text message communications.
Key Terms
Cell: The geographic area covered by a radio transmitter
K
Remember
A mobile network is a wireless WAN that uses radio to transmit and receive communications from portable devices, such as smartphones.
Mobile networks now cover a considerable amount of the inhabited areas of world.


## Slide 43: 6.5 – Mobile Networks
Page 89
Mobile Netwroks
2G networks. The second generation mobile networks switched from analogue to digital transmission, improving signal quality. 2G networks were able to connect with each other, allowing a phone to use other networks.
3G networks. Third generation networks increased data transmission speeds up to 2 Mbps, allowing internet access, video transmission and online gaming.
4G networks. Fourth generation networks are the current, latest generation of mobile network technology. In theory, they allow data transmission speeds of up to 1Gbps, allowing greater use of video streaming facilities.
Mobile networks have grown hugely in popularity, with -any users now accessing the internet through 3G or 4G connections. The rapid growth in use of social media networks has led to many people checking profiles and sending posts frequently during the day, often via a mobile network.
Find out what further developments are in progress for mobile networks.
Task

## Slide 44: 6.5 – Mobile Networks
Page 89
Mobile networks have their advantages and disadvantages.
Advantages of mobile networks | Disadvantages of mobile networks
Mobile networks have enabled users to communicate with others and access the internet while on the move, often through the use of smartphones. | Quality of reception can vary and can be poor towards the edge of a cell, leading to interrupted or delayed transmissions
Breaking the network down into cells allows for lower power radio transmitters to be used, bringing energy and cost savings. | 
There are only so many radio frequencies that can be used for mobile communications. These frequencies can be split among neighbouring cells, and reused in more distant cells, thereby increasing the number of communications that can take place at the same time. | 
Larger geographical areas can be covered than by using a single transmitter. Even high power transmitters are limited in range. By using several, low power transmitters a wider area can be covered. | The use of frequency must be carefully planned to avoid interference between cells.
The use of multiple transmitters means the network is more robust. Failure of one base station only affects one cell, leaving other areas of the network unaffected. | 
Table 6.08 - Advantages and disadvantages of mobile networks.

## Slide 45: 6.6 – Video and Web Conferencing
Page 90
Video and web conferencing
One form of communication that is slowly gaining in popularity is video conferencing. Video conferencing allows users to see and hear each other as they talk. Web conferencing is a similar communication medium.
However, whereas video conferencing allows two-way communication, web conferencing traditionally allowed one-way communication.
A user would broadcast a video to many watching users, for example a company delivering a training session or a university lecturer presenting a lecture. However, web conferencing technology has expanded to allow two-way communication.
Figure 6.08 - People can use mobile devices, such as tablets, for video conferencing calls.

## Slide 46: 6.6 – Video and Web Conferencing
Page 90
How to set up a video conference
Video conferencing requires certain hardware and software:
a desktop computer or laptop
a webcam to record the user’s image
a microphone to record the user’s voice
a monitor to display the other participant’s image
speakers to produce the other participant’s voice
network (and internet) access to connect to the other participant
video conferencing software to conduct and control the video conference.
Many modern devices such as laptops, smartphones and tablets already have this hardware. Smartphones and tablets are often supplied with video conferencing software installed.
Before a user can participate in a video conference, they must first register with a video conferencing service. The service will have software that the user needs to install. With the software running and the device connected to a network or the internet, the user selects another registered user and initiates a conference call. The other participant can accept or reject the call.

## Slide 47: 6.6 – Video and Web Conferencing
Page 90
How to set up a video conference
There are a number of checks that need to be made before a video conference goes ahead:
All participants will need to make sure they have a stable and suitable internet connection.
Each participant will need to make sure that their microphone is inputting their voice, and that it is doing this at a suitable sound level. Most video conferencing software has a built in facility that allows a user to record their voice input and play it back to assess if it is correct.
Each participant will need to make sure that they have correctly positioned their webcam, and that it is safely and securely placed. They will need to test that their image is being inputted into the system and that other participants can see them clearly. Most video conferencing software also has a facility to test this.

## Slide 48: 6.6 – Video and Web Conferencing
Page 90
How to set up a web conference
Setting up a web conference is a similar process to a video conference. Web conference software is available, but quite often the same software that is used for video conferencing can also be used to set up a web conference.
Before initiating the web conference, the user sends an invitation to interested participants, stating the time and date of the conference. The invitation often contains an access code that allows the interested participant to logon to the conference, along with a link that specifies the network address at which the conference can be accessed. Using access codes helps keep unwanted users from participating.
At the appointed time and date, users follow the link and log on using the access code. They can now watch and participate in the conference. Participants

## Slide 49: 6.6 – Video and Web Conferencing
Page 91
How to set up a web conference
Participants may watch a demonstration of a product or read a document onscreen, but will not require a web camera themselves to do this. Web conferences can also be just text based, where participants will use a messaging facility to communicate.
There are a number of checks that need to be performed before a web conference goes ahead:
Similar checks to a video conference will need to be performed for the internet connection, microphone and a web camera if used.
In some web conferences, participants may want to share documents. Most web conferencing software will allow participants to do this. This will either be through documents being preloaded into an online meeting room, or by a link sent in a messaging facility during the web conference.
A test may need to be carried out on whether the preloaded documents can be accessed, or that the text facility can be used.

## Slide 50: 6.6 – Video and Web Conferencing
Page 91
Using networks in video and web conferencing
The wide-scale use of video conferencing and web conferencing would not be possible without the use of networks. The use of packet switching enables video and sound transmissions to be broken down into packets, just like any other type of data, to be transmitted. The resulting packets can be easily and swiftly transmitted across networks and the internet.
Video and web conferences held internally within organisations will make use of that organisation’s LAN.
The LAN may be wired or wireless. To connect externally, the conferences will also need to make use of a WAN or me internet.
Video and web conferencing requires a reasonable data transmission speed. The higher the required quality of video and sound, the higher the transmission speed that is required. As a result, for video or web conference over a LAN, one of four types of connection is usually used:
Integrated Services Digital Network (ISDN)
Asynchronous Digital Subscriber Lines (ADSL)
Synchronous Digital Subscriber Lines (SDSL)
3G/4G mobile networks.

## Slide 51: 6.6 – Video and Web Conferencing
Page 91
Using networks in video and web conferencing
Integrated Services Digital Network (ISDN) is a networking technology that allows data to be transmitted digitally over analogue copper wire, usually with transmission speeds of up to 64 Kbps per channel. Two channels could also be used in parallel to send data at up to 128 Kbps. ISDN was popular in the 1990s and early 2000s but has largely been replaced by much faster ADSL and SDSL networks. However, ISDN is still used in areas where ADSL and SDSL technology has yet to be implemented.
Asynchronous Digital Subscriber Line (ADSL) technology, also known as broadband, is now the most common type of connection to the internet. It has typical transmission speeds of around 100 Mbs. ADSL is used in homes and businesses to deliver reliable, high-speed connections. Asynchronous means that download and upload speeds are different. This means that ADSL works by unevenly splitting the balance between download and upload speeds. Most homes and businesses will download more data from the internet than they upload to it. As a result, ADSL download speeds are usually far greater than upload speeds.
Synchronous Digital Subscriber Line (SDSL) technology uses the same data transmission technology as ADSL. However, this time the download and upload transmission rates are balanced and equal. SDSL is used by organisations that upload and download equivalent amounts of data.
Mobile devices such as smartphones make use of 3G/4G technology to allow users to use video conferencing when travelling, or when access to a LAN is not possible.

## Slide 52: 6.6 – Video and Web Conferencing
Page 91
Using networks in video and web conferencing
For a video conference to successfully take place, the video and audio signals must be transmitted over a network. Video signals require high volumes of data transmission. The higher the resolution of the video, the more data that needs transmission, and the greater the traffic that is placed on a network. High traffic can lead to disruption or interruption of the video conference.
To overcome this problem, video conferencing uses software called codecs. Codec is an abbreviation of the words ‘coder’ and ‘decoder’. At the sender’s end, the ‘coder’ element of the codec takes the video and audio signals and compresses them to reduce their file size. Reducing the file size means less data needs to be transmitted, reducing network traffic and the possibility of disruption to the conference. At the receiver’s end, the ‘decoder’ decompresses the video and audio signals so that they can be played.
The same codec must be used at both the source and the destination of the data transmission. Different codecs compress and decompress in different ways, therefore are incompatible with each other. As a result, several codec standards exist. The H.264 codec is one of the most common and is used not only for video conferencing, but also with DVDs and YouTube videos. Other codecs for video conferencing include H.261 and H.263+.
Blue jeans
Real Life Call

## Slide 53: 6.6 – Video and Web Conferencing
Page 92
The Impact of Video Conferencing
Additionally, many computing devices now feature inbuilt video conferencing equipment. Smartphone, laptops and tablets generally have microphones, speakers and cameras, along with the network connectivity needed for video conferencing. Free software allows cheap video conferencing.
As a result, an increasing number of users have now taken to using video conferencing as a method of communication and are enjoying the benefits it brings. Those users who live at a distance from friends and relatives have especially taken to this technology as it allows them to see, as well as hear, their loved ones. Users with hearing and speaking impairments enjoy video conferencing as it enables them to communicate using sign language.
Key Terms
Digital divide: the separation between those that have access to technologies and the internet and those that do not.
Teleworking: working from home using technologies to keep in contact with an employer.
K
Remember
Improvements in internet and communication technologies have led to affordable high-speed connections at home and at work.
These high-speed connections can usually handle video transmissions. The introduction of 4G mobile networks mean that mobile devices are also capable of high-speed connections.


## Slide 54: 6.6 – Video and Web Conferencing
Page 92
The Impact of Video Conferencing
A growing example of a video conferencing software that people use is Apple’s FaceTime. Users that have an iPhone can use the inbuilt FaceTime software application to communicate with each other using video conferencing
However, the general public has yet to fully embrace this technology. Many users feel self-conscious and uncomfortable in front of a camera. Even though connection speeds have improved greatly, videoconferencing does require high-speed data transmission. High levels of network traffic can more frequently interfere with, degrade or interrupt video transmissions. This leads users to return to more reliable voice-only methods.
It could be argued that video conferencing is helping to widen the digital divide. Many older users are wary of technology. They are afraid of the complexity of video conferencing, opting for more traditional voice communication methods that are familiar and comfortable.
Figure 6.09 - Video conferencing is used in some courts to allow witnesses to testify without being in the courtroom.

## Slide 55: 6.6 – Video and Web Conferencing
Page 92
The Impact of Video Conferencing
Video conferencing has not yet directly had an impact on law. However, legislation has been implemented in several countries that allows a witness to give testimony via video conferencing. This process is reserved for witnesses who may be psychologically upset by having to attend court, especially those that may have to face someone who has subjected them to physical assault or abuse.
In some countries, such as the United States, video conferencing allows defendants to make initial court appearances without having to leave jail. This saves travel expense and increases safety to the public as suspects remain in custody.
In the UK, several police forces have implemented video conferencing as a way of conducting interviews more quickly. An interviewer may be based at one police station, but can interview suspects and witnesses at other stations, without having to travel to each site.
Figure 6.09 - Video conferencing is used in some courts to allow witnesses to testify without being in the courtroom.

## Slide 56: 6.6 – Video and Web Conferencing
Page 93
The Impact of Video Conferencing
Video conferencing has had an impact on education and the way that students learn. Rather than listening to a teacher, or reading a book or web page, video conferencing is used to engage students. Video conferencing allows students to participate in conversations and share ideas with fellow students at schools and universities in other parts of the world. This can lead to unexplored perspectives about subjects being shared and argued in live debates, resulting in wider, more considered points of view, especially when the students are from differing cultures.
Speaking to industry and subject experts often engages and interests students in a topic. Video conferencing allows experts to give talks and lectures without having to travel to a school. Sometimes a talk can be given to more than one school at a time, allowing many students to benefit from the experience. This is especially useful to schools in remote, isolated areas where travel would be difficult or expensive.
Or Click Here

## Slide 57: 6.6 – Video and Web Conferencing
Page 93
The Impact of Video Conferencing
Universities make heavy use of video conferencing. The Technology allows lecturers to teach courses at several universities, while being based at one. Sharing of such expertise is becoming more common, especially in subjects where finding a lecturer for a course has been difficult. Additionally, video conferencing allows lecturers so hold a lecture for students while away on research or at conferences.
Medicine and medical care are areas where video conferencing continues to be of growing usefulness. Consultants and physicians in different hospitals are able so discuss a patient’s case and help to offer a diagnosis. External hardware components such as ultrasound imaging devices and video endoscopes can be connected and images from them shared in the video conference, heling consultants at other locations to help assess a patient’s condition. This has the dual benefit of reducing travelling costs for consultants and increasing efficiency as consultants can see more cases in any given time period.
Figure 6.10 - Dental students using video conferencing software to see and interact with a live appointment.

## Slide 58: 6.6 – Video and Web Conferencing
Page 93
The Impact of Video Conferencing
In some countries medical practices have introduced video conferencing to help doctors and nurses keep in touch with patients who have physical impairments, and for those in remote areas where travelling may be difficult or dangerous. In such situations video conferencing can bring comfort to a patient, especially the elderly, who might not otherwise have much human contact.
Sometimes the best way to do business is in a face-to-face meeting. Email and telephone provide useful media for arranging and making business deals, but when it comes to agreements of great value, people tend to prefer to do business in person. Meeting someone in person helps to promote goodwill, friendship and trust.
However, face-to-face meetings are not always possible. For example, time constraints or cost of travel may make them impossible. Video conferencing has provided a possible solution to these situations. It allows people to have face-to-face meetings without having to leave the office. This saves travel expenses and it also allows for more efficient use of an employee’s time, as hours are spent working and not travelling.
Figure 6.10 - Dental students using video conferencing software to see and interact with a live appointment.

## Slide 59: 6.6 – Video and Web Conferencing
Page 93
The Impact of Video Conferencing
Video conferencing has also helped to facilitate the growth in teleworking. Employee who work regularly from home can sometimes feel cut off from their employer. Teleworkers that use video conferencing tend to feel happier and less isolated from their employer and co-workers. Companies that have regional offices are finding that video conferencing brings unexpected benefits. Many companies that regularly use video conferencing to communicate with their regional offices find that employees in those offices feel more involved with the organisation, increasing employee satisfaction and productivity.
Companies are also using video conferencing for staff training. Some companies have several offices, and some, like banks, have many branches. A trainer at a company’s head office can deliver a training program via a video conference to staff at different offices or branches simultaneously.
However, video conferencing can also cause anxiety and stress among some workers. Some people are less confident in front of a camera. As a result, a video conference made by an employee with senior personnel can cause more stress than a face-to-face meeting.

## Slide 60: 6.6 – Video and Web Conferencing
Page 93
The Impact of Video Conferencing
One area in which video conferencing has seen a large-scale uptake is in the media sector. Video conferencing allows journalists to deliver live, on-the-spot reports in situations where a live broadcast might not otherwise be possible.
Another aspect to consider is press video conferencing. With businesses and organisations taking advantage of the global audience the internet permits, it is becoming increasingly common to hold international press conferences. These conferences are often held to launch new products or to make statements about political affairs. Press video conferencing allows journalists to participate without actually having to attend.
Discussion Point
Can you think of any other ways that video conferencing could be used in our lives?
!

## Slide 61: 6.7 – Summary
Page 94
Stand-alone computers that are connected together create what is called a network. There are different types of networks that can be categorised by their geographical and physical structure or their method for data storage.
A LAN is a network that is geographically small in area. They are usually found in homes, schools and small businesses.
A WAN is a network that is geographically large in area. The largest and most common WAN is the internet. The internet is the network infrastructure, whereas the World Wide Web is the web pages of content we can view using the internet, an ISP and a web browser.
The internet is used for communication in various different ways. These include IM, VOIP, news services, video conferencing and web conferencing.
Video conferencing has had an impact on many areas of society, such as personal communications, court cases, business, education, medicine and media. These impacts have been both positive and negative.
A client-server network has servers that run the network centrally. Each computer that is part of the network is called a client. A peer-to-peer network does not have servers. No single computer has control over another in this network.
A VPN is a method of allowing a remote computer to connect securely to a private network using external resources.

## Slide 62: 6 – Review Questions
Page 94
Describe the difference between a LAN and a WAN. [4]
Explain what is meant by an intranet and how it could be used in an organisation. [4]
Explain the advantages and disadvantages of a VPN. [4]
Describe the difference between the internet and the World Wide Web. [2]
Identify four pieces of hardware that could be used when video conferencing. [4]
Discuss the impact of video conferencing on education. [6]
Questions
?

## Slide 63: 6 – Review Questions
Page 94
Any four of the following points [4]:
LAN covers a small geographical area ...
... WAN covers a large geographical area.
LAN normally uses infrastructure owned by the individual or organisation ...
... WAN can often use infrastructure owned by a third party.
LAN will normally have a faster data transfer rate, up to 16Gb ...
...WAN normally has a lower rate of data transfer, up to 200Mb.
Answers

## Slide 64: 6 – Review Questions
Page 94
Any four of the following points [4]:
It is a privately owned network that uses internet technologies.
It is used internally within an organisation.
It often accessed using a webpage.
It can provide services such as news updates, file sharing and instant messaging.
It can provide access to training materials for employees.
Answers

## Slide 65: 6 – Review Questions
Page 94
Choose four of the following points (at least one advantage and one disadvantage) [4]:
Uses an additional level of security when transmitting data...
... this means that the user can feel their personal data is safer when being transmitted.
They use the infrastructure that is already in place...
... this means that there is little additional cost to setting up a VPN.
... this can mean that the performance of the infrastructure is outside the control of the individual or organisation.
They require a higher level of expertise to set up
... if this expertise is not present it may need to be purchased.
Answers

## Slide 66: 6 – Review Questions
Page 94
Answer must include both of the following [2]:
The internet is the physical infrastructure of the largest WAN.
The WWW is a collection of webpages that contain text, images, videos and sounds.
Any combination of four from the following [4]:
Desktop computer/laptop/mobile device
Webcam
Microphone
Monitor
Speakers
Network infrastructure.
Answers

## Slide 67: 6 – Review Questions
Page 94
Level of response: Level 3 [5-6 marks] Candidates will discuss in detail a range of points about the impact of video conferencing on education. The points raised will be justified. There will be a reasoned conclusion. The information will be relevant, clear, organised and presented in a structured and coherent format.
Level 2 [3-4 marks]
Candidates will provide limited discussion of points about the impact of video conferencing on education. The development of some of the points will be limited. There will be a conclusion. For the most part the information will be relevant and presented in a structured and coherent format.
Level 1 [1-2 marks]
Candidates may only give reference to a single aspect of video conferencing and its use in education. Answers may be simplistic with little or no relevance.
0 marks for a response with no valid comments. Possible points:
Learners can participate in conversation with other learners world wide.
learners can speak to and listen to industry experts without the need for travel.
Learners can benefit from watching international lectures to experience a range of teaching methods.
Experts can instruct those in training in important educational training, such as medical procedures.
Answers