## Slide 1: Unit 03
Unit 03 – Computer Systems
M/601/7261
LO1 - Understand the components of computer systems

## Slide 2: P1.1 – Uses of Spreadsheets - Scenario
The purpose of this unit is to prepare the learners to undertake part of the role of IT technician. They will investigate a range of hardware components including looking at the technical specifications and how the components work together in a computer system. They will explore at least two types of operating systems and software utility programmes. With the knowledge gained from investigating the components and software the learners will be required to recommend a range of systems to meet different user needs.
The learners will be expected to have the opportunity to practice the installing hardware and software components, configuring the systems to meet the user’s needs and to test the systems. This unit aims to give learners an understanding of the different components in a computer system and the skills to be able to recommend, set up and maintain computer systems for business use.

## Slide 3: LO1 - Assessment Criteria
Learning Outcome (LO) The learner will: |  | Pass The assessment criteria are the pass requirements for this unit. The learner can: |  | Merit For merit the evidence must show that, in addition to the pass criteria, the learner is able to: | Distinction For distinction the evidence must show that, in addition to the pass and merit criteria, the learner is able to:
1 | Understand the components of computer systems | P1 | Explain the function of computer hardware components | M1 Compare the different backing storages available | 
 |  | P2 | Explain the purpose of operating systems |  | 
 |  | P3 | Explain the purpose of different software utilities |  | D1 Explain how the performance of computer systems can be improved with the use of software utilities
2 | Be able to recommend computer systems for a business purpose | P4 | Recommend a computer system for a given business purpose | M2 Justify how final recommendations meet a given business purpose | 
3 | Be able to set up and maintain computer systems | P5 | Set up a standalone computer system, installing hardware and software components |  | 
 |  | P6 | Configure a computer system to meet user needs |  | D2 Recommend computer system improvements based on feedback from users
 |  | P7 | Test a configured computer system for functionality | M3 Analyse the test results identifying any discrepancies | 
 |  | P8 | Undertake routine maintenance tasks on a standalone computer system |  | 

## Slide 4: LO1 - Assessment Criteria P1, P2 and M1
Assessment Criteria P1
Learners need to show understanding of the components of a computer system. This could be evidenced in the form of a detailed user guide explaining the functions of computer components. The evidence could include the learner providing photos, video recordings (separately), images or diagrams with clear descriptive notes of the functions for each component.
Assessment Criteria P2
Learners must give a basic outline of the functions of operating systems in general and explain their purpose in managing the computer components. This could be evidenced with a report which compares different types of operating systems and the purpose of their different features.
Assessment Criteria M1
The learner must show that they have compared the features and functions of different backing storages in addition to the strengths and weaknesses. The learners must look at different types of storage and consider how much storage is available, transfer rates, suitability for different systems, security issues, costs. This could be evidenced in a report format.

## Slide 5: LO1 - Assessment Criteria P3 and D1
Assessment Criteria P3
Learners should consider a range of different software utilities and their findings could be presented in a table; they must include at least two examples from each category of software utility:
security,
clean up tools,
drives formatting
and must also include a rationale explaining why the software is fit for an identified purpose.
Assessment Criteria D1
Learners must produce evidence that they have considered the benefits of software utilities and identified how these utilities will improve the performance of computer systems. This can be an extension of P3 where learners have explained why the software would be used for a purpose. This could be presented in the form of a report or a table with explanatory notes and each improvement will need to be detailed and clearly linked to a business purpose.

## Slide 6: LO1 - Understand the Components of Computer Systems - Scenario
To introduce the unit the tutor should provide brief presentations on the different areas in learning outcome 1. The areas would be internal system components, peripherals, backing storage, operating systems and software utilities. The learners should then explore, investigate and analyse these areas including any of the new technologies. This could be done as groups taking one topic each and reporting back giving examples or purpose, options and usage identifying these to the group. Learners should experience other operating systems besides Microsoft Windows, this may be through alternative technologies such as mobile devices or research but they should be able to compare and understand the differences. These activities could lead to the creation of a manual, leaflet or guide on the various devices and software, to be presented to the wider group.

## Slide 7: P1.1 – Understanding Computer Components
Over the last 30 years in IT little has changed other than speed and size. This has been considerable, even the basic Home Computer now at 2.4ghz is 80 times the speed of the Pentium P33 machines in 1990. Memory back then was 32mb ram, 128mb if you could afford it and it was costly, roughly £1 per MB. Now the low end computer has 2gb, that is 60 times less than now and now 1GB ram costs £14 or less. But it is the same technology, some concept, same structure as it has always been.
Some cabling has gone to be replaced with faster versions, Serial and Parallel with Firewire, Sata and USB, Motherboards are not even smaller and the physical size of hard drives has changed little other than SSD. You could have done this project 20 years ago and the methods would be the same but it is still necessary to know these things.
Monitors have gotten thinner and larger, the connector cables can now output at a higher definition and Graphics Cards can drive them harder. External devices are similar, a scanner has improved in speed, cost, integrated into printers, can now do 3D but the concept and technology is still the same. Keyboards have some more keys, mice have no balls any more but are still the same principle.
Input devices, Floppy has become CD, DVD, Blue Ray, USB stick, progression and progress, nothing that has been an invention. Similarly for networking, we have new programs, faster cables, Fibre optics but the principles of IP addressing, cabling and Routers, Switches and Servers and Hubs are still the same as 30 years ago.
P1.1 – Task 01 – Introduce the principles, concepts and purpose of Computer Systems.

## Slide 8: Look at the specification of the motherboard below, look at the individual specifics, from what you have read about graphics, sound and video, what can you see is incorporated onto this motherboard.
Form Factor: Micro ATX CPU Socket: AM2+ QPI Speed: N/A FSB/HT Speed: 2000 MHz Chipset: AMD 740G Memory Type: DDR2 Memory Type (ECC): Non-ECC Memory Type (R/U): Unbuffered Memory Speed (Mhz): DDR2 - 667 DDR2 - 800 Memory Capacity: 8GB On Board Graphics: Graphics Interface: PCI-E (x16) SLI: Hybrid SLI: Hybrid Crossfire: Crossfire: Water Cooled: Intel i7 Compatible: HDCP: Expansion Slots: 2 x PCI (32 bit) 1 x PCI-E x1 1 x PCI-E x16 SATA: SATA 3Gb/s RAID: SATA RAID SCSI: MODT: Back Panel: 1 x 10/100/1000 (LAN) 1 x 7.1 Audio I/O 1 x D-Sub 1 x DVI-D 1 x Line In 1 x Line Out 1 x Mic In 1 x Parallel (LPT) 1 x PS/2 Keyboard 1 x SPDIF Out (Coaxial) 4 x USB 2.0/1.1 Internal I/O: 1 x 24pin (V) 2 x 3pin Fan (V) 1 x 4pin (V) 1 x CD-In 1 x Chassis Intrusion connector 1 x Floppy 1 x FP Audio Header 1 x IDE 2 x Memory Slots (DDR2) 6 x SATA 3Gb/s 1 x Serial (COM) Header 1 x SPDIF-In/Out Header 4 x USB2.0/1.1 Header
P1.2 – Understanding Computer Components - Internal

## Slide 9: P1.2 – Understanding Computer Components - Internal
Every component inside a computer is there for a reason, upgrade any of these and the computer will be better, take them out and the machine will not work.
Motherboard: The motherboard is the computer’s main electronic circuit board to which all the other components of your computer are connected. More than any other component, the motherboard is the computer. All other components attach to the motherboard, the CPU, the supporting circuitry called the chipset, memory, expansion slots, a standard IDE hard drive controller, and I/O ports for devices such as keyboards, mice, and printers. Some motherboards also include additional built-in features such as a graphic adapter, SCSI disk controller, or a network interface. Apples and Laptops obviously have different motherboards than PC’s and tablets have different forms again.
Processor: The processor, or CPU, is the brain of the computer. Although the processor isn’t the only component that affects overall system performance, it is the one that most people think of first when deciding what type of computer to purchase. Intel has four processor models, Two of them — the Pentium 4 and Celeron — should be used only for desktop or notebook computers.
More powerful computers should have an Itanium 2 or a Xeon processor, or a comparable processor from one of Intel’s competitors, such as AMD. Each motherboard is designed to support a particular type of processor. CPUs come in two basic mounting styles: slot or socket. However, you can choose from several types of slots and sockets, so you have to make sure that the motherboard supports the specific slot or socket style used by the CPU. Some more powerful motherboards can have two or more slots or sockets to hold two or more CPUs.
Apples and Laptops obviously have different CPU’s than PC’s and tablets have different forms again. It all started with a 8088 processor running at 100mhz and with every computer generation (4 years) stepped up a grade, 286, 386, 486, P1, P2, P3, P4. With each generation a new generation of games and applications to work with. Core Duo works well with Vista, P2 and P3 with Windows Xp, P1 with Windows 95. Look at the specifications again of World of Warcraft, could these have run on a Pentium 2 machine at 1.6ghz.

## Slide 10: P1.2 – Understanding Computer Components - Internal
BIOS – Built in operating system is a small battery linked to the core of the motherboard that tells a computer what it is, what CPU, what hard drives, what kind of motherboard, where the connectors are, what time of day it is. All computers have one but they seem the least of things.
The two most common types are Phoenix and Ami, they contain a battery life of at least 3 years and contain several pages of important information, specifically hard drive configurations and IRQ allocation. Operating systems can override the BIOS but this takes extra time and can lead to IRQ conflicts.
Hard drive configuration and controllers (e.g. SATA, IDE, master, slave) – All motherboards contain at least 2 controllers for hard drives. Modern machines have the capacity for more than 2 with SATA and SSD. More than one hard drive can be on one cable from the controller port but these will need to be configured as Master and Slave drives. Older hard drives had this capacity on the Hard drive, a set of pins with a jumper to manage master and slave but SATA drives take this information from BIOS.
The difference between SATA (new) and IDE (older) is speed, hard drives are measures in RPM and Buffer Memory, an 8100RPM drive with 8mb buffer means it is very fast, can take 8mb chunks of information at a time while searching for more information to drop to the CPU. Other speeds include 5300 and 7200. For most computer functions, putting the OS on the master and programs on the slave frees the master for speed efficiency.
SSD – Solid State Drive – this has no moving parts and therefor is faster than normal Hard drives.

## Slide 11: P1.2 – Understanding Computer Components - Internal
There are two sizes of hard drive for a PC, 2.5” for a laptop and 3.5” for a full machine. This has been the de facto standard since PC’s first came out. The original PC hard drive on home computers were a massive 20mb. But with operating systems starting at MS Dos 3, all you needed was 2mb for operating system storage. Word processors were 4mb, spreadsheets another 1mb leaving a massive 13mb for games and file storage. Doom, the most popular PC game ever, installed onto 5mb and could only run off the hard drive. So you played Doom or you played something else. These all used an IDE standard, the same connectors on the PC for linking up the Hard Drive to the motherboard.
With the development of Windows 3.1, Hard Drives grew to 80mb leaving more room for PC developments like Graphic Cards to play better games. The first Windows games were invented to take advantage of the operating system already in place and this signalled the first steps towards the death of Dos based games.
Speed differentiation came into play, hard drive speeds of 5300 rpm, increased to 7200 rpm, and hard drives grew in size exponentially. 80mb became 120, then 200, 320, 500 and then a massive 10gb by 2000. Now the standard hard drive with a new PC is 250gb but 1.5 terabyte ones are available for home use at affordable prices. The faster the hard drive, the quicker the loading speed. For games this meant installing huge numbers of games on one machine at a time.
The new standard is SATA which is faster than IDE and easier to install allowing the use the daisy chain multiple drives onto a PC.

## Slide 12: P1.2 – Understanding Computer Components - Internal
Ports e.g. USB, parallel, Firewire – These have been among the few things in hardware that has changed and the main change has been the method of information transfer. Parallel and Serial were first and stayed the de-facto standard for 25 years.
  USB was the first and only true direct replacement making it the standard. All machines come with them, tablets have them, mobiles connect through them, and there are currently 3 standards, defined by speed rather than compatibility, USB 1-3. Basically they transfer information from one thing to another, allow devices to connect from printers to fondue sets.
  Parallel was the standard for Printers and Scanners for a generation, a larger socket device that meant only one or two per machine. Information was slower but reliable.
  Firewire – When USB is just not good enough, a high speed transfer connector, mostly used for Video transfer, still twice as fast as USB3, but not all machines have one. Looks like a larger USB socket, often mistaken for one.
Internal memory (e.g. RAM, ROM, cache) - Memory demands on a PC have grown exponentially over the years and doubles every time a new version of windows is released. Currently 2gb of memory is enough to run Windows Vista smoothly but not enough to play good games well. 3gb is good, 4gb is better.
Ten years ago with Windows 98, 256mb was the standard for a good game on a PC, 512mb for hardcore gamers. But memory is necessary, the more there is, the faster a game will be.
  RAM - There are three standards for RAM and all of them are speed based. DDR, DDR2 and DDR3. They have a clock speed, the faster the clock speed, the faster the processing time. And this improves games, the more processing power that is taken from the CPU, the faster the CPU can deal with the instruction code of the game.
  Rom and Cache – This is the memory that the computer stores in its head for a task. The need and management of this has changed with OS’s. Programs force the CPU, GPU or RAM to store current tasks in Cache while they are thinking about things, this is why games work so well, the next directions the character moves are cached so loading time is massively reduced. The more RAM there is, the more ROM can be Cached for use. Cache memory makes things faster but it is not something that can be bought, it is something that is allocated.

## Slide 13: P1.2 – Understanding Computer Components - Specialised cards - GPU
Similarly, 3D games often rely on a powerful graphics processing unit (GPU), which accelerates the process of drawing complex scenes in real time. GPU’s may be an integrated part of the computer's motherboard, the most common solution in laptops, or come packaged with a discrete graphics card with a supply of dedicated Video RAM, connected to the motherboard through either an AGP or PCI-Express port. It is also possible to use multiple GPUs in a single computer, using technologies such as NVidia's Scalable Link Interface and ATI's CrossFire but all this takes money, time and effort and not all games will take advantage of these, depending on the way a game is programmed.
Game compatibility and development however does not immediately recognise this hardware and games may need downloads and bug fixes from the game sites to take advantage of these technologies. The standard graphics card used as a template has changed over the years and used to be NVidia GeForce. Without this the graphics were worse, lower quality, lower speed. Better cards brought the game up to a level and downloads made the game better. Doom when it was released used a GL download for Pentium machines with a Graphics card to improve the screen quality and for a number of years GL technology was the standard. Now every PC has a unique card which can be specified by the user.
Graphics cards handle all of the visual data within a computer, interpret it and display it via a VDU. Components on a Graphics card include:
  GPU – Graphical Processing Unit is a dedicated microprocessor making calculations in order to display both 2D and 3D graphics.
  Motherboard interface – This is the method of connection and transfer of information between the motherboard. These include PCI, AGP and PCI express.
  Video BIOS - basic program that governs the video card's operations and provides the instructions that allow the computer and software to interface with the card.
  Video memory – if the card is integrated onto the mother board it may use the computers RAM, otherwise it will have a dedicated amount of memory for use for storing other data as well as the screen image such as object co-ordinates.
  Random Access Memory Digital-to-Analogue Converter – This coverts the digital signals produced by the computer processor into an analog signal which can be understood by the computer display
  Output connectors – this is how the graphics card connectors to the VDU. This can include DVI, HDMI and component.
  Cooling device – Video cards may use a lot of electricity, which is converted into heat. If the heat isn't dissipated, the video card could overheat and be damaged. Cooling devices are incorporated to transfer the heat elsewhere. Three common methods are heat sink, fan or water block.

## Slide 14
Intensive image manipulation often rely on a powerful graphics processing unit (GPU), which accelerates the process of drawing complex images in real time. GPU’s may be an integrated part of the computer's motherboard, the most common solution in laptops, or come packaged with a discrete graphics card with a supply of dedicated Video RAM, connected to the motherboard through either an AGP or PCI-Express port. It is also possible to use multiple GPUs in a single computer, using technologies such as NVidia's Scalable Link Interface and ATI's CrossFire but all this takes money, time and effort and not all imaging tools will take advantage of these, depending on the way the operating system is programmed.
Higher end graphics programs like 3D Studio Max, ZBrush and Maya will take fuller advantage of whatever the machine has going for it, especially the graphics cards. To create a 3D version of a file requires processing, especially if the image needs rotating within an environment.
With the new 3D version of Photoshop this is also the case, the image needs to handle an object in a 3D world, calculate the location, the perspective, the shadowing and lighting, to do this through the CPU is slower than to process this through a dedicated image handling system like a graphics card.
P1.2 – Understanding Computer Components - Specialised cards - GPU

## Slide 15: P1.2 – Understanding Computer Components - Specialised cards - Soundcard
Sound cards - These are also available to provide improved audio in computer games. These cards provide improved 3D audio and provide audio enhancement that is generally not available with integrated alternatives, at the cost of marginally lower overall performance. The Creative Labs SoundBlaster line was for many years the de facto standard for sound cards, although its popularity dwindled as PC audio became a commodity on modern motherboards. Newer developments in PC technology meant 8bit to 16 bit sound cards and now 32bit and sixty four bit technology is available. Sound cards used to be separate from the motherboard but are now part of the on board system taking away some of the compatibility issues but the quality will not be as good as a separate card.
Physics processing units - PPUs such as the Nvidia PhysX (formerly AGEIA PhysX) card, are also available to accelerate physics simulations in modern computer games. PPUs allow the computer to process more complex interactions among objects than is achievable using only the CPU, potentially allowing players a much greater degree of control over the world in games designed to use the card.

## Slide 16: P1.2 – Understanding Computer Components - Specialised cards - Network
Network Card - The network connection can be one of the most important additional parts of any computer. Many computers have network adapters built into the motherboard and if not, you’ll need to add a separate network adapter card.
For computers, you can usually get away with using the inexpensive built-in NIC because client computers are used only to connect one user to the network. But they are very cheap and as a result, it makes sense to spend more money on a higher quality NIC for a heavily used computers. Name-brand cards from manufacturers include Intel, SMC, or 3Com.
The network interface cards that you use must have a connector that matches the type of cable that you use. A NIC is a Physical layer and Data Link layer device. Because a NIC establishes a network node, it must have a physical network address, also known as a MAC address. The MAC address is burned into the NIC at the factory, so you can’t change it. Every NIC ever manufactured has a unique MAC address.
WI-Fi - A wireless card is a network that uses radio signals rather than direct cable connections to exchange information. A computer with a wireless network connection is like a mobile phone. Just as you don’t have to be connected to a phone line to use a mobile phone, you don’t have to be connected to a network cable to use a wireless networked computer.
A wireless network is often referred to as a WLAN, for wireless local area network. The term Wi-Fi is often used to describe wireless networks, although it technically refers to just one form of wireless networks: the 802.11b standard. A wireless network has a name, known as a SSID. SSID stands for service set identifier. Each of the computers that belong to a single wireless network must have the same SSID.
Wireless networks can transmit over any of several channels. In order for computers to talk to each other, they must be configured to transmit on the same channel. The simplest type of wireless network consists of two or more computers with wireless network adapters. This type of network is called an ad-hoc mode network.
A more complex type of network is an infrastructure mode network. All this really means is that a group of wireless computers can be connected not only to each other, but also to an existing cabled network via a device called a wireless access point, or WAP (Hotspot).
P1.2 – Task 02 – Create a User Guide that explains the forms, function and varieties of computer hardware components
Motherboards | CPU’s | BIOS | Hard Drives | Ports | Memory | Graphics | Sound | Network

## Slide 17: P1.3 – Understanding Computer Components – Peripheral Devices - Output
There are three kinds of devices that connect to a system that allows extended features other than software to be used, Inputs, outputs and cables. Each of these has different forms and almost every System except Thin Client can use these devices to manage operation.
Monitor - There are 2 ways of outputting work on computers for the user to see in preview, work-in-progress or in finished form. These are called Soft Copy and Hard Copy. Both forms have their uses and both have their different quality standards to consider.
Monitors have developed over thirty years from Monochrome 12” to high definition Flat Screens. But the biggest revolution is not their size, which can be quite impressive, or the technology to have multiple monitors, which is quite useful, but the resolution, the DPI and the controllers to push the display faster to manage the colour depth and resolution.
They say that a monitor is only as good and the graphics card that drives it, the better the card the more depth the monitor can manage. Up to a point, then it just handles the information faster.
The standard resolution for a monitor is 800x600, 800 pixels across by 600 high. Most monitors now have settings to push that higher, but the display will slow down because the quality of the image displayed will be more dense. This is where the graphics card comes in.
Larger monitors like a 24” can manage that better because it will still be the standard resolution just on a wider area. The benefit of these is that it allows for more room, more icons, more open toolbars and more of the image to be seen. Who does not want to have a larger monitor than the one in front of them.
The alternative is multiple screens, this is where graphic cards come into their element, to display on two screens at one time, or three, tools on one, image on another, second image on the third. This takes processing power and should be managed by a separate card rather than putting pressure on a CPU.

## Slide 18: P1.3 – Understanding Computer Components – Peripheral Devices - Output
Monitor – Vga – 16 colours 14” screen
Graphics Card – None
Processor - 286
Memory – 1mb , minimum
Sound – Internal speaker.
Controller – Keyboard or mouse controlled only.
Monitor – Vga – 16 bit colours 14” screen
Graphics Card – None but Open GL or 16mb for optimum effects.
Processor – Pentium 1
Memory – 8mb , minimum, 64mb optimal
Sound – None or 16mb optimal.
Controller – Keyboard, mouse or joypad controlled.
Monitor – Vga – 16 bit colours 14” screen
Graphics Card –
Processor: AMD 64 3200+/Intel Pentium 4 3.0GHz or better
Memory: 8 GB free hard-drive space, 512MB RAM (XP)/1GB RAM (Vista)
Graphics: Shader 3.0 or better, 256MB Nvidia GeForce 6600GT/ATI Radeon 1600XT or better
Monitor – 17” minimum

## Slide 19: P1.3 – Understanding Computer Components – Peripheral Devices - Output
Printers - Hard Copy means output, something that can be held and handled. Sooner or later the client will want an outputted version either for a magazine, billboard or just as an image. The quality of this output will differ depending on the device and the options chosen on the device.
Printers come in four varieties, inkjet, laser, 3D and dye-subliminal and for each of these are their merits and drawbacks. We will discount 3D as this is for modelling.
Ink – This works by having ink from a cartridge shot onto a page in the patterns requested, they come in four colours, CMYK. When an Inkjet printer prints something in between the colours, a blend, it prints the Yellow first, then Cyan then Magenta, depending on the darkness of the colour. These work by printing one line at a time, going back and printing the second colour and then the third and finally black (K).
The biggest benefit of these is price, the cartridges inside the printer and worth more than the printer itself and a colour on most can be replaced separately from the others. The downside is that inkjet printers cannot print on larger page formats, A2 or A1, and struggle to print onto glossy paper because the ink does not dry quickly enough and will run. There are exceptions to each of these rules of course.
The major disadvantage is speed, Inkjets are slow, even good ones are slow and measured in PPM, laser printers are at least 6 times faster and can do bulk printing. They are also noisy, the ink runs out quickly and the ink fades after a period of time. An example is the pictures in a take away shop window, they fade with black and blue breaking down first to form yellows and greens.

## Slide 20: P1.3 – Understanding Computer Components – Peripheral Devices - Output
Laser printers – In comparison these are faster and the ink does not fade as quickly. Laser printers work by superheating the toner powder and burning this powder onto the paper. The Drum lays down the heat and locks it into the paper threads so the colours dry immediately. This is why the paper is hot when it comes out.
Like Inkjets, laser printers work in DPI, Dots per Inch, the more concentrated settings like 1200dpi, means better quality but the density means time to print, 4 times the colour depth so 4 times the time.
Most laser printers are black and white and colour lasers are more expensive, 4 times the price sometimes. Printing above A4 in Laser costs even more but the quality and sped difference between laser and inkjets in their unique selling point. Because it is toner powder rather than ink and because the toner colours are blended together using heat rather than mixing laid down colours, the density and smoothness of the colour difference is more precise. Pushing this up to 1200 dpi and the image is going to be more photorealistic and the precise. Additional options added to this like Postscript increase the quality and capacity without adding price.
However, anything bigger than A3 and the cost spirals. For larger than A3 companies move into printing houses for their prints, businesses dedicated to this one function, mass producing using lasers and industrial printers for bulk and size output.
Dye-Subliminal – This is a more unique kind of printing that allows the printer to print onto different materials like cloth to form the image by printing onto wax and then heating the wax with the ink onto the material or surface or having the user print it onto a wax page and then ironing the wax page onto the material. Again like the other prints they are limited to size, you will not be able to print onto something larger than A3 without a huge cost outlay.
The DPI resolution of these is similar to inkjet rather than laser and the finished quality is as much down to the printing quality as it is to the paper quality chosen by the user.

## Slide 21: P1.3 – Understanding Computer Components – Peripheral Devices - Output
Plotters - A plotter is an output peripheral device used with a computer, similar to a printer. However instead of printing text or images, a plotter is more usually used to draw up technical plans and blueprints. Instead of the print cartridge found in a printer, a plotter commonly uses pens, the number of colours depending on the quality of the plotter.
If you want to put a mark on a piece of paper with a printer, at a specific point, for example printing off some text, you need to make specific coordinates for where the text will end up on the page. When a printer sets to work, the paper feeds through the printer in a single pass, until the correct place down the length of the paper is found. Then the print head will move across the paper to the correct point and the printing will begin. If a whole page is to be printed, the print head will move across line by line until the text is printed.
With a plotter, a similar method of moving the paper and pen holder are used to allow the pen to be in precisely the right point at the right time. However the order of print is different from a printer. The pen does not start at the top right moving to the left and then down a line. The plotter takes the whole image data, then calculates a path for the pen. While the path for the pen may look complicated while the pen is in motion, In fact the plotter has calculated the shortest route for the pen, that involves the least amount of crossed lines as possible. This not only makes the path more efficient, but also ensures there is the least possible chance of the final drawing getting smudged.
More than just pens can be employed, for example some plotters are used with small knife blades that pivot to follow the path of the plotter. These 'drag knife' cutters are used for such tasks as cutting out vinyl sheet to make custom signs, like the type seen on the sides of vehicles to advertise the details of a company, or tradesman.

## Slide 22: P1.3 – Understanding Computer Components – Peripheral Devices - Output
Speakers – One of the few things that has not changed much over the last 30 years is the quality of speaker output. There are multiple ways that they can connect to the System, through the sound card, through the DVD or CD output or through wirelessly through Wi-Fi.
As an output there are several kinds, Standard, 5.1 and 7.1, different ways of hearing the same thing, Jack of USB, different ways of plugging them in. Speakers externally are ultimately better than internal speakers, speakers cost and computer sales companies prefer for the buyer to incur that cost in their own time. But they are important, from the moment the start up sound rings out to shutting down we listen to them, we play music through them, watch videos through them, use them for editing and recording and yet we pay them little attention.
Speakers often come as part of the package, small footprint speakers that connect directly through a split left and right audio to a single output jack on the system, they are usually powered but sometimes the speakers are of such low capacity that they may not require power or feed power from the USB socket.
The highest level is the Midi output card, used my musicians for the best of sound quality and input facilities.
P1.3 – Task 03 – Create a User Guide that explains the forms, function and varieties of output components.
Monitor | Printer | Plotter | Speaker

## Slide 23: P1.4 – Understanding Computer Components – Peripheral Devices - Input
  Digital cameras (e.g. zoom, ISO, aperture f/stop) – This is the most common method companies now use to get images from one location to another and with the development of removable medium like memory cards, the process has become easier and more usable.
  Digital cameras bacically are like the older SLR cameras, they open their apertures, control the amount of light and digitally imprint the image whereas SLR’s burn the image onto negative film.
  Digital cameras are rarely better than SLR’s in terms of quality of captured image resolution but there are cameras that are better. The digital images stored of Vancouver, Paris, Tokyo and London are 26gigapixels, the equivilent of 26,000 digital images in a single stored image.
  The biggest difference between SLR and Digital is the Zoom, SLR’s use lenses that allow the cameras to get distant information closer. Digital cameras do not. Lenses work like a telescope, they take the massive amount of information the eye can see and brings it closer using convex light focuses. Digital does not, it merely takes the image it seems through the lens and when zoomed, makes up the missing pixels by adjusting the sharpen width. This is flawed and only Digital Cameras with SLR lenses can manage these without the loss of definition.
  Despite the technology for storing the images being different, the technology of filtering and grabbing the images are the same for SLR and Digital. They both use ISO, aperture and f/stop settings to open the iris and allow light in.

## Slide 24: P1.4 – Understanding Computer Components – Peripheral Devices - Input
  Scanners – Basically what they do is image recognise whatever is on the tray, digitally scan each line like a barcode, stores each line as a image of pixels and attaches the lines back as a solid image when complete. Scanners do not know or care what they scan until the software with them or an external programs is requested.
  Image depth on scanners is about how much of the lines they scan, the higher the resolution, the smaller the lines are in length but not width. 4800 dpi for instance is good but can grow larger to 9600dpi when set to 64bit colour depth. Either way this will be a large file size and good quality.
  At the end of the day scanners are there to scan something that is already created, a 9600 dpi scan of an image in a magazine will not improve it’s quality if the image is published at 600dpi. The scanned image will pick out the grain of the paper, the tonal variations of the bind but not change the closeness of the pixels. Image manipulation can take care of a little of that by blending (blurring) or sharpening (adding missing pixels) to the image.
  Alternatively scanning a digital image will not make it better but scanning a 35mm published photo can. This will pick out the depth and resolution of the image that will be there because it is a real image that burns the picture onto film in maximum resolution. This is their greatest benefit and one of the few successful ways of transferring an image from printed to digital form without the loss of quality. The downside is time and hardware, scanners are rare in companies, the user needs to be logged in to the connected machine and the file needs to be saved to a usable location afterwards.

## Slide 25: P1.4 – Understanding Computer Components – Peripheral Devices - Input
  WebCam– Basically these are small range, limited cameras that attach to the USB socket and on instruction record for immediate playback or save. Over the last twenty years the popularity of these has grown, specifically from the adaptation of Video Conferencing and home conferencing.
  What has changed is resolution, grown in the last ten years from 300 pixels to 1.3 mega pixels. They can be better but streaming live video on anything stronger takes memory and band width. For industry there are better cameras, conference cameras etc. with up to 4 mega pixels but work better off a T1 line than standard connection.
  The technology is simple, the camera is converted into pure digital information and streamed to the system which reinterprets it as an image, the process is so common there is little or no slow down making them useful and with their prevalence, cheap.
  Microphone – Most people overlook these until they realise they need them. Laptops for instance come with them built in to a small hole on the screen on the side. Full systems however need to have an external one. All system sound cards come with a jack socket for a microphone and as long as the sound card is installed properly, the microphone will work.
  Microphones are reverse earphones, the technology for computer microphones has not changed, just slightly improved in size and quality. They can have sound limitation, reduced feedback, audio muxing etc. but most of these are software controlled.
  On a professional level they are used through the midi interface card for better quality but for everyone else, the system jack is enough.
  P1.4 – Task 04 – Create a User Guide that explains the forms, function and varieties of input devices.
Cameras | Scanners | WebCam | Microphone

## Slide 26: P1.5 – Understanding Computer Components – Peripheral Devices - Cabling
In order for systems to connect to a network they need cables, or Wi-Fi. Cables are simply faster and in a network, work, school environment, cables are the default. With the exclusion of Fibre Optic and the increased used of Wi-Fi, cabling has changed little other than the move towards RJ45.
Coaxial Cable - You can construct an Ethernet network by using one of two different types of cable: coaxial cable, which resembles TV cable, or twisted-pair cable, which looks like phone cable. Twisted-pair cable is sometimes called UTP, or 10BaseT cable.
This type of cable that was once popular for Ethernet networks is coaxial cable, sometimes called thinnet or BNC cable because of the type of connectors used on each end of the cable. Thinnet cable operates only at 10Mbps and is rarely used for new networks. However, you’ll find plenty of existing thinnet networks still being used.
You may encounter other types of cable in an existing network: thick yellow cable that used to be the only type of cable used for Ethernet, fibre-optic cables that span long distances at high speeds, or thick twisted-pair bundles that carry multiple sets of twisted-pair cable between wiring closets in a large building. For all but the largest networks, the choice is between coaxial cable and twisted-pair cable.
Twisted-pair cable - The most popular type of cable today is twisted-pair cable, or UTP (Unshielded Twisted Pair). UTP cable is even cheaper than thin coaxial cable, and best of all, many modern buildings are already wired with twisted-pair cable because this type of wiring is often used with modern phone systems.

## Slide 27: P1.5 – Understanding Computer Components – Peripheral Devices - Cabling
BNC connectors - You attach thinnet to the network interface card by using a goofy twist on connector called a BNC connector. You can purchase preassembled cables with BNC connectors already attached in lengths of 25 or 50 feet, or you can buy bulk cable on a big spool and attach the connectors yourself by using a special tool called a crimper. With coaxial cables, you connect your computers point-to-point in a bus topology. At each computer, a T connector is used to connect two cables to the network interface card.
A special plug called a terminator is required at each end of a series of thinnet cables. The terminator prevents data from hitting a dead end and returns the information back down the line.
The cables strung end-to-end from one terminator to the other are collectively called a segment. The maximum length of a thinnet segment is about 200 meters (actually, 185 meters). You can connect as many as 30 computers on one segment. To span a distance greater than 185 metres or to connect more than 30 computers, you must use two or more segments with a device called a repeater to connect each segment.
RJ45 Connectors - UTP cable connectors look like modular phone connectors but are a bit larger. UTP connectors are officially called RJ-45 connectors. Like thinnet cable, UTP cable is also sold in prefabricated lengths. However, RJ-45 connectors are much easier to attach to bulk UTP cable than BNC cables are to attach to bulk coaxial cable. They simply plug into the network card like a telephone plugs into the wall.
The maximum allowable cable length between the hub and the computer is 100 metres (about 328 feet) All computers now come with an RJ45 connector socket because this is becoming the standard method of base unit connectivity.

## Slide 28: P1.5 – Understanding Computer Components – Peripheral Devices - Cabling
STP – Shielded Twisted pair - In environments that have a lot of electrical interference, such as factories, you may want to use shielded twisted-pair cable, also known as STP. Because STP can be as much as three times more expensive than regular UTP, you won’t want to use STP unless you have to. With a little care, UTP can withstand the amount of electrical interference found in a normal office environment.
Most STP cable is shielded by a layer of Aluminium foil. For buildings with unusually high amounts of electrical interference, you can use more expensive braided copper shielding for even more protection.
Category 5 (Cat5) - Category 5 or Cat 5 is a standard measure for cabling, Cat1 for Voice to Cat6 for 1000Mbps. Cat5 is the standard 100MBps cabling required for modern networking. If you’re installing cable for a Fast Ethernet system, you should be extra careful to follow the rules of Category-5 cabling. That means, among other things, making sure that you use Category-5 components throughout. The cable and all the connectors must be up to Category-5 specs. When you attach the connectors, don’t untwist more than 1⁄2 inch of cable. And don’t try to stretch the cable runs beyond the 100-meter maximum.

## Slide 29: P1.5 – Understanding Computer Components – Peripheral Devices - Cabling
UTP (Unshielded twisted Pairs) - Unshielded twisted-pair cable (also known as UTP) became popular in the 1990s because it’s easier to install, lighter, more reliable, and offers more flexibility in how networks are designed. 10BaseT networks use a star topology with hubs at the centre of each star. Although the maximum length of 10BaseT cable is only 100 meters, hubs can be chained together to extend networks well beyond the 100-meter limit.
10BaseT cable has four pairs of wires that are twisted together throughout the entire span of the cable. However, 10BaseT uses only two of these wire pairs, so the unused pairs are spares. UTP cable is even cheaper than thin coaxial cable, and best of all, many modern buildings are already wired with twisted-pair cable because this type of wiring is often used with modern phone systems.
Fibre optic – Fibre Optic is called 10BaseFX. Because fibre-optic cable is expensive and tricky to install, it isn’t used much for individual computers in a network. However, it’s commonly used as a network backbone. For example, a fibre backbone is often used to connect individual workgroup hubs to routers and servers.
Fibre-optic networks also require NICs. Fibre-optic NICs are still too expensive for desktop use in most networks. Instead, they’re used for high-speed backbones. If a server connects to a high-speed fibre backbone, it will need a fibre-optic NIC that matches the fibre-optic cable being used.

## Slide 30: P1.5 – Understanding Computer Components – Peripheral Devices - Cabling
Wireless mobile technology - A wireless network is a network that uses radio signals rather than direct cable connections to exchange information. A computer with a wireless network connection is like a mobile phone. Just as you don’t have to be connected to a phone line to use a mobile phone, you don’t have to be connected to a network cable to use a wireless networked computer.
A wireless network is often referred to as a WLAN, for wireless local area network. The term Wi-Fi is often used to describe wireless networks, although it technically refers to just one form of wireless networks: the 802.11b standard.
A wireless network has a name, known as a SSID. SSID stands for service set identifier. Each of the computers that belong to a single wireless network must have the same SSID.
Wireless networks can transmit over any of several channels. In order for computers to talk to each other, they must be configured to transmit on the same channel. The simplest type of wireless network consists of two or more computers with wireless network adapters. This type of network is called an ad-hoc mode network.
A more complex type of network is an infrastructure mode network. All this really means is that a group of wireless computers can be connected not only to each other, but also to an existing cabled network via a device called a wireless access point, or WAP (Hotspot).
  P1.5 – Task 05 – Create a User Guide that explains the forms, function and varieties of cabling for a System Setup.
Coaxial | Twisted Pair | BNC | RJ45
Cat-5e and 6 | UPT | Fibre Optic | Wireless

## Slide 31: M1.1 – Understanding Computer Components – Backup Storage - Options
Backing up files is an essential part of every business and is a routine even individual users should get used to. Fortunately over the years the facility, method and price of doing so has steadily come down. In companies, Network backup is a matter of routine, a program some time in the evening or night makes a copy of the network drives onto a tape or hard drive and the jobs done. For an individual the choice of medium is different.
Disks – First there was CD, 700MB, then DVD, 4400MB, now Blu-Ray. These are still not enough to back up a network drive but they are very useful as timed backups. All systems except Thin Client come with these as standard, they run off the IDE cable to the motherboard and act like a separate hard drive, taking a drive letter. Only certain Drives are RW, rewritable, but disks are so cheap that most people do not bother. This is a big step from the 3.5” and the 5.25” drives that were prevalent until 1999.
Pen drives and memory cards – These are the more probably method of System storage and backup people will use. The difference is that pen drives plug straight into the USB drive and memory cards go into sockets or bayonets. Size has changed the way we use them, the standard like memory in the machine has doubled almost every 2 years, what was 32mb 15 years ago and seemed like a lot (the equivalent of 24 floppy disks) now the cast away standard is 8gb, with 16, 32, 64 and larger available in shops. Every supermarket sells them, that’s how common they are, businesses give them away with their logos on them for publicity and it works out roughly at £1 per GB.
Portable and fixed drives – Like Pen Drives, these either plug into the USB drive, tend to be large capacity, bigger than Pen Drives, or they are secondary or third drives inside the computer. Second drives and portable hard drives are cheap, working at about 10gb per £1, sizes of 320gb up to 4tb are common. They are basically mass storage, do not need an OS installed, can work on any computer or OS except Phone or most Tablets and are relatively reliable, Fixed drives more so because they do not get moved around. The can either be SATA or IDE, portable ones are housed in a cradle or dock which is then USB connected.

## Slide 32: M1.1 – Understanding Computer Components – Backup Storage - Options
Optical media – These are more common now for network storage, capable of saving 120gb on one drive for a complete backup, takes an hour on a standard network to copy down to, can be carried away, and then reused, deleted like a memory stick and resaved. Network managers tend to use these as a medium because of their reliability, set it running, leave it, take it away when done. Sizes of these vary again with price. They are not as easily accessible for home use like memory sticks or USB because they take time to archive and search.
Offsite data storage – This should be an essential part of any secure backup routine, and the easiest approach is to use an online backup service.
Managing a local backup routine can be a chore that often gets postponed and forgotten about, but online backup, which keeps all your files in the cloud, is usually a set-and-forget affair. It’s also more secure than local backup because the data is taken offsite, so you’ll be able to recover it in the event of fire, food or theft. Now that broadband is so fast and cheap, backing up all your data online is a realistic proposition. You can also use synchronisation services to make sure the work you want to take home gets there long before you do, enabling you to access your data wherever you are.
The company running the service will ensure that your data is always readable, making it less hassle for you. However, the downside is that you have to pay a monthly or yearly fee. If you fail to keep up payments, you lose access to your files.
The other potential problem is that if the provider goes bankrupt, there’s a chance you won’t be able to access your data. This means it’s best to use online backup in conjunction with an offline one, but a local backup should be your primary method as it’s secure, quick and convenient.
  M1.1 – Task 06 – Create a User Guide that explains the forms, function and varieties of different Backup Storage options for a System Setup including suitability for different systems and costs.
Disks | Pen drives and Memory cards | Portable and fixed drives | Optical media | Offsite data storage

## Slide 33: M1.2 – Understanding Computer Components – Backup Storage - Options
  Everyone chooses their storage medium for a reason, speed, cost, capacity, portability, security etc. The choices are varied. In business the choices come down to three things, security, capacity and transfer rate.
  Security – Under the DPA, business have to protect their information but all storage has its risks. Password protection and encryption come into play but that is an extra process to deal with. Programs on networks can encrypt the information on a storage device as it writes it but the choice of an employee at a company to take work home cannot access this. Cloud computing is useful for this, password protected, secure logins etc. Pen Drives are great but easily lost, CD’s and DVD’s get corrupted or scratched, Portable hard drives are often stolen. All storage mediums have their issues.
  Capacity – Size matters, especially when it comes to file storage, work documents are small, a memory stick is good, add a video to a Powerpoint and the file size grows. Disks can store 4,7gb but a memory stick can store more. You would not backup a network drive to a memory stick, even a large one but you would also not store a few work documents on a DVD because it would take too long and be a waste of a disk.
  Transfer rate – how quickly it takes to copy the files down has an impact on the medium, DVD’s are slow, it takes almost the same time for 100mb as it does for 4.7gb. Memory sticks are fast as are portable hard drives but internal drives are faster, more direct access to the motherboard. Uploading to the Cloud takes a very long time but is more convenient.
  M1.2 – Task 07 – Using the table, compare the different backing storages available and outline the positive and negative aspects of each.
Medium | Security | Capacity | Transfer rate | Positive aspects | Negative Aspects
Disks |  |  |  |  | 
Pen drives and Memory cards |  |  |  |  | 
Portable and fixed drives |  |  |  |  | 
Optical media |  |  |  |  | 
Offsite data storage |  |  |  |  | 

## Slide 34: P2.1 – Understanding Computer Components – OS’s - Windows
Operating systems are vital to the use of computers, they tell the machine what it is, what language, where the programs are, when things are stored, how to do things, the instruction codes to do everything. All System operating systems, from the simplest to the most complex, must provide certain core functions, such as the ability to connect to other computers on the network, store files and other resources, provide for security, connect devices, etc. For this there has always been two direct rivals Microsoft and Macintosh. But now there is also Linux, the third contender.
Windows 8 is the latest in a long series of Windows OS’s. Windows XP was the first Microsoft operating system that was reliable enough to work as a network server on large networks. Version 8 shipped in 2011, so it is now more than 3 years old. That’s a lifetime in operating system years (which are kind of like dog years).
Probably the most important feature of Windows 8 is its touch screen technology, which is based on the concept of tablets. To access shared resources within a Windows System, you must have a valid user account within the OS and be granted rights to access the resources.
Although Windows 8 is newer, Windows 2000 and NT Server is currently the most popular server operating system from Microsoft. Windows Servers built on the strengths of Windows NT Server 4 by adding new features that made Windows 2000 Server faster, easier to manage, more reliable, and easier to use for large and small networks alike.
The biggest benefit of Windows, including Windows 8, is that we know how to use it, we have been brought up on Windows, we log in to it almost every day, we access our programs and files from the icons on the desktop. It may not be the best OS but it is the most common and therefor the preferred for business and home use.

## Slide 35: P2.1 – Understanding Computer Components – OS’s - MacOS
Operating systems do not come cheap and can be unreliable for numerous reasons, incompatibility with hardware being the main one, the way it manages files and allocated memory to programs is another. Other considerations need to be taken including price, speed, types of machines, ease of use, familiarity and function.
Mac OSX - For Macintosh computers, Apple offers their own operating system known as Mac OS/X. Mac OS/X has all the features you’d expect in a System operating system: file and printer sharing, Internet features, e-mail, and so on. This would require setting up a Mac System within the building and sticking to this as the ,main focus. It is possible to set up a small MAC OS/X network to run alongside the PC based network using a Bridge, this could then control the Mac computers within a sealed network space. Connection to the Microsoft or Novell side can then take place allowing MAC machines to operate as stand alone and linked to the system.
MacOS’s have been through a lot of changes over the years and was dependant on the hardware used, PowerPC’s for instance used one OS which was not totally compatible with PowerMacs or the new G5’s. The different versions, Lion, Leopard et al, have been adaptations of previous OS’s to make it better, more compatible and more in tune with the hardware changes in the industry.
At the end of the day, MacOS operated similar to Windows, it loads, saves, stored, connects etc. it just does it differently.

## Slide 36: P2.1 – Understanding Computer Components – OS’s - Linux
Linux - Linux is a free operating system that is based on UNIX, a powerful network operating system often used on large networks. Linux was started by Linus Torvalds. He enlisted help from hundreds of programmers throughout the world, who volunteered their time and efforts via the Internet. Today, Linux is a full-featured version of UNIX; its users consider it to be as good or better than Windows. In fact, almost as many people now use Linux as use Macintosh computers.
Linux offers the same System benefits of UNIX and can be an excellent choice as a server operating system. There are different types, all free, and all with their relative merits:
Fedora is one of the popular Linux distributions. At one time, Fedora was an inexpensive distribution offered by Red Hat.
Mandriva Linux is another popular Linux distribution, one that is often recommended as the easiest for first-time Linux users to install.
SuSE is a popular Linux distribution that comes on six CD-ROMs and includes more than 1,500 Linux application programs and utilities, including everything you need to set up a network, Web, e-mail, or electronic commerce server. You can find more information at www.suse.com.
At the end of the day Linux is more adaptable than Windows, it is free and it functions in the same way. The downside is compatibility, setting up a Linux machine is new to most people, integrating all the hardware can be a burden and adding new hardware along the line can cause issues.
P2.1 – Task 08 – Explain the purpose and outline the functions of operating systems with examples.
P2.2 – Task 09 - Compares different types of operating systems and the purpose of their different features.
Windows | MacOS | Linux

## Slide 37: P2.3 – Understanding Computer Components – OS’s - Functions
File Management - One of the most important functions of an operating system is its ability to store and manage files for the allowed users by separating them into locations other users cannot access without Administrative rights to do so. The most common resource that’s shared is the file system. A system must be able to share some or all of its disk space with other users so that those users can treat the systems disk space as their own computer’s disk space. Some files can be shared, templates, office files, installed programs, others are kept safe, work docs, pictures etc.
The Operating System allows the system administrator to determine which portions of the file system to share and what to restrict to users accounts. Although an entire hard drive can be shared, it is not commonly done. Instead, individual directories or folders are shared. The administrator can control which users are allowed to access each shared folder.
Because file sharing is the reason many systems are used, network operating systems have more sophisticated disk management features than are found in desktop operating systems. For example, most network operating systems have the ability to manage two or more hard drives as if they were a single drive. In addition, most can create mirrors, which automatically keeps a backup copy of a drive on a second drive.

## Slide 38: P2.3 – Understanding Computer Components – OS’s - Functions
Security services - All operating systems must provide some measure of security to protect the users accounts from unauthorized access. Hacking seems to be the national pastime these days. With most systems connected to the Internet, anyone anywhere in the world can and probably will try to break into your set up.
The most basic type of security is handled through user accounts, which grant individual users the right to access the system resources and govern what resources the user can access. User accounts are secured by passwords; therefore, good password policy is a cornerstone of any security system.
Most operating systems let you establish password policies, requiring that passwords have a minimum length and include a mix of letters and numerals. In addition, passwords can be set to expire after a certain number of days, so users can be forced to frequently change their passwords.
Most network operating systems also provide for data encryption, which scrambles data before it is sent over the network or saved on disk, and digital certificates, which are used to ensure that users are who they say they are and files are what they claim to be.
But more importantly OS’s when installed have Virus and Adware protection, not the best, but adequate enough to protect a system after installation. For instance Windows Defender. The threat is 98% from the Internet, the threat is real and OS’s manage these threats by placing files in quarantine if dangerous, restricting users from installing software without administrative rights and have programs such as Scandisk to manage faults.

## Slide 39: P2.3 – Understanding Computer Components – OS’s - Functions
System Management – An operating system must support a wide variety of networking protocols in order to meet the needs of its users. If you look at the Control Panel on the computer and click on network (hold down Windows key and press Pause) you will see that a range of networking protocols are in place that manage the internet and network connection.
Within Control Panels the IRQ resources are set, the IP addressing, the TCP etc. These are all managed by the OS so the user does not need to. Similarly folders are constructed for each user, templates from programs like Office are created and moved into each users account.
Device Driver Management – In Control Panels, click on Hardware and Device manager. In here all the devices currently connected inside and outside the machine are managed from the cards and adapters for the sound and screen to the network card, memory, Hard drives etc. When a new device is connected, device manager adds it to the list, configures the drivers, copies the relevant files from the OS set up folder and then adds the hardware ready for use. When it cannot find the hardware driver it looks on the OS site for it. All these drivers remain installed, when the device is plugged back in a week, month or years time, it is automatically added back in. Without this the user would spend a lot of time constantly adding in their USB sticks and printers before being able to use them.
P2.3 – Task 10 – Explain the purpose and outline the functions of operating systems when it comes to File Management, Security, System Management and Device Drivers with examples.
File Management | Security | System Management | Device Drivers

## Slide 40: P2.4 – Understanding Computer Components – OS’s – CLI and GUI
Visual OS - Not all operating systems stick to the WIMP (Windows, Icons, Mouse and Pointers) environment because not all programs use WIMP. Some of the major packages from the past that are sill used today, Sims, FoxPro, Novell Client Server etc. still use CLI. But we are used to the basic WIMP environment, we have been brought up on clicking.
GUI – Graphic Line Interface – This is the Icons and pointers, the OS puts these on the screen and allows us to click on them, move them, add them to toolbars, put them onto the Start Menu, delete, change their shape etc. Whatever it takes to get on with the job. MacOS, Linux and Windows are all very similar, the icons are a bit different, the right click is different but most packages installed create their own folder structure and Icons to make them recognisable.
CLI – Command Line Interface - This is a DOS based environment where the user types in commands, the background of a Visual OS, command lines like Format, Scandisk, List, Rename, Ping etc., the language used by the System to make things happen. All GUI commands have a CLI command behind them, the GUI is just the way of disguising it. Network managers use this often to instruct servers to manage controls because it is more direct than a GUI, it is written in a Basic language, a set of universal instructions for the OS though the instructions vary from OS to OS.
P2.4 – Task 11 – Explain the purpose and outline the functions of operating systems when it comes to GUI and CLI with examples.

## Slide 41: P2.5 – Understanding Computer Components – OS’s - Features
There are Different reasons why we chose the OS we want and this is likely to be the second biggest choice in the setup and use of our system other than what system to buy.
Customisation – We would choose our OS because of the flexibility it allows when it comes to making it the way we want. We might change the hard drive configuration, partitioning it, we might change the icons, customise the toolbar, have sub-screens for our icons like a tablet, allow screen resolution changes for different applications, set it up to clean or scan at night etc. All OS’s allow these features but in different ways and to different degrees.
Connectivity – We chose our OS based on how easy it is to plug things in to it without all the fuss that comes with new things. Plug an Play. We also chose based on how easy it is to connect our system to the outside world to forums, conferencing and the internet. We have hardware lying around that we need to work, printers we need to connect. All OS’s are different, even Linux has different versions.
Stability and reliability – For those who have had different systems over the years, we tend to chose what OS based on what is the more reliable one for us. This is the primary reason why we chose things, was it stable, did it crash a lot, was it reliable, did the programs I needed to use work on it without crashing. On a grander scale network managers chose the OS based on this, Novell vs. Microsoft NT Server.

## Slide 42: P2.5 – Understanding Computer Components – OS’s - Features
Cost – Installing an OS on a machine costs money, well Microsoft and MacOS do. Without these oS’s the system would cost £70 cheaper, and when some systems can be purchased for £230 with Windows, this can be a substantial saving. Linux is free, lots of network managers set up Linux on machines because of this, for instance a school will have 200 PC’s, this could be a saving of £14k or the price of 56 new machines. Systems bought from shops come with the OS bundled, ready to type in the Serial Number, those constructed by a user from purchased parts do not and cost is a large consideration of this choice.
Ease of use – We know what we like based on what we are used to. This is another big reason why we chose the OS we do. Schools will install Windows because we know students are used to it, called the learning curve. Companies are the same, people know how to use the OS at work because they have it at home, if you have an Apple then you more than likely have MacOS, you will be used to is. You will be used to where the icons are, the menu, the interface, where Office saves things, where to look for stuff. You will know shortcut keys, most of these do not transfer from OS to OS, and knowing how to use the OS is a shortcut to getting on with business.
P2.5 – Task 12 – Explain the different considerations companies have when it comes to the choice of OS on Systems with examples.
Customisation | Connectivity | Stability and Reliability | Cost | Ease of Use

## Slide 43: P3.1 – Understanding Computer Components – Software Utilities
Built in to all Operating systems is a range of software utilities that allows the user to manage functions. There are programs that do these better but the standard utilities used day to day.
Access Rights - By some estimates, human errors, ignorance, and omissions cause more than half of all security breaches sustained by Systems. One of the most common methods by which an intruder gains access to a network is to simply ask a user for his password. For example, the intruder might pose as a technical support analyst who needs to know the password to troubleshoot a problem. This strategy is commonly called social engineering because it involves manipulating social relationships to gain access. A related practice is phishing, in which a person attempts to glean access or authentication information by posing as someone who needs that information. For example, a hacker might send an e-mail asking you to submit your user ID and password to a Web site whose link is provided in the message, claiming that it’s necessary to verify your account with a particular online retailer. Following are some additional risks associated with people:
  Intruders or attackers using social engineering or snooping to obtain user passwords
  An administrator incorrectly creating or configuring user IDs, groups, and their associated rights on a file server, resulting in file and logon access vulnerabilities
  Network administrators overlooking security flaws in topology or hardware configuration
  Network administrators overlooking security flaws in the operating system or application configuration
  Lack of proper documentation and communication of security policies, leading to deliberate or inadvertent misuse of files or network access
  Dishonest or disgruntled employees abusing their file and access rights
  An unused computer or terminal being left logged on to the network, thereby providing an entry point for an intruder
  Users or administrators choosing easy-to-guess passwords
  Authorized staff leaving computer room doors open or unlocked, allowing unauthorized individuals to enter
  Staff discarding disks or backup tapes in public waste containers
  Administrators neglecting to remove access and file rights for employees who have left the organization
  Users writing their passwords on paper, then placing the paper in an easily accessible place (for example, taping it to their monitor or keyboard)

## Slide 44: P3.1 – Understanding Computer Components – Software Utilities
Firewall - A firewall is a security-conscious program that sits between the Internet and your network with a single-minded task: preventing them from getting to us, a security guard if you will. All network traffic into and out of the System must pass through the firewall, which prevents unauthorised access to the network. Some type of firewall is a must-have if your system has a connection to the Internet, whether that connection is broadband (cable modem or DSL), T1, or some other high-speed connection. Without it, sooner or later a hacker will discover your unprotected network and tell his friends about it. Within a few hours your system and information on the system will be toast.
You can set up a firewall using two basic ways. The easiest way is to purchase a firewall application, which is basically a self-contained router with built-in firewall features. Most firewall applications include a Web-based interface that enables you to connect to the firewall from any computer on your network using a browser. You can then customize the firewall settings to suit your needs.
Alternatively, you can set up a server computer to function as a firewall computer. The server can run just about any network operating system, but most dedicated firewall systems run Linux. Whether you use a firewall application or a firewall computer, the firewall must be located between your network and the Internet. Here, one end of the firewall is connected to a network hub, which is, in turn, connected to the other computers on the network. The other end of the firewall is connected to the Internet. As a result, all traffic from the LAN to the Internet and vice versa must travel through the firewall.

## Slide 45: P3.1 – Understanding Computer Components – Software Utilities
Virus Checker - Every computer user is susceptible to attacks by computer viruses, and using a network increases your vulnerability because it exposes all network users to the risk of being infected by a virus that lands on any one network user’s computer. Viruses don’t just spontaneously appear out of nowhere. Viruses are computer programs that are created by malicious programmers.
The best way to protect your System from virus infection is to use an antivirus program. These programs have a catalogue of several thousand known viruses that they can detect and remove. In addition, they can spot the types of changes that viruses typically make to your computer’s files, thus decreasing the likelihood that some previously unknown virus will go undetected.
You can install antivirus software on each System. This technique would be the most effective if you could count on all your users to keep their antivirus software up to date. Because that’s an unlikely proposition, you may want to adopt a more reliable approach to virus protection.
Managed antivirus services place antivirus client software on each client computer in your network. Then, an antivirus server automatically updates the clients on a regular basis to make sure that they’re kept up to date.
Server-based antivirus software protects your network servers from viruses. For example, you can install antivirus software on your mail server to scan all incoming mail for viruses and remove them before your network users ever see them.
Some firewall appliances include antivirus enforcement checks that don’t allow your users to access the Internet unless their antivirus software is up to date. This type of firewall provides the best antivirus protection available.

## Slide 46: P3.1 – Understanding Computer Components – Software Utilities
Permissions - User accounts are the backbone of a System’s Security. Through the use of user accounts, you can determine who can access your files, as well as what rights each user can and cannot have. You can restrict access to the System to just specific people or to certain hours of the day. In addition, you can lock out users who no longer need to access your system without deleting files.
Every user who accesses a system must have a user account. User accounts allow the person with administrator rights to determine who can access the system and what system resources each user can access. Also, the user account can be customised to provide features for users, such as a personalized Start menu or a display of recently used documents. Every user account is associated with a username (sometimes called a user ID), which the user must enter when logging in to the system. Accounts also has other information associated with it. In particular:
  The user’s password: This also includes the password policy, such as how often the user has to change his or her password, how complicated the password must be, etc.
  The user’s contact information: This includes full name, phone number, e-mail address, home address, and other related information.
  Account restrictions: This includes restrictions that allow the user to log on only during certain times of the day. This feature enables you to restrict your users to normal working hours and can also specify that the user can log on only at certain computers.
  Account status: You can temporarily disable a user account so that the user can’t log on.
  Home directory: This specifies a shared system folder where the user can store documents.
  External Access: These authorise the user to access the system remotely (Intranet access).
  Group memberships: These grant the user certain rights based on groups to which they belong.
  P3.1 – Task 13 – Explain the different considerations companies have when it comes to the Security options with the OS with examples.
  D1.1 – Task 14 - For a specific business system, identify how these security utilities and protocols will improve the performance of computer systems.
  Each improvement will need to be detailed and clearly linked to a business purpose.
Access Rights | Firewall | Virus Checker | Permissions

## Slide 47: P3.2 – Understanding Computer Components – Software Utilities
Defragmentation – This is a useful little program built into the CLI and GUI on OS’s in order to speed computer and file access up. When a file is saved the file looks for a place on a track to store itself, if there is space it will store in one complete file, if the space is not available, it will store fractions of itself in different areas. When the computer opens the file, the computer hunts for the fractions and patches it back together. This does not take long but if the file was saved intact, the system would not need that process. Defragmenting puts all the files back together as single access files, sorts out the clutter to allow the file to open faster.
Housekeeping – Systems need to manage files and file locations, backing up, restoring, self repairing, recovering from crashes, overwriting duplicate files, removing and uninstalling old programs, deleting previous versions of programs when a new version is installed. These are all part of the OS job, without these your System would get filled.
Drive formatting – When a system needs to kill a drive and start again, formatting and partitioning a drive means starting again. When a new hard drive for instance needs to be set up, the OS formats it, blanks it of all previous references. Similarly for Disks, memory stick, pen drives etc. a clean start on drives means they work faster, remove corruption and repurpose them.
Other – On the Start menu of your machine, for everything you see there are ten things you do not see, programs built into the OS for managing the system. They may never get used but they need to be there just in case, e.g. Bluetooth setup, Printer Configuration, backup and restore, changing Ease of Access, Setting Updates, Setting Remote Access, Power Options etc. Other than the programs you install for specific purposes, the OPS should have everything needed to manage the safety and use of the computer, and if it does not, then the next versions might.
  P3.2 – Task 15 – Explain the different purposes and options companies have when it comes to the Utility programmes with the OS with examples.
  D1.2 – Task 16 – For a specific business system, identify how these Utilities and procedures will improve the performance of computer systems.
  Each improvement will need to be detailed and clearly linked to a business purpose.
Deframentation | Housekeeping | Drive Formatting | Other

## Slide 48: LO1 - Assessment Task List
  P1.1 – Task 01 – Introduce the principles, concepts and purpose of Computer Systems.
  P1.2 – Task 02 – Create a User Guide that explains the forms, function and varieties of computer hardware components
  P1.3 – Task 03 – Create a User Guide that explains the forms, function and varieties of output components.
  P1.4 – Task 04 – Create a User Guide that explains the forms, function and varieties of input devices.
  P1.5 – Task 05 – Create a User Guide that explains the forms, function and varieties of cabling for a System Setup.
  M1.1 – Task 06 – Create a User Guide that explains the forms, function and varieties of different Backup Storage options for a System Setup including suitability for different systems and costs.
  M1.2 – Task 07 – Using the table, compare the different backing storages available and outline the positive and negative aspects of each.
P2.1 – Task 08 – Explain the purpose and outline the functions of operating systems with examples.
P2.2 – Task 09 - Compares different types of operating systems and the purpose of their different features.
  P2.3 – Task 10 – Explain the purpose and outline the functions of operating systems when it comes to File Management, Security, System Management and Device Drivers with examples.
  P2.4 – Task 11 – Explain the purpose and outline the functions of operating systems when it comes to GUI and CLI with examples.
  P2.5 – Task 12 – Explain the different considerations companies have when it comes to the choice of OS on Systems with examples.
  P3.1 – Task 13 – Explain the different considerations companies have when it comes to the Security options with the OS with examples.
  D1.1 – Task 14 - For a specific business system, identify how these security utilities and protocols will improve the performance of computer systems.
  P3.2 – Task 15 – Explain the different purposes and options companies have when it comes to the Utility programmes with the OS with examples.
  D1.2 – Task 16 – For a specific business system, identify how these Utilities and procedures will improve the performance of computer systems.