## Slide 1: Unit 15
Project Planning with IT
L/600/6610
LO4 - Be able to Connect and Configure Platforms and Devices

## Slide 2: LO4 - Assessment Criteria
Learning Outcome (LO) The learner will: |  | Pass The assessment criteria are the pass requirements for this unit. The learner can: |  | Merit For merit the evidence must show that, in addition to the pass criteria, the learner is able to: | Distinction For distinction the evidence must show that, in addition to the pass and merit criteria, the learner is able to:
1 | Understand game platform types | P1 | Describe game platform types with some appropriate use of subject terminology | M1 - Describe how computer games platform types have developed over time | D1 - Explore potential future gaming platform types
2 | Understand hardware technologies for game platforms | P2 | Describe hardware technologies for game platforms with some appropriate use of subject terminology | M2 - Describe mobile technologies for game platforms | D2 - Evaluate the suitability of mobile technologies for game play
3 | Understand software technologies for game platforms | P3 | Describe software technologies for game platforms expressing ideas with some appropriate use of subject terminology | M3 - Discuss the different software technologies for multiple platform usage | D3 - Justify the choice of platform on which to run an identified software technology
4 | Be able to connect and configure platforms and devices to enable gameplay | P4 | Apply techniques to connect and configure platforms and devices with some assistance | M4 - Explain the different connection types for multiplayer gaming | D4 - Justify how the connection types are appropriate for the different multiplayer gaming experiences

## Slide 3: Assessment Criteria P4, M4 and D4
Assessment Criteria P4
P4 The learners will need to provide evidence they have connected and configured at least two different platforms types, devices and games ready for game play. This could be evidenced in a report which could be supported with observation reports and photos with annotations.
Assessment Criteria M4,
For merit criterion M4 learners must explain the different ways in which you could connect for multiplayer gaming for at least three of those identified in the learning outcome. This could be evidenced in the form of a report, presentation or leaflet for new users and supported by detailed annotated photos for connecting different multiplayer games
Assessment Criteria D4
For distinction criterion D4 learners must justify from the available connection types how each is appropriate for the different multiplayer gaming experiences. It may be beneficial for the Unit 15 learners to be given a scenario which enables them to research and discuss different connections for different users with a view to providing a final judgment. This could be an expansion on the merit criteria and learners should include costs, speed, number of users and user locations. Findings should be well documented and justifications clearly explained.

## Slide 4: LO4 - Be able to connect and configure platforms and devices to enable gameplay
In this outcome the learners will need to be given the opportunity to connect and configure platforms and devices to enable gameplay including connecting the connections needed for multiplayer gaming. They should practice across a range of platforms including mobile technologies and understand the configuration settings and devices that they will use.
The learners should carry out practical exercises using a variety of different platforms, peripherals and software. This works well with tutor demonstrating, then the learners carrying out practical exercises and recording their findings. If it is difficult to provide the learners with individual exercise they could work in groups, each taking a different role to ensure practical and hands-on experience for all.

## Slide 5: P4.1 – Connection devices – Console to Display
Ever since the first console beyond a box came out, the Atari VCS and Intellivision Console, there has been a need to connect them to the television sets. Unlike Computers, the consoles took advantage of the UHF/VHF signal to output, restricting the quality down to its own internal hardware and cards but never restricted on the quality on the screens.
For most consoles up to the PlayStation 1 and Nintendo 64 a standard 3 pinned jack, one for VHF, one for left and one for right audio was needed. See the image on the right. For the Megadrive this was a one pin lead with all three wires merged to the VHF output.
Higher quality output from the 32bit onwards consoles demanded a different connector, and every console had something different depending on the motherboard inside. Even then the standard screen adapter tended to be VHF or Scart for the better signal and better graphics.
Now there is HDMI, the new standard ending. Ever console now has the HDMI standard connector and different output socket which is capable of handing graphics up to 1900dpi.
P4.1 – Task 1 – Using examples and terminology discuss and explain the technology around the connector cables used to connect a console to a display.

## Slide 6: P4.2 – Connection devices – Console to Console
Even the earlier consoles could not connect to each other. With the exception of a PC using a network card, consoles worked independently of each other and other machines. The advent of the Internet capable consoles changed this but before the Internet there have been generations of consoles that had other methods of talking to each other.
Gameboy Advance network play – On the right is the cable used to connect two Gameboy advances to each other. The cable was little more than a chain link, games like Fifa and Mario Links 4 Swords allowed up to 4 people to play against each other through a daisy chain link, Speeds were tolerable as the distance was short. Games too advantage of this to add that extra level of gameplay and novelty.
Newer handhelds like DS and DSi allow network play via internal Wi-Fi. This is not something new but it was something novel, to play multiplayer games in a house against other people in the house. This works off the Wi-Fi signal, as long as both machines are within the Wi-Fi range they can see each others IP address and connect to it.
Xbox System Link - System link play is a form of multiplayer gaming that lets you connect two Xbox 360 consoles by using a cable or up to 16 consoles through a network. With linked consoles, multiple players can play the same game. This type of multiplayer gaming is different from split-screen multiplayer gaming, in which all the players are connected to the same console.
PS4 and Vita – The new trend is to connect the Vita to the Wi-Fi and allow PS4 games to be streamed to the console. This way the Vita is nothing more than a joystick with a screen routing whatever the PS4 is doing onto it in real time. This is similar to the WiiU which allows the same streaming of the game onto the WiiU Gamepad, allowing the game to continue through streaming.
P4.2 – Task 2 – Using examples and terminology discuss and explain the technology around the connector cables used to connect a console to a Console.

## Slide 7
A Local Area Network (LAN) is a network that is confined to a relatively small area. It is generally limited to a geographic area such as a writing lab, school, or building. Rarely are LAN computers more than a mile apart.
In a typical LAN configuration, one computer is designated as the file server. It stores all of the software that controls the network, as well as the software that can be shared by the computers attached to the network. Computers connected to the file server are called workstations.
The workstations can be less powerful than the file server, and they may have additional software on their hard drives. On many LANs, cables are used to connect the network interface cards in each computer; other LANs may be wireless.
All non wireless devices are connected along the cabling and information flows along that line through direct or an indirect path if the path is blocked or busy like water would flow through inter-connected pipes. Directing this traffic are hubs, routers and servers.
In terms of gameplay companies used to set up LAN’s for PC gaming in Internet Cafes and for conferences. Today it is much easier with Wi-Fi and the availability of hardware even for the home to set up LAN games. With modern LAN’s the consoles can also connect but not to PC’s, allowing LAN play of multiplayer gaming over a short distance. With the advent of Internet Play this is becoming less and less.
Handhelds can still use this, see slide 6 for details.
P4.3 – Connection devices – Networks

## Slide 8
DISTRIBUTED SYSTEMS
Networked computers linked by cables.
Networks were developed allowing standalone computers to communicate with each other through cabling.
Processing is carried out both centrally on a ‘server’ and on the computers. These computers can either be base Units(machines with storage) or workstations (thin client).
LANs allow local network access allow global network access (such as to the Internet) by linking back to a network server.
Different types of cabling allows communication between computers e.g. Star, linear, ring.
P4.3 – Connection devices – Networks

## Slide 9
P4.3 – Connection devices – Networks

## Slide 10
Wide Area Networks (WANs) connect larger geographic areas, such as Florida, the United States, or the world. Dedicated transoceanic cabling or satellite uplinks may be used to connect this type of network.
Using a WAN, schools in Florida can communicate with places like Tokyo in a matter of minutes, without paying enormous phone bills. These are usually dedicated or protected lines that separate the system from the Internet lines.
A WAN is complicated. It uses multiplexers to connect local and metropolitan networks to global communications networks like the Internet. To users, however, a WAN will not appear to be much different than a LAN except for geographical location and speed of use.
Examples of WAN game playing includes Starcraft, linked servers provide the space just for the game and traffic, dedicated lines just for gameplay, this reduces down the amount of exterior traffic that slows a line down.
P4.3 – Task 3 – Using examples and terminology discuss and explain the technology around the LAN and WAN network connections and how it is used in the gaming world.
P4.3 – Connection devices – Networks

## Slide 11: P4.4 – Connection devices – Wireless and Wireless Devices
Wi-Fi or Wireless - The common name for wireless networking using the 802.11 protocols. With wireless networking, you don’t need cables to connect your computers. Instead, wireless networks use radio waves to send and receive network signals. As a result, a computer can connect to a wireless network at any location in your home or office. Wireless networks are especially useful for notebook computers. After all, the main benefit of a notebook computer is that you can carry it around with you wherever you go.
A wireless network is often referred to as a WLAN, for wireless local area network. The term Wi-Fi is often used to describe wireless networks, although it technically refers to just one form of wireless networks: the 802.11b standard. A wireless network has a name, known as a SSID. SSID stands for service set identifier . Each of the computers that belong to a single wireless network must have the same SSID.
Wireless networks can transmit over any of several channels. In order for computers to talk to each other, they must be configured to transmit on the same channel. The simplest type of wireless network consists of two or more computers with wireless network adapters. This type of network is called an ad-hoc mode network.
A more complex type of network is an infrastructure mode network. All this really means is that a group of wireless computers can be connected not only to each other, but also to an existing cabled network via a device called a wireless access point, or WAP.
In terms of gaming Wireless has become more common as a platform for connecting machines and as a gaming link between machines. Wi-Fi play has been around since the Gameboy Advance in terms of Handhelds. PC’s have dominated this market for decades having the technology at hand. Now all handhelds and mobiles come with a Wi-Fi connection. Games like DrawIt, Links 4 Swords and Fifa used this method as a selling point with the machines capable of taking advantage of the increased Wi-Fi speed of homes.
For a full console like Xbox or PS£ and 4, the Wi-Fi is just a means of connecting, slower than a direct Ethernet connection but useful for occasions.

## Slide 12: P4.4 – Connection devices – Wireless and Wireless Devices
Wireless devices to platforms e.g. joystick, controller, wheel – First there were wireless mice and they never caught on, then wireless keyboard, chewed through the batteries, ran out before you saved and when the batteries were low the keystrokes were intermittent. But everything is wireless as long as there is a charge we would all prefer our devices to be wireless.
XBox360 – The first controllers were not but then we found the battery packs chargeable off USB, now we would not play it without the wireless joy pads. Kinect is trying the next option and making you the joystick and not needing wireless at all. There is also the headset and a device to make the whole internet wireless.
Mobiles – born wireless and now connecting to Wi-Fi to do everything wireless. There is an App for that philosophy, being able to control devices wirelessly and through Bluetooth.
Wii – the ultimate goal was for all controllers, wheels, sticks, wands, surfboards, Wii Fit boards etc. to be wireless, to make it safer and be more adaptable to the games.
Xbox One and PS4 – they now come as standard to be wireless, wires are extra, wires are more expensive, wires get in the way.
Handhelds – with advances in battery technology they have been wireless for a while but now they have control wirelessly.
P4.4 – Task 4 – Using examples and terminology discuss and explain the technology around the Wireless and Wireless Devices and how it is used in the gaming world.

## Slide 13: P4.5 – Connection devices – Wired Controllers
Despite the wish for everything to be wireless, there are far more devices out there that make games more interesting, add-ons that make games special and controllers that rarely are considered in the mix like mice and keyboards.
Mice and keyboards – On a console these are novel, mostly pointless and haphazard but on a PC and Apple, Amiga, Atari, BBC micro and generation 3 of the consoles these were vital. For PC’s games like Starcraft and WOW would not be the same without mouse control and keyboards, users even adapt what they have to make them faster, argue over click speeds and key-press charts.
Joy Pads – The evolution of the Joy Pad has been slow, for a period of ten years it was two buttons and an Up Down Controller. Then for 8 years it was 3 buttons (Master Systems and Megadrive) or 4 (NES and SNES) plus two top buttons. Then it evolved to a three hand controller (N64) before settling back to what it is now. Touch pad never caught on, too many buttons was limiting, the thumb control was replaced back with an Up Down. It is currently ideal with the shape of the hand.
Paddles – these were the fashionable for 6 years back in the late 70’s when games could only go on two directions. Like flippers on a pinball machine the user controlled the direction of the object, not the character so much by the position of the hit.

## Slide 14: P4.5 – Connection devices – Wired Controllers
Extras – We all know of the add-ons, guitars for guitar games, surf boards, Wii Boards, Wheels for driving games, there has been a huge range of novelty devices added to enhance gameplay. They are still the same controller, up, down, left and right, or button pressing on a guitar so the technology is little different. The Wii was king of this with tennis rackets, golf clubs, microphones, swords etc. anything the controller could go into. They were the USP of a lot of games going back to the days of Duck Shoot. They work with motion control, sensors that measure the direction of the tilt within the pad.
Kinect – The next phase, improved with version 2 but still a novelty. The Human Interaction, working with dual cameras for 3D motion control, still requiring configuring and still not entirely accurate but a leap all the same. The camera control comes with a microphone allowing the user voice activation. This was tried before with PS Move and PS Go but the technology is getting better with each generation.
Occulus Rift – Hoping to be the next generation controller, VR with movement controls allowing the user a more direct input to the game. Still in the early stages and hoping to expand to new VR markets.
P4.5 – Task 5 – Using examples and terminology discuss and explain the technology around the d controllers and how they are used in the gaming world.
Mice and Keyboards | Joysticks and Paddles | Extras | Kinect and Rift

## Slide 15: P4.6 – Hardware Requirements – Graphics cards
Graphics card - Graphics cards handle all of the visual data within a computer, interpret it and display it via a VDU. With a PC Game in particular, the better the graphics card, the better and faster the game will play. Xbox and PS both have a very good Graphics Processor built in, the equivilent of a £150 PC card.
Components on a Graphics card include:
  GPU – Graphical Processing Unit is a dedicated microprocessor making calculations in order to display both 2D and 3D graphics.
  Motherboard interface – This is the method of connection and transfer of information between the motherboard. These include PCI, AGP and PCI express.
  Video BIOS - basic program that governs the video card's operations and provides the instructions that allow the computer and software to interface with the card.
  Video memory – if the card is integrated onto the mother board it may use the computers RAM, otherwise it will have a dedicated amount of memory for use for storing other data as well as the screen image such as object co-ordinates.
  Random Access Memory Digital-to-Analogue Converter – This coverts the digital signals produced by the computer processor into an analog signal which can be understood by the computer display
  Output connectors – this is how the graphics card connectors to the VDU. This can include DVI, HDMI and component.
  Cooling device – Video cards may use a lot of electricity, which is converted into heat. If the heat isn't dissipated, the video card could overheat and be damaged. Cooling devices are incorporated to transfer the heat elsewhere. Three common methods are heat sink, fan or water block.

## Slide 16: P4.6 – Hardware Requirements – Graphics cards
Intensive Game manipulation often rely on a powerful graphics processing unit (GPU), which accelerates the process of rendering complex objects in real time. GPU’s may be an integrated part of the computer's motherboard, the most common solution in laptops, or come packaged with a discrete graphics card with a supply of dedicated Video RAM, connected to the motherboard through either an AGP or PCI-Express port. It is also possible to use multiple GPUs in a single computer, using technologies such as NVidia's Scalable Link Interface and ATI's CrossFire but all this takes money, time and effort and not all rendering engines will take advantage of these, depending on the way the operating system is programmed.
Higher end graphics programs like 3D Studio Max, ZBrush and Maya will take fuller advantage of whatever the machine has going for it, especially the graphics cards. To create a 3D version of a character requires processing, especially if the image needs rotating within an environment.
With the new 3D version of Photoshop this is also the case, the image needs to handle an object in a 3D world, calculate the location, the perspective, the shadowing and lighting, to do this through the CPU is slower than to process this through a dedicated image handling system like a graphics card.

## Slide 17: P4.6 – Hardware Requirements – NIC Card
NIC Cards - Every PC and Apple computer on a network, both base machines and servers, requires a network interface card (or NIC) in order to access the network and without a network all PC games are stand alone. A NIC is usually a separate adapter card that slides into one of the computers motherboard expansion slots. However, most newer computers have the NIC built into the motherboard, so a separate card isn’t needed. And again, the faster the Card, the faster the game connection will be.
For client computers, you can usually get away with using the inexpensive built-in NIC because client computers are used only to connect one user to the network. However, the NIC in a server computer connects many network users to the server.
The network interface cards that you use must have a connector that matches the type of cable that you use. If you plan on wiring your network with thinnet cable, make sure that the network cards have a BNC connector. For twisted pair wiring, make sure that the cards have an RJ-45 connector.
A NIC is a Physical layer and Data Link layer device. Because a NIC establishes a network node, it must have a physical network address, also known as a MAC address. The MAC address is burned into the NIC at the factory, so you can’t change it. Every NIC ever manufactured has a unique MAC address.

## Slide 18: P4.6 – Hardware Requirements – Sound Card
Sound cards are also available to provide improved audio in PC computer games. These cards provide improved 3D audio and provide audio enhancement that is generally not available with integrated alternatives, at the cost of marginally lower overall performance. The Creative Labs SoundBlaster line was for many years the de facto standard for sound cards, although its popularity dwindled as PC audio became a commodity on modern motherboards. Newer developments in PC technology meant 8bit to 16 bit sound cards and now 32bit and sixty four bit technology is available.
Sound cards used to be separate from the motherboard but are now part of the on board system taking away some of the compatibility issues but the quality will not be as good as a separate card.
Basically they output the sound through a digital system, similar to the Xbox and PS but PC users have a choice of which card, how good it is, memory capacity, digital quality etc. With newer cards they tend to reach the peak games can manage and it is all down now to the speakers attached, 5.1, 7.1, or creative.
P4.6 – Task 6 – Using examples and terminology discuss and explain the PC hardware games requirements and how they are used in the gaming world.
Graphics Cards | NIC Cards | Sound Cards and Speakers

## Slide 19: P4.7 – Installing and configuring platforms and devices to enable gameplay - PC
Installing PC games has changed little over the years, put in Disk 1, run setup, wait, choose sound card, wait, put in Disk 2, choose graphics card, wait, put in disk 3, choose keyboard and mouse, wait, put in disk 4. Done. Run game, wait, configure keyboard, configure up, down, left, right, shoot, pause etc. Play game, die. Try again. Second time no more installing, game had an icon, double click and load game where we left off.
The only thing that is different is the Disk 1 change, now they are on CD, DVD, Blue Ray, downloaded off Steam. Configuring them is different in that we have more choice now, Internet play, server choice, leagues to join, Maps areas to choose, guns to take with us etc.
For this section you will need to write an introduction and then demonstrate Installing a PC game, setting the options, configuring the controller, screen resolution, sound and finally configuring the network play options. Evidence needs to be created and described with technical descriptions of how to set up and configure the connectors on the computer. Justification needs to be given of the choice of connectors and the choice of settings.
Show setting the sockets on the back of the PC for the mouse, monitor, keyboard and sound connectors and explain your choices.
Show installing a PC game of your choice (it should have some network play option)
Show changing the setting of your installed game, sound, screen, controller etc. and justify your choices.
Show in game configurations and justify your choices.
Show configuring the game for network play and justify your choice.
Show the game playing on-line and off-line.
P4.7 – Task 7 – Using examples and terminology demonstrate configuring a PC for a game setup, setting up a game and configuring the game for optimal settings.
M4.1 – Task 8 - Explain the different ways in which you could connect for multiplayer gaming for PC Games
D4.1 – Task 9 - Justify from the available PC connection types how each is appropriate for the different multiplayer gaming experiences in terms of costs, speed, number of users and user locations.

## Slide 20: P4.8 – Installing and configuring platforms and devices to enable gameplay - Console
Installing Console games has changed only twice over the years. First connect the Console, then switch telly on, choose the right channel. Switch Console on, Run game, wait, configure up, down, left, right, shoot, pause etc. Play game, die. Try again. Second time no more configuring, game had an option for the saved setting and load game where we left off.
The first thing that changed is the advent Hard Drive storage. Games can now install straight onto the Hard drive, stored games are there and loading is a matter of clicking on the game and the avatar and selecting play. Configuring them is still the same.
Second thing to change is that we have more choice now, Internet play, server choice, leagues to join, Maps areas to choose, guns to take with us etc. What would a game of COD be like without it.
For this task you will need to write an introduction and then demonstrate Installing a Console game, setting the options, configuring the controller, screen resolution, sound and finally configuring the network play options. Evidence needs to be created and described with technical descriptions of how to set up and configure the connectors on the console. Justification needs to be given of the choice of connectors and the choice of settings.
Show setting the sockets on the back of the Console for the output, power supply and sound connectors if possible and explain your choices.
Show installing a Console game of your choice (it should have some network play option)
Show changing the setting of your installed game, sound, screen, controller etc. and justify your choices.
Show in game configurations and justify your choices.
Show configuring the game for network play and justify your choice.
Show the game playing on-line and off-line.
P4.8 – Task 10 – Using examples and terminology demonstrate configuring a Console for a game setup, setting up a game and configuring the game for optimal settings.
M4.2 – Task 11 - Explain the different ways in which you could connect for multiplayer gaming for Console Games
D4.2 – Task 12 - Justify from the available Console connection types how each is appropriate for the different multiplayer gaming experiences in terms of costs, speed, number of users and user locations.

## Slide 21: P4.9 – Installing and configuring platforms and devices to enable gameplay - Mobiles
Installing a Mobile Phone or Tablet game has changed only once over the years. First switch on the Mobile, then click the setting and choose the game section, Run game, wait, configure up, down, left, right, shoot, pause etc. Play game, die. Try again. Second time no more configuring, game had an option for the saved setting and load game where we left off.
The thing that changed is the advent downloading games from stores. Games on Mobiles can now install straight onto the Internal drive, stored games are there and loading is a matter of clicking on the game and selecting play. Configuring them is still the same.
For this task you will need to write an introduction and then demonstrate Installing a Mobile Game, setting the options, configuring the controller, sound and finally configuring the network play options. Evidence needs to be created and described with technical descriptions of how to download, pay for and configure game settings. Justification needs to be given of the choice of store and the choice of settings.
Show choosing the online store to download the game from and logging in to your account to pay for it.
Show installing a Mobile game of your choice (it should have some network play option)
Show changing the setting of your installed game, sound, screen, controller etc. and justify your choices.
Show in game configurations and justify your choices.
Show configuring the game for network play and justify your choice.
Show the game playing on-line and off-line.
P4.9 – Task 13 – Using examples and terminology demonstrate configuring a Mobile Phone or Tablet for a game setup, setting up a game and configuring the game for optimal settings.
M4.3 – Task 14 - Explain the different ways in which you could connect for multiplayer gaming for Mobile Games.
D4.3 – Task 15 - Justify from the available Mobile connection types how each is appropriate for the different multiplayer gaming experiences in terms of costs, speed, number of users and user locations.

## Slide 22: P4.10 – Installing and configuring platforms and devices to enable gameplay - Handheld
Installing a Handheld game has changed only once over the years. First put the cartridge into the Handheld device. Then switch on the Handheld, game boots up, then click the setting and choose the configuration, wait, configure up, down, left, right, shoot, pause etc. or load where you left off, then Run game. Play game, die. Try again. Second time no more configuring, game had an option for the saved setting and load game where we left off.
The thing that changed is the advent downloading games from stores onto Handhelds. Games on Handhelds can now install straight onto the Memory Stick, MMC, stored games are there and loading is a matter of clicking on the game from the multiple menu system and selecting play. Configuring them is still the same.
For this task you will need to write an introduction and then demonstrate Installing a Handheld Game, setting the options, configuring the controller, sound and finally configuring the network play options. Evidence needs to be created and described with technical descriptions of how to download, pay for and configure game settings. Justification needs to be given of the choice of store and the choice of settings.
Show choosing the online store to download the game from and logging in to your account to pay for it.
Show running or installing a Handheld game of your choice (it should have some network play option)
Show changing the setting of your installed game, sound, screen, controller etc. and justify your choices.
Show in game configurations and justify your choices.
Show configuring the game for network play and justify your choice.
Show the game playing on-line and off-line.
P4.10 – Task 16 – Using examples and terminology demonstrate configuring a Handheld for a game setup, setting up a game and configuring the game for optimal settings.
M4.4 – Task 17 - Explain the different ways in which you could connect for multiplayer gaming for Handheld Games
D4.4 – Task 18 - Justify from the available Handheld connection types how each is appropriate for the different multiplayer gaming experiences in terms of costs, speed, number of users and user locations.

## Slide 23: Assessment Task List
P4.1 – Task 1 – Using examples and terminology discuss and explain the technology around the connector cables used to connect a console to a display.
P4.2 – Task 2 – Using examples and terminology discuss and explain the technology around the connector cables used to connect a console to a Console.
P4.3 – Task 3 – Using examples and terminology discuss and explain the technology around the LAN and WAN network connections and how it is used in the gaming world.
P4.4 – Task 4 – Using examples and terminology discuss and explain the technology around the Wireless and Wireless Devices and how it is used in the gaming world.
P4.5 – Task 5 – Using examples and terminology discuss and explain the technology around the d controllers and how they are used in the gaming world.
P4.6 – Task 6 – Using examples and terminology discuss and explain the PC hardware games requirements and how they are used in the gaming world.
P4.7 – Task 7 – Using examples and terminology demonstrate configuring a PC for a game setup, setting up a game and configuring the game for optimal settings.
M4.1 – Task 8 - Explain the different ways in which you could connect for multiplayer gaming for PC Games
D4.1 – Task 9 - Justify from the available PC connection types how each is appropriate for the different multiplayer gaming experiences in terms of costs, speed, number of users and user locations.

## Slide 24: Assessment Task List
P4.8 – Task 10 – Using examples and terminology demonstrate configuring a Console for a game setup, setting up a game and configuring the game for optimal settings.
M4.2 – Task 11 - Explain the different ways in which you could connect for multiplayer gaming for Console Games
D4.2 – Task 12 - Justify from the available Console connection types how each is appropriate for the different multiplayer gaming experiences in terms of costs, speed, number of users and user locations.
P4.9 – Task 13 – Using examples and terminology demonstrate configuring a Mobile Phone or Tablet for a game setup, setting up a game and configuring the game for optimal settings.
M4.3 – Task 14 - Explain the different ways in which you could connect for multiplayer gaming for Mobile Games.
D4.3 – Task 15 - Justify from the available Mobile connection types how each is appropriate for the different multiplayer gaming experiences in terms of costs, speed, number of users and user locations
P4.10 – Task 16 – Using examples and terminology demonstrate configuring a Handheld for a game setup, setting up a game and configuring the game for optimal settings.
M4.4 – Task 17 - Explain the different ways in which you could connect for multiplayer gaming for Handheld Games
D4.4 – Task 18 - Justify from the available Handheld connection types how each is appropriate for the different multiplayer gaming experiences in terms of costs, speed, number of users and user locations.