## Slide 1
03 - Storage devices and media
INFORMATION AND COMMUNICATION TECHNOLOGY– iGCSE
2016
0417

## Slide 2: Assessment At A Glance
Chapters
1
Components | Weighting
Paper 1 Theory 2 hours This written paper tests sections 1–21 of the syllabus content. All questions are compulsory, mostly multiple choice or short answer questions, but also some require longer answers. 100 marks External assessment | 40%
Paper 2 Document Production, Data Manipulation and Presentations 2 hours 30 minutes This test assesses the practical skills needed to use the applications covered in sections 17, 18 and 19 of the syllabus content. All tasks are compulsory. 80 marks External assessment | 30%
Paper 3 Data Analysis and Website Authoring 2 hours 30 minutes This test assesses the practical skills needed to use the applications covered in sections 20 and 21 of the syllabus content. All tasks are compulsory. 80 marks External assessment | 30%
2
3
4
5
6
7
8
9
10

## Slide 3: Assessment objectives
Assessment Objective | Paper 1 | Paper 2 | Weighting for qualification
AO1: Knowledge and understanding | 40% | 20% | 30%
AO2: Application | 30% | 30% | 30%
AO3: Analysis | 12% | 25% | 20%
AO4: Evaluation | 15% | 25% | 20%
Relationship between assessment objectives and components The approximate weightings allocated to each of the assessment objectives are summarised below.

## Slide 4: Grade Descriptors – A Grade
Grade descriptions are provided to give a general indication of the standards of achievement likely to have been shown by candidates awarded particular grades. The grade awarded will depend in practice upon the extent to which the candidate has met the assessment objectives overall and it might conceal weakness in one aspect of the examination which is balanced by above average performance in another.
A Grade - A candidate should demonstrate the following:
Knowledge and understanding
  an excellent ability to identify detailed facts, conventions and techniques in relation to the content of the syllabus
  an excellent ability to define the concepts and ideas of the syllabus.
Application
  a thorough ability to apply knowledge and understanding, using terms, concepts, theories and methods effectively to address business problems and issues
  a thorough ability to form conclusions from this information and to demonstrate these conclusions clearly and logically.
Analysis
  an excellent ability to classify and comment on information presented in various forms
  an excellent ability to distinguish between evidence and opinion.
Evaluation
  an excellent ability to make clear, reasoned judgments and communicate them in an accurate and logical manner.

## Slide 5: Grade Descriptors – C Grade
A Grade C candidate should demonstrate the following:
Knowledge and understanding
  a sound ability to identify detailed facts, conventions and techniques in relation to the content of the syllabus
  a sound ability to define the concepts and ideas of the syllabus.
Application
  a sound ability to apply knowledge and understanding, using terms, concepts, theories and methods appropriately to address problems and issues
  a sound ability to draw conclusions, and to present these in a clear manner.
Analysis
  a sound ability to use and comment on information presented in various forms
  a sound ability to distinguish between evidence and opinion.
Evaluation
  a sound ability to evaluate and make reasoned judgments.

## Slide 6: Grade Descriptors – F Grade
A Grade F candidate should demonstrate the following: Knowledge and understanding
  a limited ability to identify specific facts, conventions or techniques in relation to the content of the syllabus
  a limited familiarity with definitions of the central concepts and ideas of the syllabus.
Application
  a limited ability to apply knowledge and understanding, using terms, concepts, theories and methods appropriately to address problems and issues.
Analysis
  a limited ability to classify and present data in a simple way and a limited ability to select relevant information from a set of data
  a limited ability to distinguish between evidence and opinion.
Evaluation
  a limited ability to understand implications and make recommendations.

## Slide 7: 3 – Assessment Objectives
How large will the storage be in ten years time Just how much music do you need to listen to What new technologies will catch on What is Beta, Mini-Disc and Zip Drive Should I get a SSD hard drive for my system Is Cloud Storage the future or not
Outlines below are the objectives for this section of the Unit. They should be revised as part of the exam preparation.
In this chapter you will learn about:
Backing storage
Why back up data?
Types of access used by secondary storage devices
Types of internal and external secondary storage devices;
  Magnetic
  Optical
  Solid State
Page 44

## Slide 8: 3.1 – What is Backing up of Data?
How large will the storage be in ten years time Just how much music do you need to listen to What new technologies will catch on What is Beta, Mini-Disc and Zip Drive Should I get a SSD hard drive for my system Is Cloud Storage the future or not
This chapter covers many forms of secondary storage and compares the advantages and disadvantages of each type. In Chapter 1 you learnt about the primary memory, known as RAM and ROM. We will consider a number of storage devices later but first it is important to consider why we need to back up data using these devices and also how data is accessed.
Backing up refers to the copying of files/data to a different medium (disk, tape, flash drive etc.) is case of a problem with the main secondary storage device. Backing up files and data on a regular basis is seen as good computing practice and many computer systems can be set up to backup up files automatically on a regular basis. An example would be the use of magnetic tapes to back up internet servers regularly, or cloud storage companies using magnetic tape of hard disk drives to back up clients’ data on a regular basis.
The backups are often stored in a different place to the main storage. This is in case of fire or some other situation that could lead to irretrievable loss of key data/files.
Page 44

## Slide 9: 3.1 – Why Backup Data?
How large will the storage be in ten years time Just how much music do you need to listen to What new technologies will catch on What is Beta, Mini-Disc and Zip Drive Should I get a SSD hard drive for my system Is Cloud Storage the future or not
There are various reasons why backups are made. Some of the more common reasons are considered below:
To safeguard against loss of data due to the failure of the original secondary storage device; this could be due to hardware failure (e.g. head crash on a hard drive unit), problems caused by files being overwritten accidentally, (or otherwise), or possible corruption of files (i.e. caused by power surges).
To safeguard against damage caused by hackers. This may not be their intention (they may only want to gain access to the information for others purposes, e.g. to find personal information such as bank account details). However, the very act of hacking into files could cause problems such as corruption or data loss.
Backups are also made in case the files need to be used elsewhere; this protects the originals against the possible corruption or loss.
Backups don’t necessarily guard against the effect of a virus. The virus could attach itself to the files, which could mean that the backups are also affected. If the computer was ‘cleaned’ of the virus then the backup files are reloaded, there is a real risk that the virus could infect the computer system again. The best protection is not to get a virus in the first place.
Page 44

## Slide 10: 3.1 – Types of Access
How large will the storage be in ten years time Just how much music do you need to listen to What new technologies will catch on What is Beta, Mini-Disc and Zip Drive Should I get a SSD hard drive for my system Is Cloud Storage the future or not
A number of secondary storage devices are discussed in 3.3. The way data is stored and read by each of these devices is very different, however.
This section briefly describes the two main methods of accessing data. It is important to understand three new terms here:
Field
Record
File
Suppose we are storing data about 20 cars in a car showroom. Data about each car – such as its colour, engine size, type of fuel, number of doors and whether it’s new or used – are stored in an allocated space known as a field. All of the data about car 1, for example, is known as the record for that car. Putting all the data together for all 20 cars produces a file like this.
Figure 3.1: Data for 20 cars in a showroom
Page 45
Field 1 | Field 2 | Field 3 | Field 4 | Field 5 | Field 6 | 
Car 1 | Red | 1.5 litres | Petrol | 3 doors | New | Record 1
Car 2 | Blue | 1.3 litres | Petrol | 5 doors | New | Record 2
Car 3 | Green | 2.2 litres | Diesel | 5 doors | new | Record 3
 |  |  |  |  |  | …
Car 20 | White | 1.6 litres | Petrol | 2 doors | New | Record 20

## Slide 11: 3.1 – Serial access
When using serial access it is necessary to start at the beginning of the file and then access each record in turn until the required record is found. In Figure 3.1, to find the record for Car 15, it is necessary to first read all of the preceding steps (steps 1-14), until the required record is located.
It is primarily used on magnetic tape systems and is essentially a very slow for of data access. It is used in applications where speed of access, or where the order in which the data is accessed, isn’t important (i.e. utility billing, clearing bank checks or producing pay slips).
Page 45
When the original magnetic tape (called the master file) needs updating, an additional take (called a transaction file) is required. The transaction file contains all the new data to allow the master file to be updated (although the transaction file is very often another tape, the new data could in fact be stored on a different medium). The updated tape is referred to as the new master file. When using tapes, it is essential that the records on both master file and transaction file are sorted in the same order (i.e. sorted by customer number if it is a billing application – the field used to sort the record is often referred to as a key field).
This is an example of how a master file (MF) can be updated using a Transaction File (TF), The scenario here is a book show that sells books.
Old data stored on magnetic tape
New data to be used to update master file
New tape produced from A and B
(Old) master file
Figure 3.2: Updating a magnetic tape
A
B

## Slide 12: 3.1 – Serial access
All of the books held in stock are stored in the MF in ISBN order – the ISBN acts as the key field for each record (each different book title will have its own record made up of the ISBN, title of book, author, genre, cost price and selling price). All the changes during the day will be stored on the TF – if a books sells, if new books come in, if a book is out of print, and so on. At the end of each day, the MF is updated using the new data stored on the TF. The basic steps in the update process are shown below:
At the end of the day, the TF is sorted in the same order as the MF (this will be done using the ISBN which is known here as the key field)
A new master file (NMF) is created to store the updated records of the books in the shop
The first record in the TF is then read and the first record in the MF is also read
  The two records are compared with each other
  If the key field on the MF < the key field on the TF, then no transactions took place and the MF record is written to the NMF; a new MF record is now read
  If the key field on the MF = the key field on the TF, then a transaction took place and the new record from the TF is written to the NMF; the next record from both the TF and MF are now read
  If the transaction file indicates a deletion then the record is simply not written to the NMF and a new record from each file is read
  If the key field on the MF > the key field on the TF, then the record doesn’t yet exist and a new record is created on the NMF; a new TF record is now read
The process is repeated until the end of the MF
Finally, any remaining records on the TF are written to the NMF.
Page 45

## Slide 13: 3.1 – Serial access - Example
Page 46
The Master File (MF) contains the following records with key fields shown: |  |  |  |  |  |  |  |  | 
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 
The Transaction File (TF) contains the following records with key fields shown: |  |  |  |  |  |  |  |  | 
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
The first record from each file is read. The key fields both match, so the record with key field 1 is written from the TF to the new master file (NMF): |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
The second record is then read from the TF and MF; again the keys are equal so the record on the TF with key field 2 is now written to the NMF: |  |  |  |  |  |  |  |  | 
1 | 2 |  |  |  |  |  |  |  | 
The third record is then read from the MF and TF; this time the key fields are different (3 and 4). The MF key < the TF key, so the MF record with key 3 is now written to the NMF. |  |  |  |  |  |  |  |  | 
1 | 2 | 3 |  |  |  |  |  |  | 
1 | 2 | 3 | 4 |  |  |  |  |  | 
1 | 2 | 3 | 4 | 5 |  |  |  |  | 
1 | 2 | 3 | 4 | 5 | 6 |  |  |  | 
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10

## Slide 14: 3.1 – Direct Access
Page 47
Exercise 3a
Continue the above exercise for the remainder of records to see if you arrive at the above NMF.
What would happen if two of the records on the TF (with key fields of 4 and 8) needed deletion to be carried out? What would be the final NMF?
Direct access is used with magnetic disks, optical media and solid state media. The computer uses the key field to calculate where data should be stored. It is then able to access the data directly from the calculated position. Consequently, access is much faster than with serial access.
When updating files using direct access, the old records/data are simply written over by the new records/data. It is not necessary to sort records into any specific order first.
It is used in applications where data access speed is vital (for example, in re:tltime operations such as controlling a chemical plant or online systems such as booking air tickets or automatic stock control).

## Slide 15: 3.2 – Secondary Storage Media
Page 47
Dating right back to the advent of the personal computer, all systems have come equipped with some form of secondary storage. When a user loads data into a computer, the information is stored temporarily in the RAM - if the computer was turned off, this data would be lost.
Secondary storage devices ensure that data is stored permanently so that it can be used again at a later date. This section will consider the various types of secondary storage and the media used.
Throughout the chapter, you will notice that the term byte is used to measure the size of memory or storage. Typically, storage sizes or file sizes are measured in kilobytes (kB), megabytes (MB), gigabytes (GB) and terabytes (TB) as shown next.
How large will the storage be in ten years time Just how much music do you need to listen to What new technologies will catch on What is Beta, Mini-Disc and Zip Drive Should I get a SSD hard drive for my system Is Cloud Storage the future or not

## Slide 16: 3.2 – Secondary Storage Media
Page 47
1 KB= 1024 (2 10) bytes, 1 MB = 1 048576 (220) bytes, 1 GB = 1073741824 (230) bytes and 1 TB= 1099511627 776 (2 40) bytes. These values are all powers of 2.
This section reviews the various types of secondary storage devices available. These are either internal or external ( that is, plug-in devices) to the computer.
Devices full into the three different types of storage media:
• magnetic
• optical
• solid state.
How large will the storage be in ten years time Just how much music do you need to listen to What new technologies will catch on What is Beta, Mini-Disc and Zip Drive Should I get a SSD hard drive for my system Is Cloud Storage the future or not
Storage Size | Number of Bytes | Number of Bytes as power of 10
1 KB | 1000 bytes | 103 bytes
1 MB | 1000 000 bytes | 106 bytes
1 GB | 1000 000 000 bytes | 109 bytes
1 TB | 1000 000 000 000 bytes | 1012 bytes

## Slide 17: 3.2 – Magnetic Storage Media
Page 47
Magnetic storage media depend on the magnetic properties of certain materials (iron and nickel alloys being the most common). Magnetic material is coated on the surface of a disk or tape that can be magnetised in such a way as to represent a 1 or a 0.
Many hard disk drives are made up of more than one disk and these disks are known as platters. Each platter is made from glass, ceramic or aluminium coated in a nickel alloy that can be magnetised. In the case of tape, plastic that is coated in a magnetic material is used to store the data.
How large will the storage be in ten years time Just how much music do you need to listen to What new technologies will catch on What is Beta, Mini-Disc and Zip Drive Should I get a SSD hard drive for my system Is Cloud Storage the future or not

## Slide 18: 3.2 – Magnetic Storage Media
Page 48
Fixed/internal hard disk drive (HDD)
Fixed hard disk drives are available on all computers and are the main method used for data storage. On a PC this is usually a fixed hard disk with read/write heads allowing data to be written to or read from the disk surface.
The disk surface is coated in a magnetic film that allows data to be stored by altering the magnetic properties to represent binary 1’s or 0’s (the fundamental units of computer memories).
The hard disks usually store the disk operating system (DOS) and other systems software, as well as applications software and files. Applications software (such as spreadsheets and word processors) also needs a hard drive to allow them to quickly retrieve and save data.

## Slide 19: 3.2 – Magnetic Storage Media
Page 48
Uses
To store the operating system, systems software and working data/files.
Storing applications software that needs fast retrieval and storage of data.
Used in real-time systems (e.g., robots, control of a chemical plant where data for the process is stored to allow real-time operations) and in online systems (for example, booking airline tickets or automatic stock control using EFTPOS, which allows immediate updating of the stock files).
Used in file servers for computer networks.
Advantages
They have a very fast data transfer rate and fast access times to data.
They have very large memory capacities.
Disadvantages
Can be easily damaged if the correct shut down procedure is not carried out; this can lead to a head crash which would result in a loss of data.
They have many moving parts when compared to, for example solid state drives (SSDs).
Their read/write operation can be quite noisy compared to SSDs.

## Slide 20: 3.2 – Magnetic Storage Media
Page 48
Portable hard disk drives
These devices work in much the same way as fixed hard disk drives but are usually connected to the computer via the USB (universal serial bus) port and can be disconnected and used on different computers. The disks are generally capable of storing more data than the equivalent optical disk (CD, DVD and so on).
Uses
They can be used as backup systems to prevent loss of data.
They can be used to transfer data/files/software between computers.
Advantages
The data access time and data transfer rate is very fast.
They have a large memory capacity.
They can be used as a method of transferring information between computers.
Disadvantages
They can be easily damaged if dropped or subjected to a strong magnetic field;
As with fixed hard disk drives, an incorrect shut-down procedure could also lead to loss of data.

## Slide 21: 3.2 – Magnetic Storage Media
Page 49
Magnetic Tapes
A magnetic tape is a very thin strip of plastic that has been coated in a magnetic layer. They are read and written to by a read/write head. The data is stored in magnetic areas that represent 1’s and 0’s.
Data is read from the tape using serial access (see earlier description). This type of storage is useless in a real-time or online applications ( due to the very slow data access speeds) and is best suited to offline or batch processing.
Uses
In applications where batch processing is used, for example, clearing bank cheques, utility billing (gas, electricity, water) and producing pay slips; in these applications there is no need for any specific processing order and speed of data access is not essential. to be stored.
Used in long-term archiving of data; magnetic tapes have huge data storage capacities and are known to be very stable, which makes them ideal for long term storage.

## Slide 22: 3.2 – Magnetic Storage Media
Page 49
Advantages
They are generally less expensive (per byte) than the equivalent bard disk.
It is a very robust technology (they don't deteriorate very much over time).
They have a huge data storage capacity.
The data transfer rate is actually fast (this should not be confused with data access time, which is very slow for magnetic tapes).
Disadvantages
Very slow data access times (need to read all the earlier records on the tape until the required record is found - see slide 13).
When updating, another tape is needed (see description slide 13) to store the final updated version.
They are affected by magnetic fields; a strong magnet can corrupt data stored on the tape.

## Slide 23: 3.3 – Optical Storage Media
Page 50
CD/DVD disks
CDs and DVDS are described as optical storage devices. Laser light is used to read data and to write data on the surface of the disk. Both CDs and DVDs use a thin layer of metal alloy or light-sensitive organic dye to store the data.
As can be seen from the diagram, they use a single spiral track that runs from the centre of the disk to the edge.
The data is stored in 'pits' and 'bumps' on the spiral track. A red Laser is used to read and write the data. CDs and DVDs can be designated as follows:
R - write once only
ROM- can only be read
RW - can be written to or read from many times.
DVD technology is slightly different to that used in CDs. One of the main differences is me use of dual-layering, which considerably increases the storage capacity. Basically, this means that there are two individual recording layers.

## Slide 24: 3.3 – Optical Storage Media
Page 50
CD/DVD disks
The two layers of a standard DVD are joined together with a transparent (polycarbonate) spacer; a very thin reflector is also sandwiched between the two layers. Reading and writing of the second layer is done by a red laser focusing at a fraction of a millimeter difference. compared to tile first layer laser reads layer 1
Standard, single-layer DVDs have a larger storage capacity than CDs because the 'pit' size and track width are both smaller. This means that more data can be stored on the DVD surface. DVDs use lasers with a wavelength of 650 nanometers; CDs use lasers with a wavelength of 780 nanometers. The shorter the wavelength of the laser light, the greater the storage capacity of the medium.
Figure 3.3 Dual-layering in a DVD

## Slide 25: 3.3 – Optical Storage Media
Page 50
CD-ROM and DVD-ROM
These optical disks are read-only memory (ROM), which means they cannot be written over and can only be read. The data is stored as a series of pits ( equivalent to a binary value of 1 and lands ( equivalent to the binary value of 0) in the metallic optical layer.
The 'pits' are formed by a laser beam etching the surface at the manufacturing stage. Only a single track exists which spirals out from the centre of the disk.
The 'pits' and 'lands' are read by a low-powered laser beam that follows the data stream and reads from the centre outwards in a spiral. The light reflects differently off a 'pit' than it does off a 'land' and this is interpreted as 1’s and 0’s (that is data) - hence the term digital media.
Click Here

## Slide 26: 3.3 – Optical Storage Media
Page 50
Uses
CD-ROMs are used to store music files, software, computer games and reference software (such as an encyclopedia).
DVD-ROMs have much larger storage and are used to store films, computer data and ever-more sophisticated computer/arcade games.
CD-ROM’s and DVD-ROM’s are used in applications where there is a real need to prevent tl1e deletion or overwriting of important data.
Advantages
They hold far more data than floppy disks (one CD = 800 floppy disks).
They are less expensive than hard disk. drive systems.
Disadvantages
The data transfer rate/data access time is slower than for hard disks.
Click Here

## Slide 27: 3.3 – Optical Storage Media
Page 51
CD-R and DVD-R
The letter R here means the disk is recordable once only; it becomes a CD-ROM or DVD-ROM once it has been finalised (this means that the CD/DVD cannot have any additional data written to it). This is the last step in the CD/DVD process; finalising or 'closing' of a CD-R, in which Table of Contents (TOC) data are written on the disc to enable the computer to read the CD/DVD.
A thin layer of an organic dye (DVDs also use an additional silver alloy or gold reflector) is used as the recording media. A laser beam produces heated spots and unheated spots. On reading the disk, a laser beam is capable of distinguishing between the two types of spots and effectively reads the data stream from the centre outwards in a spiral action. This data is then interpreted as 1’s and 0’s.

## Slide 28: 3.3 – Optical Storage Media
Page 51
Uses
Home recordings of music (CD-R) and films (DVD-R).
Used to store data to be kept for later use or to be transferred to another computer.
Advantages
Cheaper than RW disks.
Once burned (and finalised) they are like a ROM.
Disadvantages
If finalised, the CD-R/DVD-R can only be recorded on once; if an error in the data has occurred then the disk has to be discarded. since it can no longer be written to.
Not all CD/DVD players can read CD-R/DVD-R.

## Slide 29: 3.3 – Optical Storage Media
Page 51
CD-RW and DVD-RW
The RW means these disks are a rewritable media and can be written over several times. Unlike CD-R/DVD-R, they don't become ROMs. The recording layer uses a special phase-changing metal alloy (often GeSbTe [Germanium-AntimonyTerbium alloy]; a number of different methods are used to produce these alloys).
The alloy can switch between crystalline phase and amorphous phase (noncrystalline), thus changing its reflectivity to light depending on the laser beam power. Spots are produced that can be read by a laser and then interpreted as 1’s and 0’s. The system allows data to be written, erased and rewritten many times.

## Slide 30: 3.3 – Optical Storage Media
Page 52
Uses
Used to record television programs (like a video recorder), which can be recorded over time and time again.
Not as wasteful as R format as more data can be added to at a later stage (with CD-R/DVD-R it is only possible to do a write operation once if you have already finalised the disc).
Used in CCTV systems.
Advantages
Can be written over many times.
Can use different file formats each time it is used.
Disadvantages
Can be relatively expensive.
It is possible to accidentally overwrite data.

## Slide 31: 3.3 – Optical Storage Media
Page 52
DVD-RAM
DVD-RAM uses a very different technology to CDs and DVDs. They have the following features:
instead of a single, spiral track, they use a number of concentric tracks
the use of concentric tracks allows simultaneous read and write operations to take place
they allow numerous read and write operations (up to 100000 times) and have great longevity (over 30 years), which makes them ideal for archiving
DVD-RAMs can be written to and read from many times.
The recording layer is made from a similar phase-changing material as used in RW technology. When writing, a laser heats the phase-changing alloy on the disk to about 500 °C to 700 °C changing the reflective properties from shiny to dull (i.e. pits).
If the disk needs to be erased, a laser heats the surface to :about 200 °C to return the disk to its original shiny state. A low-power laser is used to read the written marks on the surface. The shiny and dull marks ('pits') represent data to a computer where they are interpreted.
Click Here

## Slide 32: 3.3 – Optical Storage Media
Page 52
Uses
In recording devices such as satellite receivers to allow simultaneous recording and playback.
Used in camcorders to store movies.
Advantages
They have a long life (estimated 30 years minimum life).
It is possible to do a rewrite operation over 100,000 times (compare this to the RW format, which only allows about 1000 rewrites).
Writing on DVD-RAMs is very reliable - they have in-built verification software, so the accuracy of the data is ensured.
Very fast access if the files are fairly small.
No need to finalise the disk.
Very large capacity (about 10 GB if double-sided format I is used).
They offer the ability to read data at the same time as data is being written
Disadvantages
Not as compatible as R or RW format; many systems won't recognise the DVD-RAM format.
Relatively expensive (about four times the cost of a DVD-RW disk).
They have been superseded by newer technologies such as solid state memories.
Click Here

## Slide 33: 3.3 – Optical Storage Media
Page 53

## Slide 34: 3.3 – Optical Storage Media
Page 53
Blu-ray discs
Blu-ray discs are another example of optical storage media. However, they are fundamentally different to DVDs in their construction and in the way they carry out read-write operations.
The main differences are:
a blue laser, rather than a red laser, is used to carry out read and write operations; the wavelength of blue light is only 405 nanometers (compared to 650 nanometers for red light)
using blue laser light means that the 'pits' and 'bumps' can be much smaller; consequently, Blu-ray can store up to five times more data than a normal DVD.
Blu-ray uses a single 1.1 mm-thick polycarbonate disk; normal DVDs use a sandwich of two 0.6mm tl1ick disks
using two sandwiched layers can cause birefringence (light is refracted into two separate beams causing reading errors); because Blu-ray uses only one layer, the disks don't suffer from birefringence
Blu-ray discs automatically come with a secure encryption system, which helps to prevent piracy and copyright infringement.

## Slide 35: 3.3 – Optical Storage Media
Page 53
Uses
Home gaming consoles.
Storing and playing back movies (one high-definition movie of two hours duration uses up 25 GB of memory).
PCs can use this technology for data storage or backing up hard drives.
Advantages
Very large storage capacity, therefore ideal for storing high-definition movies.
Very fast data transfer rate.
The data access speed is also greater than with other optical media.
Blu-ray discs automatically come with a secure encryption system, which helps to prevent piracy and copyright infringement.
Disadvantages
Relatively expensive.
Encryption problems (which are used to stop piracy) when used to store video.
There are fewer movie titles on Blu-ray format, which is reducing its impact on the home movie market.

## Slide 36: 3.3 – Optical Storage Media
Page 54
All these optical storage media are used as backup systems (for photos, music and multimedia files). This also means that CDs and DVDs can be used to transfer files between computers. Manufacturers often supply their software using CDs and DVDs. When the software is supplied in this way, the disk is usually in a read only format.
The most common use of DVD and Blu-ray is the supply of movies or games. The memory capacity of CDs isn't big enough to store most movies.

## Slide 37: 3.3 – Optical Storage Media
Page 54
The future of optical media
In recent times both the CD and DVD are showing signs of becoming obsolete. Many computer systems now come with USB connectors only and no DVD or CD drive. The main method of transferring files between devices has become flash memory. Many people now store all tl1eir music in the following ways:
on hard disk drive systems (set up as sound systems, as shown in the photo)
in MP3 format on:
  a computer/tablet
  their mobile/smartphone
  a portable music player (such as an iPod)
using the 'cloud' to store all their files so they can access tl1eir music from anywhere in the world
by 'streaming' their music from the internet; provided the user has an internet connection they can access music through a laptop computer, mobile phone, tablet or any other receiving device.

## Slide 38: 3.3 – Optical Storage Media
Page 54
The future of optical media
It is a similar story for movies, where strean1ing is becoming increasingly common. Many television sets are now set up as 'smart' televisions - this means it is now possible to simply stream movies or television programs on demand without the need for any DVD or Blu-ray players. In effect, the television set has become the central computer with a link to the internet using wireless connection.
Floppy disks met the same fate in the early twenty-first century. How often do you see floppy disks? It is very likely that CDs and DVDs will meet the same fate and be replaced by one of the systems described above or something entirely new.
Click Here
Click Here

## Slide 39: 3.3 – Optical Storage Media
Page 54
Exercise 3b
Using this student book and the internet, do some research to find out all the different ways to store music files and movie files.
Draw a table similar to the one shown below to list all the advantages and disadvantages of each of the methods you have identified.
Storage Method | Advantage | Disadvantage

## Slide 40: 3.4 – Solid State Storage Media
What would you upgrade on your computer at home to make it better. Why do we still have unreliable Hard Drives in computers What is the difference between SSD and HDD Are they Mac compatible Can they get any faster What is the next big thing when these become old.
Solid State Drives (SSD) are rapidly taking over from HDDs/ They have no moving parts and all data is retrieved at the same rate no matter where it is stored. They don’t rely on magnetic properties; the most common type of solid state storage devices store data by controlling the movement of electronics within NAND* chips.
The data is stored as O’s and 1‘s in millions of tiny transistors within the chip, This effectively produces non-volatile rewriteable memory.
Technical part (do not need to know this)
NAND flash memory is a type of non-volatile storage that does not require power to retail data. NAND flash memory stores data in an array of memory cells made from floating-gate transistors which are insulated from each other by an oxide layer. NAND is a type of logic gate and is basically one of the building blocks of many electronic circuits including solid state devices.
Page 55

## Slide 41: 3.4 – Solid State Storage Media
What would you upgrade on your computer at home to make it better. Why do we still have unreliable Hard Drives in computers What is the difference between SSD and HDD Are they Mac compatible Can they get any faster What is the next big thing when these become old.
However, a number of solid state storage devices sometimes use electronically erasable programmable read-only memories (EEPROM) technology. The main difference is that it uses NOR* chips rather than NAND. This makes them faster in operation; however, devices using EEPROM are considerably more expensive than those that use NAND technology. EEPROM also allows data to be erased in single bytes at a time. Use of NAND only allows blocks of data to be read or erased. This makes EEPROM technology more useful in certain applications where data needs to be accessed or erased in byte-sized chunks.
Technical part (do not need to know this)
NOR flash memory is also a type of non-volatile storage; a NOR ate is a type of logic gate that makes up many electronic circuits, NOR gates work in a different way to NAND gates. Essentially, solid state memories made from NOR gates allow faster read/write operations than those made from NAND gates, but the storage devices cost more to manufacture – consequently, most solid state storage devices use NAND gate technology.
Page 55

## Slide 42: 3.4 – Solid State Storage Media
Because of the cost implications, the majority of solid state storage devices use NAND technology. The two are usually distinguished by the terms flash (uses NAND) and EEPROM (uses NOR).
So what are the main advantages of using SSD rather than HDD? The main advantages are summarized below:
They are more reliable (no moving parts to go wrong)
They are considerably lighter (which makes they suitable for laptops)
They do not have to ‘get up to speed’ before they work properly
They have lower power consumption
They run much cooler than HDDs (laptop suitable)
Because there are no moving parts, they are thin
Data access us considerably faster than HDD
The main drawback of SSD is the questionable longevity of the technology. Most SSD are conservatively rated at only 20GB write operations per day over a 3 year period – this is known as SSD endurance. For this reason, SSD is not used in Internet Servers, for example, where a huge number of write operations take place every day. However, this issue is being addressed by a number of manufacturers to improve the durability of these SSD systems.
Page 55

## Slide 43: 3.4 – Memory Stick – Pen Drives
Memory sticks/pen drives can store several gigabytes of data and use the solid state technology described above. They are usually connected to a computer through the USB port and power to operate them is drawn from the host computer.
They are extremely small and very portable. Most operating systems recognise these storage media, which means no additional software is needed to operate them.
Some expensive software now uses these storage methods (sometimes referred to as portable flash drives) as a form of security. They plug into the computer using the USB port and are known as dongles. The software installed on a computer sends out a request (in encrypted form) to the dongle asking for an encrypted validation key. Thus a person trying to carry out software piracy would have to break the code on the dongle first before they could use the software.
Some systems go one stage further and have key bits of software stored on the dongle in encrypted form. The software looks for these pieces of encrypted code to enable it to run. This gives an added security benefit to the software.
Page 55

## Slide 44: 3.4 – Memory Stick – Pen Drives
Uses
Transporting files between computers or used as a backup store.
Used as a security device to prevent software piracy (known as a dongle ).
Advantages
Very robust and compact and portable media.
Doesn't need additional software to work on most computers.
They are not affected by magnetic fields.
Disadvantages
Can't write-protect the data/files.
Easy to lose (due to their small physical size).
The user needs to be very careful when removing a memory stick from a computer - incorrect removal (for example, while it is still doing a read/write operation) will corrupt the data on the memory stick, rendering it useless.
Page 55

## Slide 45: 3.4 – Flash Memory Cards
Flash memory cards
These are a form of electrically erasable programmable read-only memory (EEPROM) and are examples of solid state memories.
Uses
Storing photos on digital cameras.
Used as mobile phone memory cards.
Used in MP3 players to store music files.
Used as a backup store in hand-held computer devices.
Advantages
Very compact and can be easily removed and used in another device or for transferring photos directly to a computer or printer.
Since they are solid state memories, they are very robust.
Disadvantages
Expensive per gigabyte of memory when compared to hard drive disks.
Have a finite life regarding the number of times they can be read from or written to.
Have a lower storage capacity than hard disks.
Page 55

## Slide 46: 3 – Glossary
What is SMART What is the difference between and Aim and an Objective Why would Objectives change when a company merges What happens when Objectives are not met How are objectives of a charity different from a private business.
Solid State Drive – Hard drive with no moving parts, expensive but 100% reliable as nothing but a circuit board to break down.
Page 54

## Slide 47: Exam Questions – Unit 03
?
May - 2015
(c) Name two storage devices shown in the diagram above.
1...............................................................................................................................
2.......................................................................................................................... [2]

## Slide 48: Exam Questions – Unit 03
?
November - 2009
2 Ring two items which are storage devices.
Bar code reader Keyboard Laser printer
Memory stick Mouse Zip disc drive [2]
Tick True or False for the following statements about RAM and ROM.
 | True | False
RAM is not volatile. |  | 
ROM is used to store the BIOS of a computer. |  | 
The data in ROM is easier to change than that in RAM. |  | 
RAM is used to store the data the user is currently working on. |  | 

## Slide 49: Exam Questions – Unit 03
?
November – 2010 – Paper 11
11 All computers come with main memory as well as backing storage. Give a reason why the following are needed.
RAM ____________________________________________ ________________________________________________________________________________________________
ROM ___________________________________________ ________________________________________________________________________________________________
Backing storage ___________________________________
_____________________________________________________________________________________________ [3]

## Slide 50: Exam Questions – Unit 03
?
November – 2010 – Paper 12
11 Most PCs come with a hard disc drive. Give a reason why each of the following are also used with PCs.
Magnetic tape ____________________________________ ________________________________________________________________________________________________
CD R ___________________________________________ ________________________________________________________________________________________________
DVD ROM _______________________________________ _____________________________________________________________________________________________ [3]

## Slide 51: Exam Questions – Unit 03
?
November – 2010 – Paper 13
11 Explain why the following are used with PCs.
Pen drives ______________________________________ ________________________________________________________________________________________________
Blu-ray _________________________________________ ________________________________________________________________________________________________
Fixed hard disc drives _____________________________
______________________________________________________________________________________________ [3]