## Slide 1
4 – Networks and the Effects of Using Them
INFORMATION AND COMMUNICATION TECHNOLOGY– iGCSE
2016
0417

## Slide 2: Assessment At A Glance
Chapters
1
Components | Weighting
Paper 1 Theory 2 hours This written paper tests sections 1–21 of the syllabus content. All questions are compulsory, mostly multiple choice or short answer questions, but also some require longer answers. 100 marks External assessment | 40%
Paper 2 Document Production, Data Manipulation and Presentations 2 hours 30 minutes This test assesses the practical skills needed to use the applications covered in sections 17, 18 and 19 of the syllabus content. All tasks are compulsory. 80 marks External assessment | 30%
Paper 3 Data Analysis and Website Authoring 2 hours 30 minutes This test assesses the practical skills needed to use the applications covered in sections 20 and 21 of the syllabus content. All tasks are compulsory. 80 marks External assessment | 30%
2
3
4
5
6
7
8
9
10

## Slide 3: Assessment objectives
QO3
Checklist
QO2
Assignment
QO1
Relationship between assessment objectives and components The approximate weightings allocated to each of the assessment objectives are summarised below.
QO4
Q05
QO6
Assessment Objective | Paper 1 | Paper 2 | Weighting for qualification
AO1: Knowledge and understanding | 40% | 20% | 30%
AO2: Application | 30% | 30% | 30%
AO3: Analysis | 12% | 25% | 20%
AO4: Evaluation | 15% | 25% | 20%

## Slide 4: Grade Descriptors – A Grade
QO3
Checklist
QO2
Assignment
QO1
Grade descriptions are provided to give a general indication of the standards of achievement likely to have been shown by candidates awarded particular grades. The grade awarded will depend in practice upon the extent to which the candidate has met the assessment objectives overall and it might conceal weakness in one aspect of the examination which is balanced by above average performance in another.
A Grade - A candidate should demonstrate the following:
Knowledge and understanding
  an excellent ability to identify detailed facts, conventions and techniques in relation to the content of the syllabus
  an excellent ability to define the concepts and ideas of the syllabus.
Application
  a thorough ability to apply knowledge and understanding, using terms, concepts, theories and methods effectively to address business problems and issues
  a thorough ability to form conclusions from this information and to demonstrate these conclusions clearly and logically.
Analysis
  an excellent ability to classify and comment on information presented in various forms
  an excellent ability to distinguish between evidence and opinion.
Evaluation
  an excellent ability to make clear, reasoned judgements and communicate them in an accurate and logical manner.
QO4
Q05
QO6

## Slide 5: Grade Descriptors – C Grade
QO3
Checklist
QO2
Assignment
QO1
A Grade C candidate should demonstrate the following:
Knowledge and understanding
  a sound ability to identify detailed facts, conventions and techniques in relation to the content of the syllabus
  a sound ability to define the concepts and ideas of the syllabus.
Application
  a sound ability to apply knowledge and understanding, using terms, concepts, theories and methods appropriately to address problems and issues
  a sound ability to draw conclusions, and to present these in a clear manner.
Analysis
  a sound ability to use and comment on information presented in various forms
  a sound ability to distinguish between evidence and opinion.
Evaluation
  a sound ability to evaluate and make reasoned judgements.
QO4
Q05
QO6

## Slide 6: Grade Descriptors – F Grade
QO3
Checklist
QO2
Assignment
QO1
A Grade F candidate should demonstrate the following: Knowledge and understanding
  a limited ability to identify specific facts, conventions or techniques in relation to the content of the syllabus
  a limited familiarity with definitions of the central concepts and ideas of the syllabus.
Application
  a limited ability to apply knowledge and understanding, using terms, concepts, theories and methods appropriately to address problems and issues.
Analysis
  a limited ability to classify and present data in a simple way and a limited ability to select relevant information from a set of data
  a limited ability to distinguish between evidence and opinion.
Evaluation
  a limited ability to understand implications and make recommendations.
QO4
Q05
QO6

## Slide 7: 4 – Assessment Objectives
What a network manager does How do all the wires connect together When I play games in school, how do they talk to each other Why is wireless slower What is a Proxy, VPN, Tunnel. In hacking films, what does the terminology mean Should I set up a home network
Outlines below are the objectives for this section of the Unit. They should be revised as part of the exam preparation.
In this chapter you will learn about:
Networks
Network devices such as routers, hubs and switches
IP and MAC addresses
Wi-Fi and Bluetooth
How to set up and configure a small network
Intranets and Extranets
LAN, WAN and WLAN
Network security (e.g. policing)
Accessing the internet
Authentication
Viruses
Data Protection Acts
Faxes and Emails
Video, audio and web conferencing.
Page 58

## Slide 8: 4.1 - Networks
What a network manager does How do all the wires connect together When I play games in school, how do they talk to each other Why is wireless slower What is a Proxy, VPN, Tunnel. In hacking films, what does the terminology mean Should I set up a home network
Most computer systems are now connected together in some way to form what is known as a network. This ranges from basic school/home networks of only a few computers (often set up to share resources such as printers r software) to large networks such as the internet, which effectively allows any computer connected to it to communicate with any other computer similarly connected.
This chapter considers the type of network that exist and many of the features that are available because of networking. You will learn that devices such as hubs and switches are needed to distribute data within a network; that local area networks (LAN’s) can be connected together using bridges; and that devices such as modems and routers are needed to connect these LAN’s or single computers to external networks, such as the internet.
Page 58

## Slide 9: 4.1.1 – Network Devices - Modem
Modem means ‘modulator demodulator’ and is a device that converts (i.e. modulates) a computer’s digital signal into an analogue signal for transmission over an existing telephone line. It also does the reverse process, in that it converts analogue signals from a telephone line into digital signals (demodulates), to enable the computer to process the data.
Modems are essentially used to allow computers to connect to networks (e.g. the internet) over long distances using the existing telephone networks.
Dial-up modems operate at transmission speeds of about 60 kilobits per second, which is extremely slow by today’s standard (60 kilobits = 60,000 bits, 1 bit refers to a binary digit and has the value of 1 or 0).
Page 58

## Slide 10: 4.1.1 – Network Devices - ADSL
Modern broadband or ADSL (asymmetric digital subscriber line) modems operate at up to 100Megabits per second (12.5 Mbytes / second)(*1 byte = 8 bits; 100 megabits = 100 million bits) when using fibre optic cables (although the old technology copper cables usually only offer a maximum of 20 Mbits/second), The term ‘asymmetric’ actually means that the modem is faster at downloading data (i.e. receiving data) than it is at uploading data (i.e. sending data).
Although ADSL modems still use the existing telephone network, unlike dial-up modems they do not tie up the line while accessing the internet – they can always be ‘on’, so internet access is available 24 hours if necessary, and the landline telephone can be used at the same time because of the wide bandwidth signal used (different frequencies are used to transmit internet signals so they don’t interfere with normal telephone traffic). Cable modems also exist, which allow cable television providers to offer internet access as well as receiving television signals.
Page 58

## Slide 11: 4.1.1 – Network Devices - Hubs
Hubs are hardware devices that can have a number of devices or computers connected to them. They are often used to connect together a number of devices to form a LAN – e.g. a star network.
Its main task is to take any data packet (this is a group of data being transmitted) received at one of its ports and broadcast to every computer in the network. This essentially means that using a hub is not a very secure of efficient method of data distribution.
Page 59

## Slide 12: 4.1.1 – Network Devices - Switch
Switches are similar to hubs but are much more efficient in the way that they distribute data packets. As with hubs, they connect a number of devices or computers together to form a LAN.
However, unlike a hub, the switch checks the data packet received and works out its destination address (or addresses) and sends the data to the appropriate computer(s) only, This makes using a switch a more secure way of distributing data.
Each device or computer on a network has a media access control (MAC) address that uniquely identifies it. Data packets sent to switches will have a MAC address identifying the source of the data and additional addresses identifying each device that should receive the data (see 4.1.2 for more on MAC addresses).
Page 59

## Slide 13: 4.1.1 – Network Devices - Bridge
Bridges are devices that connect one LAN to another LAN that uses the same protocol (communication rules). They are often used to connect together different parts of LAN so that they can function as a single LAN.
Bridges tend to be used to interconnected LAN’s (or parts of LAN’s) since sending out every data packet to all possible destinations would quickly flood larger networks with unnecessary traffic. For this reason a router is used to communicate with other networks, such as the internet.
Page 59
Server
HUB/SWITCH
HUB/SWITCH
BRIDGE
Computer
Computer
Computer
Computer
Computer
Computer

## Slide 14: 4.1.1 – Network Devices - Router
Routers enable data packets to be routed between the different networks, e.g. to join a LAN to a wide area network (WAN). A router would typically have an internet cable plugged into it and several cables connecting to computers and other devices on the LAN.
Figure above shows how routers work.
Page 60
Server
ROUTER
HUB/SWITCH
Computer
Computer
Computer
Internet
LAN

## Slide 15: 4.1.1 – Network Devices - Router
Broadband routers sit behind a firewall. The firewall protects the computers on a network. The router’s main function is to transmit internet and transmission protocols between two networks and also allow private networks to be connected together.
Routers inspect the data packets (see next slide) sent to it from any computer on any of the networks connected to it. Since every computer on the same network has the same part of an internet protocol (IP) address, the router is able to send the data packet to the appropriate switch and it will then be delivered using the MAC destination address (see 4.1.2). If the MAC address doesn’t match any device on the network, it passes on to another switch on the same network until the appropriate device is found.
Page 60

## Slide 16: 4.1.1 – Network Devices – Data Packets
The data is carried in the packet according to which protocol (set of rules) is used. Packets of data usually contain the following information:
Some form of header to identify the data packets
The sender’s IP address
The receiver’s IP address
How many data packets make up the whole ‘message’
The identity number of each packet
This information allows the router to route a packet across the network to its correct destination and allows the data packets to be reassembled in their correct order according to identity number at the receiving station.
When a router receives a packet of data, it checks the IP address against the stored routing table. The routing table stores the MAC address of the device, the assigned IP address and the lease time the assigned IP address is assigned for. The bits forming the destination IP address in the data packet are used to point to the correct route. The packet is sent to a number of routers until it reaches its final destination.
Page 61

## Slide 17: 4.1.1 – Network Devices – Other Hardware
Gateway
A Gateway is a network point (or Node) that acts as an entrance to another network. It is a key point for data on its way to and from other networks. All networks will have boundaries so that all communication within the network is conducted using devices such as switches or routers, If a network node needs to communicate outside its network, it needs to use a gateway.
Network Interface Card
A Network Interface Card (NIC) is needed to allow a device to connect to a network (e.g. the internet). It is usually part of the device hardware and frequently contains the MAC address generated at the manufacturing stage.
Network Cables
Even though many computer systems use Wi-Fi, network cables are still used because they have the following advantages over Wi-Fi.
Faster data transfer rates
Can be more secure that wireless networks
The cables can be either copper or fibre optics – the latter offers higher data transfer rates and also better security (see notes on quantum cryptography).
Page 61

## Slide 18: 4.1.2 – Differences Between IP and MAC Addresses
A MAC address is a unique number that identifies a device connected to the Internet. SO what is the difference between an IP address and a MAC address? The IP address gives the location of a device on the internet, whereas the MAC address identifies the device connected to the Internet
You can think of the IP as the address if the house you live in (it will have some unique ways of identifying it, such as a post or zone code). Using this example, the MAC address can be thought of as a way if uniquely identifying each person living in that house. It is possible to move house (so your IP address will change) but the same people will be living in the new house (so their MAC address will remain unchanged).
Page 61

## Slide 19: 4.1.3 – Wi-Fi and Bluetooth
Both Wi-Fi and Bluetooth offer wireless communication between devices. They both use radio frequencies as the carrier of data transmission.
How Computers use Wi-Fi and Bluetooth to connect to Networks
Wi-Fi
A wireless transmitter (WAP) receives information from a network via its connection (e.g. a broadband connection if the internet is used). This transmitter converts the received information into radio waves and then transmits them.
A device (e.g. a computer) receives the radio waves via an installed wireless adaptor which allows it to download the information from the data source. This, of course, works in reverse when the device wishes to transmit data over the network.
Wi-Fi is best suited to operating full-scale networks since it offers much faster data transfer rates, better range and better security than Bluetooth. A Wi-Fi-enabled device (such as a computer or smartphone) can access, for example, the internet wirelessly at any access point (AP) of hot spot up to 100M away.
Page 62
Or Click here

## Slide 20: 4.1.3 – Wi-Fi and Bluetooth
Bluetooth
Bluetooth sends and receives radio waves in a band of 79 different frequencies (known as channels). These are all centered on a 2.45GHz frequency.
Devices using Bluetooth automatically detect and connect to each other, but they don’t interfere with other devices since each communicating pair uses a different channel (from the 79 options)
When a device wants to communicate, it picks one of the 79 channels at random. If the channel is already being used, it randomly picks another channel. This is known as spread-spectrum frequency hopping.
To further minimise the risk of interference with other devices, the communication pairs constantly change the frequencies (channels) they are using (several times a second).
Page 62
Or Click here

## Slide 21: 4.1.3 – Wi-Fi and Bluetooth
Essentially, Bluetooth is useful:
When transferring data between two or more devices that are very close together (<30m distance)
When the speed of data transmission is not critical
For low bandwidth applications (e.g. when sending music files from a mobile-phone to a headset)
Bluetooth creates a secure wireless personal area network (WPAN) based on key encryption.
Table below summarises some of the differences between Wi-Fi and Bluetooth.
Page 62
Feature | Bluetooth | Wi-Fi
Transmission frequency used | 2.4GHz | 2.4, 3.6, 5.0GHz
Data transfer rate (maximum) | 25 Mbits/second (-3.1 Mbytes/second) | 250 Mbits/second (-31 Mbytes/Second)
Maximum effective range (metres) | 30M | 100m (but can be obstructed by walls etc. reducing effective range to only a few metres)
Maximum number of devices connected | Up to 7 | Depends on the router used (can be one or many devices)
Type of data transmission security | Key matching encryption | WEP (wireless equivalent privacy) and WPA (Wi-Fi protected access) are the most common security systems.

## Slide 22: 4.1.4 – How to set up and configure a small network.
Suppose you were asked to set up and configure a small network of 10 computers. You would need to consider the following points in the next slide:
Apart from all the hardware and software, you would also have to think about doing the following:
Setting an IP account if internet access is required
Setting up the system (or buying appropriate hardware correctly configured) to allow for wireless connectivity
Configuring all the hardware and software so that they work correctly together
If internet is required, ensuring that a high-speed broadband connection exists
Putting all the common software onto a server and also making sure that a network license has been acquired so that all network users can make use of the software
Setting up privileges so that each user can only access their own area or common shared area
Setting up a network-manager-level of privilege so that they can monitor network usage, change passwords etc.
Page 62

## Slide 23: 4.1.4 – How to set up and configure a small network.
Page 63
Purchase of software and hardware
Network cables to connect devices together
If a connection to the internet is needed, then a router is required to do this
A firewall (either hardware or software) is needed to help protect the network against hacking
Servers to manage network security, store common software and files, etc.
Switches, hubs and other devices needed to link everything together on the network
Exercise 4A – Find out any other hardware or tasks that need to be carried out when setting up a small network. Ask questions such as ‘would Wi-Fi or Bluetooth be the best type of connectivity?’. ‘Should PC’s or Laptops be used?’ etc.
Notes: Suppose you were asked to set up and configure a small network of 10 computers. You would need to consider the following points:
Apart from all the hardware and software, you would also have to think about

## Slide 24: 4.1.5 – Internet, Intranet, Extranets, LAN’s and WAN’s
The main features of the internet, intranets and extranets, and the difference between them, are covered in Chapter 10.
4.1.6 – Local Area Networks (LAN’s) and Wide Area Networks (WAN’s)
Local Area Networks (LAN’s)
These systems are usually within one building, or certainly not very far from each other geographically. A typical LAN will consist of a number of computers and devices (e.g. printers) that are connected to hubs or switches. One of the hubs or switches will usually be connected to a router and a modem (usually broadband) to allow the LAN to connect to the internet; in doing so it then becomes part of a WAN.
Page 64

## Slide 25: 4.1.6 – Internet, Intranet, Extranets, LAN’s and WAN’s
Advantages
The sharing of resources (such as expensive peripherals and applications software)
Ease of communication between users.
A network administrator to control and monitor all aspects of the network (e.g. changing passwords, monitoring internet use etc.)
Disadvantages
Easier spread of viruses throughout the whole network.
Printer queues developing, which can be frustrating.
Slower access to external network, such as the internet.
Increased security when compared to stand-alone computers.
If the main server breaks down, in most cases the network will no longer function.
Page 64

## Slide 26: 4.1.6 – Wide Area Networks
Wide Are Networks (WAN’s) are used where computers or networks are situated a long distance from each other geographically (e.g. in a different city or country). If a number of LAN’s are joined together using a router or modem, then they can form a WAN. The most common examples of WAN include the Internet and the network of ATM;s (automated teller machines) used by banks.
Because of the long distances between devices, WAN’s usually make use of some public communications networks (such as telephone lines or satellites) but they can use dedicated or leased communication lines which can be less expensive and also ,more secure (less risk of hacking).
A typical WAN will consist of end systems and intermediate systems (see right).
1, 3, 7 and 10 and known as end systems and the remainder are known as intermediate systems. The distance between each system can be considerable, especially if the WAN is run by a multinational company.
Page 64
1
2
3
4
5
6
7
8
9
10

## Slide 27: 4.1.6 – Wide Area Networks
Wireless LAN’s (WLAN’s) are similar to LAN’s but there are no wires or cables. In other words, they provide wireless network communications over fairly short distances (a few metres) using radio or infrared signals instead of cables.
Devices, known as access points (AP’s) or wireless nodes are connected into the wired network at fixed locations. Because of the limited range, most commercial LAN’s (e.g. at a college campus or at an airport) need several AP’s to permit uninterrupted wireless communications. The AP’s use either spread spectrum technology (which is a wideband radio frequency with a range of about 30-50m) or infrared (which has a very short range, about 1-2m, and is easily blocked; it therefor has a limited use).
The AP receives and transmits the data between the WLAN and the wired network structure. End-users access the WLAN through wireless LAN adapters that are built into the devices or are a plug-in module.
Page 64

## Slide 28: 4.1.6 – Wide Area Networks
Advantages
All computers can access the same servers and resources (such as printers, scanners, internet access) from anywhere within the range of the AP’s.
As there is no cabling there is a safety improvement and increased flexibility (since the user no longer has to remain at their desk).
Adding new computers and devices is very easy (all that is required is a WLAN adapter) and the costs are reduced since extra cabling isn’t needed.
Disadvantages
Security can be a big issue since anyone with a WLAN-enabled laptop can access a network if it can pick up a signal; it is therefor necessary to adopt complex data encryption techniques.
There may be a problem with interference, which can affect the signal.
The data transfer rate is slower than in a wired LAN.
Page 64
Click Here

## Slide 29: 4.1.7 – Accessing the Internet
Mobile Phone and Tablets
The same comments also refer to tablets ( and phablets) but, as they usually have bigger screens and keyboards, they have an advantage in that respect when compared to mobile phones. The other advantages and disadvantages are similar to mobile phones - it all depends on the screen size of the tablet being used.
Page 65
The displays on mobile phones are smaller than on other devices - this makes it more difficult to read web pages
Keyboards are very small – it is therefor more difficult to type in messages or navigate web pages
Not all websites are mobile-friendly, therefore not all websites may be accessible
Signal less likely to be as stable or reliable as a wired system (used by PC’s and Laptops)
Expensive to use if Wi-Fi hot spot not available.
Very portable; can be used almost anywhere provided a mobile phone network signal can be accessed.
A person is more likely to have a mobile phone with them at all times
It is easier to use a mobile phone while on the move than other devices.
Figure 4.6 Advantages and disadvantages of connecting to the internet with a mobile phone

## Slide 30: 4.1.7 – Accessing the Internet
Laptops
Page 66
Although the screen size is usually bigger than a mobile (and some tablets) it is not usually as large as that on a desktop computer
Laptops require expensive 'dongles' to access phone networks
Processors used in, laptops are not usually as powerful as those in desktops, so access speed is not as quick
Laptops are more mobile than desktops but heavier and less portable than tablets or mobile phones
Touchpads on laptops are not as easy to use as a mouse when - navigating web pages but much easier than mobile phones
The keyboards on laptops are not as easy to use as a desktop but are much better than those on a mobile phone
Figure 4.7 Advantages and disadvantages of connecting to the internet with a laptop

## Slide 31: 4.1.7 – Accessing the Internet
Desktop Computer
Page 66
Because the parts are all separate and because of the large size, desktop computers are not very portable
Desktops require expensive 'dongles' to access the
phone network
Use of full-sized keyboard and pointing devices, such as a mouse, make web page navigation much easier
Tend to have more powerful with faster processors than other devices
Usually have a more stable and reliable internet connection since they use a wired system rather than
Wi-Fi
All web pages are
accessible due to larger screen size than other devices
Figure 4.8 Advantages and disadvantages of connecting to the internet with a desktop computer
Exercise 4b
Refer to the notes in Chapter 1 and write an article on the relative advantages and disadvantages of using various devices to access the internet and to download information from the internet, using these various devices, to allow you to produce a presentation on a topic of your own choice. Include a conclusion to indicate which device(s) you would choose.

## Slide 32: 4.2 – Network Issues and Communication
4.2.1 – Network Security
Many aspects of security (such as hacking, phishing, pharming and viruses) are covered in depth in Chapter 8. This section covers some of the more general aspects of internet security.
When accessing the internet, users have to be very careful of many issues – not all of them obvious. Let us first consider the material found on the internet.
Should the internet be policed?
This question has raged for many years. The internet doesn't presently have any controlling body that ensures that it conforms to certain standards. There are many arguments in favour of having control, and as many arguments against it.
Arguments in favour of some form of control:
it would help to prevent illegal material being posted on websites (for example, racist/prejudiced and pornographic material, terrorist activities, and so on)
people find it much easier to discover information that can have serious consequences (for example, how to be a hacker, how to make bombs, and so on); although most of this information can be found in books, it is much easier to find it using a search engine
it would help to prevent children and other vulnerable groups from being subjected to undesirable websites
it would help to stop incorrect information being published on websites.
Page 64

## Slide 33: 4.2 – Network Issues and Communication
4.2.1 – Inappropriate sites and the accuracy of information
The social and general impacts of using the internet or devices that rely on microprocessors have been discussed in earlier sections. It is now worth spending some time looking at the quality of information found on the internet when using a search engine. There are three main aspects to consider:
reliability of information
undesirability of certain websites
security issues.
Reliability of information
Information on the internet is more likely to be up to date than in books (websites can be updated very quickly).
It is much easier to get information from websites (search engines quickly link key words together and find information that matches the criteria).
There is a vast amount of information on the internet that is easier to locate than using the indices in several books.
Information could also be incorrect, inaccurate or even biased, since it doesn't go through any checking process.
There is a real risk of information overload, even if the search engines are used properly; it is possible to get millions of hits, which may make it difficult to find the relevant information.
Page 67

## Slide 34: 4.2 – Network Issues and Communication
Undesirability of certain websites
There is always a risk of finding undesirable websites.
There is also a risk of connecting to websites that are not genuine, which could lead to a number of problems (such as undesirable web links, security risks, and so on).
Security risks ( these are a real problem - this topic is covered in Chapter 10 and elsewhere throughout the book).
Page 67
Exercise 4c
Using the information above and information from Chapter 10 (and elsewhere), write an article on the pros and cons of using the internet (rather than other methods, such as consulting books) to search for information when doing some research for a science or geography project.
Remember to draw a conclusion when you have finished giving your advantages and disadvantages.

## Slide 35: 4.2 – Network Issues and Communication
Security Issues
Passwords are used in many instances when accessing the internet, for example when:
accessing your email account
carrying out online banking
accessing social networking sites.
There are many more instances when you might need to type in a password and, in many cases, a user ID. It is important that passwords are protected; some ways of doing this are described below:
run anti-spyware software to make sure that your passwords aren't being relayed back to whoever put the spyware on your computer
change passwords on a regular basis in case they have come into the possession of another user illegally or accidentally.
Page 68

## Slide 36: 4.2 – Network Issues and Communication
passwords should not be easy to guess or break (for example, don't use your favourite colour, name of a pet or favourite rock group); passwords are defined as either 'strong' (hard to break or guess) or 'weak' (relatively easy to break or guess). Strong passwords should contain:
  at least one capital letter
  at least one numerical value
  at least one other keyboard character (such as@, *, &).
  An example of a strong password would be: Syl2@#TT90kj=0.
  An example of a weak password would be: GREEN.
Page 68
Exercise 4d
Which of the following are weak passwords and which are strong passwords?
Explain your decision in each case.
25-May-2000
Password
ChapTer@15
AbC*N55!
12345X

## Slide 37: 4.2.2 – Authentication
Authentication is used to verify that data comes from a secure and trusted source. It works with encryption to strengthen internet security, for example.
User IDs and passwords are authentication techniques. Some forms of authentication include:
digital certificates (see Section 8.4.4 for more details)
biometrics (see Section 8.4.4 for more details)
magnetic stripe cards/id cards/passports.
Magnetic stripe cards were covered in Chapter 2. These cards have a magnetic stripe on one side ( made up of tiny magnetic particles on a plastic film). Each particle can act as a north-pole or a south-pole (which corresponds to the two binary values of 0 and 1).
The stripe is read by swiping it through a card reader (see Chapter 2). Data such as name, ID number, sex and date of birth may be contained on a magnetic stripe when used as a security device to allow entry to a building, for example.
Page 68

## Slide 38: 4.2.2 – Authentication
Contactless cards can be read from a distance and don't have to be swiped through a card reader. This technology was discussed in Chapter 2. Contactless technology can be used in credit/ debit cards, for example, to speed up payments in a shop, but they can also be used as a security device. If the card is in a wallet or a pocket, as the owner of the card walks through a security gate, readers either side of the gate quickly scan the security data stored on the tag/chip embedded in the card. Access will only be allowed if the scanned data matches data in a database.
Some ID cards also use a holographic image (hologram). These are designed to make forgery of the card more difficult. Holographic images change colour or appear to have a moving object when the image is viewed from different angles. As these are difficult to make it stops somebody, for example, simply photocopying a card and using it illegally.
Another form of security is to have a photographic image of the card user printed on the card surface.
Passports make use of some of the technology described above. Many passports contain an RFID tag/chip, a photograph and a holographic image.
Page 69

## Slide 39: 4.2.2 – Authentication
Page 69
The passport page containing the photograph is placed face down on a reader
The owner of the passport now looks up at a digital camera and a photograph is taken
The photograph is converted into a digital format so that it can be compared to the scanned facial image
A microchip embedded in the page is now read by the reader and the facial image on the passport is also scanned in
The data read from the microchip is also compared to data stored on a central database
Data stored on the microchip varies from country to country but sometimes includes biometric data, country of origin, date of birth, countries visited and so on.
The scanned image from the passport and photograph just taken by the camera must match and the data stored on the microchip must also match with the data on a central database. If either produces any differences then the passport is rejected.
Figure 4.9 What happens when somebody approaches passport control at an airport?

## Slide 40: 4.2.3 – Viruses
This section considers how the risk of viruses can be minimised when using the internet or any situation where data is transferred from computer to computer or other electronic devices - it is important to point out that tablets and mobile phones can also be infected by viruses. Any electronic device with a storage capability can be affected by virus attacks.
Ways of preventing or minimising the risk of viruses are outlined below.
Antivirus software
Running antivirus software in the background on a computer will constantly check for virus attacks. Although various types of antivirus software work in different ways, they all have the following common features:
they check software or files before tl1ey are run or loaded on a computer
anti virus software compares a possible virus against a database of known viruses
they carry out heuristic checking - this is tl1e checking of software for types of behaviour that could indicate a possible virus; this is useful if software is infected by a virus not yet on the database
Page 69

## Slide 41: 4.2.3 – Viruses
any possible files or programs that are infected are put into quarantine that:
  allows the virus to be automatically deleted, or
  allows the user to make the decision about deletion (it is possible that the user knows that the file or program is not infected by a virus - this is known as a false positive and is one of the disadvantages of antivirus software)
antivirus software needs to be kept up to date since new viruses are constantly being discovered
full system checks need to be carried out once a week, for example, since some viruses lie dormant and would only be picked up by this full system scan.
Page 70

## Slide 42: 4.2.3 – Viruses
Avoiding viruses when accessing the internet
One way to help prevent virus attacks when accessing websites on the internet is to avoid unknown or suspicious-looking websites. If in doubt, don't access the website - look for security indicators such as https or the padlock symbol.
Also look out for odd behaviour in the URL. When accessing a new website, for example from an advert in an email, copy and paste the URL into the address bar at the top of the page rather than just clicking on the link in the email. This can help to avoid links to bogus/fake websites.
It is also not advisable to open emails ( or any attachments) from unknown sources. Essentially, the best form of defence against malicious behaviour when making use of the internet is to apply common sense.
Page 70

## Slide 43: 4.2.3 – Viruses
Viruses from hardware devices
It is possible to pick up viruses from any device plugged into your computer.
Apart from the obvious precaution of scanning the device for viruses, it is still unsafe to plug in a device from an unknown source. Even memory sticks or DVDs from friends or from school could still be infected unless they have also carried out all the necessary precautions.
Task: Research the effect of any virus (other than Lovesan or ILoveYou), and describe the following:
How it appeared
The damage caused
What kind of virus it was (Trojan, worm, hardware or software)
The method of delivery
Page 70

## Slide 44: 4.2.4 – Data Protection Acts
Most countries have some form of data protection act (DPA). These are designed to protect individuals and to prevent incorrect or inaccurate data being stored.
Essentially DPAs are set up to protect the rights of the individual about whom data is obtained, stored and processed (i.e., collection, use, disclosure, destruction and holding of data). Any such act applies to both computerised and paper records.
Many data protection acts are based on eight principles, as outlined in Figure 4.10.
In many countries, failure to abide by these simple rules can lead to a heavy fine or even imprisonment to anyone who holds data about individuals.
Page 71

## Slide 45: 4.2.4 – Data Protection Acts
There are general guidelines about how to stop data being obtained unlawfully:
don't leave personal information lying around on a desk when not attended
lock filing cabinets at the end of the day or when the room is unoccupied
do not leave data on a computer monitor if it is unattended; log off from the computer if away from your desk for any length of time
use passwords and user ids, which should be kept secure; passwords should be difficult to guess/break and should be changed frequently
make sure that anything sent in an email or fax (including attachments) is not of a sensitive nature.
Page 71

## Slide 46: 4.2.5 – Network Communication
Faxes and emails
There are two basic ways of sending a fax (abbreviation for facsimile - a copy):
a physical fax (a dedicated machine connected to a telephone line; it requires the number of the recipient to be dialled before the document is copied and then sent electronically)
electronic faxing (this requires a network, such as the internet, for the fax to be sent).
Physical fax machines
Fax machines have been used for many years to send and receive paper documents.
A standard fax machine allows documents to be sent to another fax machine using a normal telephone line. The user places me document in the fax machine tray, lifts me receiver and dials the fax number of the recipient and then presses <send>.
At the receiving end, the document is printed on another fax machine. It can be quite a slow way to send a document if the fax line is busy or if there are several pages to send.
Page 71

## Slide 47: 4.2.5 – Network Communication
Figure 4.11 Sending an electronic fax
However, a more modern way is electronic faxing (or online faxing) which makes use of computer technology and the internet. Electronic faxing has the following advantages over the more traditional method described above:
costs are reduced as there is no need to buy a fax machine, ink/toner or paper
transfers using electronic methods are encrypted, improving security
transmissions are sent to an email account, which is password protected
there is no issue of a 'busy signal' preventing the fax being sent.
At this point you may be wondering what is the difference between an electronic fax and an email?
Page 72

## Slide 48: 4.2.5 – Network Communication
The simple answer is not a lot. The only real difference is that online faxing is always associated with an email address and a fax number. The fax number is similar to the traditional fax number and needs to be known by the sender. Having this number allows a user to send fax messages to the recipient.
Once a fax is received, the on-line fax service provider sends an email with the fax message attached in a tiff or pdf format. The sender of the fax can either use an email account or log into any online account to send
It is important to realise that it is possible to send a fax from your computer to another device connected to the internet or to a traditional fax machine, where the document will be printed out in the normal way.
Page 72
Figure 4.11 Sending an electronic fax

## Slide 49: 4.2.5 – Network Communication
Emails
Electronic mail (email) is discussed in many parts of this book. Emails are particularly useful when sending attachments (for example, documents, videos, music, and so on). Emails can be sent to, or sent from, any device connected to the internet.
When sending attachments it is usually important to have a good, stable internet connection - particularly when sending or receiving large files. The basic difference between emails and electronic faxes was described above; all the advantages and disadvantages of emails apply to electronic faxing when it is sent from computer to computer.
Emails require an account with an ISP. When sending an email, it is necessary to include the email address (which must be exact), a subject line and any attachments if required.
The recipient simply has to log on to their account and read the emails in their inbox.
It is now worth comparing emails with traditional, physical faxes ( as indicated above, there are few differences between electronic faxes and emails so they won't be part of this comparison).
Page 72

## Slide 50: 4.2.5 – Network Communication
Page 72

## Slide 51: 4.2.5 – Network Communication
Page 73
Traditional Faxes | Emails
They are more likely to be intercepted since the document needs to be printed out and the fax machine is potentially accessible to many people in the office. Signatures on faxes are accepted legally The quality of the documents printed out can be quite poor at times If the telephone lime is busy (or shared), there can be a considerable delay in sending the fax. It can be a slow process if several documents are to be sent since each document needs to be scanned before it is transmitted | More secure than faxes (password protected and usually sent to an individual's computer) No need to print the document (cost saving and more environmentally friendly) The document is usually of a much better quality Unlike paper-based faxes, documents received in emails can be modified or easily copied and pasted into other documents. Documents and files can be sent and received from any device that has internet connectivity. It is much easier to send to multiple recipients at the same time - with a fax you have to dial up the fax number of each recipient before sending People are more likely to have access to email accounts than a fax machine.
Exercise 4e - Carry out an assignment to compare emails, faxes and traditional post as a way to send documents and items to people.

## Slide 52: 4.2.5 – Network Communication
Video Conferencing
Video conferencing is a communication method that uses both video and sound. It is a substitute for face-to-face conferences between a number of people, who may be in a different part of the country or live overseas. It is carried out in real time and makes use of some form of network. The basic hardware includes:
webcams
large monitors/television screens
microphones
speakers.
There are a few items to consider when a conference is about to begin:
it is essential to agree a time and date for the conference to take place
the delegates in each conference room must log in to the video conference system
webcams need to be placed in the correct position so that all the delegates in the room are within visual contact (the webcams will capture the images and then transmit them to the other delegates - they will see the images on their own large screens)
Page 73

## Slide 53: 4.2.5 – Network Communication
the video conference set-up needs to be checked before the meeting goes live
microphones need to be placed centrally so that all of the delegates can speak - the sound is picked up by the microphones and transmitted to the other delegates (they hear the voices through speakers in their own conference room)
it is important for one person to be the main contact in each conference room to make sure that each delegate is able to be heard; this is particularly important if more than two video conference rooms are linked up at the same time.
In addition to the hardware items described above, it is important to realise that software plays an important role in a successful video conference.
Page 73

## Slide 54: 4.2.5 – Network Communication
Page 73
Software | Description
Webcam and microphone drivers | It is vital that the correct software is used to ensure that the webcam and microphone transmitter images and sound to the other delegates (these are sometimes referred to as hardware drivers)
CODEC | CODEC can stand for coder-decoder or compression-decompression. The first is used to encode or decode the digital data stream to allow data to be transmitted (encoded) and played back (decoded). The second is used to compress the data before it is transmitted and then decompress it again at the receiving conference room.
Echo cancellation software | Echo cancellation software allows talking to take place in real time and permits the synchronisation of communication. Microphones can pick up sound from the speakers (i.e. creating an echo); this software copies received signals and checks for parts of the signal that reappear but are delayed slightly. The reappearing parts are removed from the signal (i.e. the echo is removed)
In addition to the hardware items described above, it is important to realise that software plays an important role in a successful video conference.
Table 4.3 Software used in video conferencing

## Slide 55: 4.2.5 – Network Communication
Page 74
Potential issues with video conferencing
Potential time lag in responses/delays when talking.
Jerking images - usually due to poor internet/network performance or a poor bandwidth.
Can be very expensive to set up in the first place (both the hardware and the software are expensive to purchase and set up correctly).
There can be problems if the delegates live in different countries where the time zone differences are large.
Training people to use the system correctly can be both costly and time consuming.
It can be demotivating for staff if they believe that one of the 'perks' of their job is international travel.
The whole system relies on a good network connection - if it breaks down or the signal strength is diminished in any way, then the video conference can be almost unusable.

## Slide 56: 4.2.5 – Network Communication
Page 74
Advantages
As people are in their own building, it is much easier to access important documents or bring in 'experts' at key parts of tl1e conference - this would be difficult if they were a long way away from their office.
It is possible to hold conferences at short notice (a conference date can be set up within a few hours as no person needs to travel fur ).
Not travelling physically to meetings reduces costs:
  reduced travelling costs
  no need to pay for hotel accommodation or venue hire
  it also reduces the cost of taking people away from their work for two or three days to travel - people are still paid their wage even though they are not in the office, so this is a large 'hidden' cost.
It may be better to use video conferencing than have delegates travel to potentially unsafe places around the world.

## Slide 57: 4.2.5 – Network Communication
Page 75
Audio conferencing
This refers to meetings held between people using audio (sound) equipment. The equipment used can be the telephone, a computer (with microphones and speakers) or an internet phone.
Audio conferencing can be done over the telephone network (often referred to as a phone conference). The procedure to be carried out when doing a phone conference is detailed below.
The organiser of the phone conference is given two PINs by the phone company. One PIN is the personal PIN (e.g. 2151) given to the organiser and the second PIN is the participants' PIN (e.g. 8422).
The organiser contacts all of the participants and informs them of their PIN and the data and time of the phone conference.

## Slide 58: 4.2.5 – Network Communication
Page 75
When the phone conference is about to start, the organiser dials the conference phone number and, once he/she is connected, keys in his/her personal PIN (2151 in this case).
The participants then call the same conference number to join in - once they get through they each input the PIN given to them by the organiser (8422 in this case). Without this PIN, it will be impossible to join the phone conference.
It is possible to hold an audio conference using a computer provided a microphone and speakers are connected. This makes use of Voice over Internet Protocol (VoIP). It is also possible to hook up an internet telephone, which usually plugs into the router or other internet device.

## Slide 59: 4.2.5 – Network Communication
Page 75
Using VoIP allows an organiser to create a group of people to take part in the conference call. The group is created by dragging and dropping user names and telephone numbers into the group. When the conference is to take place, the organiser clicks on the required group and the conference is initiated. Using VoIP allows communication using voice, instant messaging and video (by using an attached webcam).
If some of the users don't have an internet connection or don't have access to a computer, it is possible to add actual telephone numbers (landline or mobile) to the group. The only real drawback is the quality of the sound when using this technique since it is totally reliant on a fast, stable broadband connection - otherwise 'drop out' (loss of voice on occasions), echoing (when the user can hear their own voice being echoed back as they speak) or a very noisy line making it difficult to understand.

## Slide 60: 4.2.5 – Network Communication
Page 76
Web Conferencing
Often referred to as a webinar, uses the internet to permit conferencing to take place. Multiple computers are used with this system, all connected over the internet. As with video conferencing, it is carried out in real time and allows the following types of meeting to take place:
business meetings to discuss new ideas
presentations
online education or training.
The only requirement is a computer and a high-speed, stable internet connection.
To carry out web conferencing, each user either downloads an application or logs on to a website from a link supplied in an email from the conference organiser.
Delegates can leave or join the conference as they wish. The organiser can decide on who can speak at any time using the control panel on their computer.

## Slide 61: 4.2.5 – Network Communication
Page 76
If a delegate wishes to speak, they raise a flag next to their name. Delegates can post comments using instant messaging for all delegates to see at any time. Some of the main features include:
slide presentations using presentation software that can be posted on the conference website in advance of the meeting
it is possible for any delegate to draw or write on a 'whiteboard' using their own keyboard or mouse
it is possible to transmit images or videos using the webcam throughout the conference
documents can be shared by uploading them to the website before the conference begins
as described earlier, it is possible to chat verbally or by using instant messaging throughout the conference.
As indicated earlier, web conferencing clearly links into video conferencing and audio conferencing through the use of webcams and built-in microphone and speakers. Essentially it is possible to have a conference using any device that allows these functions (for example, tablets and smartphones would both permit this type of group communication).

## Slide 62: Exam Questions: November 2009
(a) Name two network devices that could be used to connect a LAN to a WAN. 1 ________________________________________________________________ 2 _____________________________________________________________ [2] (b) Describe the differences between a WAN and a LAN ______________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________ [5]
?

## Slide 63: Exam Questions: November 2009
13 (a) | Two from: Modem Router Or any other suitable answer | [2]
(b) | Five from: WAN is a wide area network WAN covers a large geographical area/worldwide The Internet is a WAN LAN is a Local Area Network LAN covers a small area such as one building/A school network is a LAN A WAN consists of connected LANs More difficult to share peripherals using a WAN | [5]

## Slide 64: Exam Questions: November 2009
Tick three essential components of a computer to be used in a video conferencing system. [3]
 | 
Graph Plotter | 
Trackerball | 
Microphone | 
Speakers | 
Optical mark reader | 
Web Cam | 

## Slide 65: Exam Questions: November 2009
Tick three essential components of a computer to be used in a video conferencing system. [3]
 | 
Graph Plotter | 
Trackerball | 
Microphone | 
Speakers | 
Optical mark reader | 
Web Cam | 

## Slide 66: Exam Questions: November 2009
Multi-national companies often use video conferencing instead of face-to-face meetings. (a) Tick three advantages of video conferencing.[3]
 | 
Companies don’t have to employ so many workers. | 
Companies can call meetings at short notice. | 
Employees don’t have to prepare for meetings. | 
Companies do not have to pay travelling expenses. | 
Employees can work from home. | 
Companies don’t have to have any offices. | 

## Slide 67: Exam Questions: November 2009
(b) Tick three disadvantages of video conferencing. [3]
 | 
It is difficult to call international meetings because of time differences. | 
It is difficult to call international meetings because of time differences. | 
The initial cost of hardware can be expensive. | 
There is a loss of personal and social contact. | 
Companies are unable to contact the employees about having a conference. | 
Companies have to hire expensive halls. |